## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Evaluation of IEEE 802.15.6ma Ultra-wideband Physical Layer Utilizing Super Orthogonal Convolutional Code]
Date Submitted: [12 July 2023]
Source: [Kento Takabayashi1, Ryuji Kohno2,3 ] [1;Toyo University, 2;Yokohama National University, 3;YRP International Alliance Institute(YRP-IAI)]
Address [1: 2100 Kujirai, Kawagoe, Saitama, Japan 351-8585, Japan 719-1197,
2; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, Japan 240-8501,
3; YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan]
Voice:[1; +81-866-94-2104, 2: +81-90-5408-0611],
Email:[1: takabayashi.kento.xp@gmail.com, 2:kohno@ynu.ac.jp]
Re: []
Abstract: [The performance of an IEEE 802.15.6ma ultra-wideband physical layer utilizing super orthogonal convolutional codes is evaluated. These slides may offer opportunity to discuss on revision for a dependable physical layer technology of a new standard IEEE802.15.6ma.] Purpose: [The discussion will lead definition and requirement of current ongoing research and development on dependable wireless networks.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: doc.: IEEE 802.15-09-0117-00-0007
<month year>

## Slide 2
Evaluation of IEEE 802.15.6ma Ultra-wideband Physical Layer Utilizing Super Orthogonal Convolutional Code
July 2023,
Hybrid Session ,
Estrel Hotel, Berlin, Germany
Kento Takabayashi1, Ryuji Kohno2,3
1. Toyo University, Japan
2. Yokohama National University, Japan
3. YRP International Alliance Institute, Japan

## Slide 3: 1. Motivation and Aim of study
UWB is a promising technology that may satisfy the requirements of IoMT
IEEE 802.15.6 UWB PHY has limited transmission output and requires to ensure dependability
New consideration is given to the application of Super Orthogonal Convolutional Codes (SOCC) as a technique for improving dependability for higher priority case
We perform evaluation when SOCC is applied at the IEEE 802.15.6 UWB PHY, and confirm the effectiveness of these combinations
Notes: SOCCs have attracted attention as error correction codes for code division multiple access (CDMA) using the spread spectrum
Therefore, SOCCs are considered to be compatible with the UWB, as they use a very wide bandwidth

## Slide 4: 3. SOCC
Fig. SOCC encoder
SOCC is a kind of orthogonal convolutional code of very low coding rate
The encoder is composed of K length shift registers (constraint length) and a block orthogonal (Hadamard) encoder
The coding rate is given by
The decoder uses the Viterbi algorithm
Notes: The inner (K- 2) bit memories are mapped into one Walsh sequence of length (two to the power of K-2)
The two outer bits are added to each binary number of the selected Walsh sequence by exclusive OR
One divided by two to the power of K-2
The inner (K- 2) bit memories are mapped into one Walsh sequence of length 2^(𝐾−2) (two to the power of K-2)
The two outer bits are added to each binary number of the selected Walsh sequence by exclusive OR
One divided by two to the power of K-2

## Slide 5: 3. Application of SOCCs to IEEE 802.15.6 UWB PHY
Procedure for applying an SOCC
For the PHR, after the CRC encoding of the PHR frame, whether to apply the shortened BCH code is determined, and then, whether to apply an SOCC is determined
Similarly, for the PSDU, after the CRC encoding of the MAC header and MAC frame body, whether to apply the BCH code is determined, and then, whether to apply an SOCC is determined
Concatenated encoding using the BCH code as the outer code and an SOCC as the inner code is performed when both the BCH code and SOCC are applied
Fig. Block diagrams showing the procedure for applying an SOCC to the IEEE 802.15.6 UWB PHY

## Slide 6: 4. Evaluation
Channel model | AWGN, IEEE model CM3
Pass loss model | IEEE model CM3
Bandwidth () | 499.2 MHz
Center Frequency | 3993.6 MHz
Modulation | DBPSK
Transmission power () | 0 dBm
Thermal noise density () | -174 dBm/Hz
Implementation losses () | 3 dB
Receiver noise figure () | 5 dB
FEC (PHR) | (40, 28) Shortened BCH code, (11, 5) Shortened Reed-Solomon (RS) code, SOCC (K=3~7)
FEC (PSDU) | (63, 51) BCH code, (31, 25) Reed-Solomon (RS) code, SOCC (K=3~7)
Communication distance () | 0.5 m
Pulse waveform duration () | 2.003 ns
Information bit length () | 540 bits
Pulse option | Single pulse option, burst pulse option
Channel model | AWGN, IEEE model CM3
Pass loss model | IEEE model CM3
 | 499.2 MHz
Center Frequency | 3993.6 MHz
Modulation | DBPSK
 | -174 dBm/Hz
 | 3 dB
 | 5 dB
FEC (PHR) | (40, 28) Shortened BCH code, (11, 5) Shortened Reed-Solomon (RS) code, SOCC (K=3~7)
FEC (PSDU) | (63, 51) BCH code, (31, 25) Reed-Solomon (RS) code, SOCC (K=3~7)
 | 0.5 m
 | 2.003 ns
 | 540 bits
Pulse option | Single pulse option, burst pulse option
4. Evaluation
Table. Simulation Parameters
Notes: For comparison, the computer simulation also evaluates the case where the (11, 5) shortened Reed–Solomon (RS) code and the (31, 25) RS code are applied to the PHR and PSDU, respectively, as error correction codes with coding rates almost equal to those of the BCH codes used in IEEE 802.15.6

## Slide 7: 4. Evaluation
Fig. Transmission failure ratio as a function of the transmission power (IEEE model CM3，BCH encoding)
Red line: dBm/MHz

## Slide 8: 4. Evaluation
Fig. Transmission failure ratio as a function of the transmission power (IEEE model CM3，RS encoding)
Red line: dBm/MHz

## Slide 9: 4. Result
The overall tendency was for the performance of the IEEE model CM3 to deteriorate compared to that of the AWGN channel due to the effect of multipath fading
When the constraint length of the SOCC increased, the transmission failure ratio improved because the error-correcting capability increased with decreasing
On the other hand, the energy efficiency decreased because the number of redundant bits in the PPDU increased
There was almost no difference between the applications of the concatenated coding of BCH codes and an SOCC and a single SOCC when = 1/8 or less in the former
An improvement effect was seen even at = 1/32 in the case of the concatenated coding of RS codes and an SOCC

## Slide 10: 4. Discussion – Single Pulse Option
The transmission failure ratio is focused on when meeting the UWB usage limitation such that BW = 499.2 MHz and = –41.3 dBm/MHz (transmission power of -14.3 dBm)
Under the above conditions, the transmission failure ratio was more than unless an SOCC was applied, which means that sufficient reliability cannot be ensured by the current standard in the case of the single pulse option
Then, the transmission failure ratio was below when = 1/2 and below when = 1/8
RS encoding obtained better results than BCH encoding
  The compared RS code has better error-correcting capabilities than the BCH code specified in the standard
  The RS code can be expected to correct burst errors that occur during SOCC decoding since the RS code is a burst error-correcting code

## Slide 11: 5. Conclusion
Numerical results showed that sufficient dependability could not be ensured by the error control method defined by IEEE 802.15.6 and that high energy efficiency was obtained while ensuring a sufficient transmission failure ratio by applying an SOCC
It was also confirmed that a combination effect could be obtained with an SOCC by applying RS codes with almost the same coding rate as the BCH code specified in IEEE 802.15.6
SOCC has potential to be applied to more important user priority case because of the powerful error correcting capability but very low coding rate

## Slide 12: Reference
Kento Takabayashi, Hirokazu Tanaka, Katsumi Sakakibara, "Evaluation of Wireless Body Area Network Utilizing Super Orthogonal Convolutional Code," in Proceedings of 2019 International Symposium on Intelligent Signal Processing and Communication Systems (ISPACS 2019), Beitou, Taipei, Taiwan, pp.1-2, Dec. 2019.
Kento Takabayashi, Hirokazu Tanaka, Katsumi Sakakibara, "Toward Dependable Internet of Medical Things: IEEE 802.15.6 Ultra-Wideband Physical Layer Utilizing Superorthogonal Convolutional Code," Sensors, 2022, vol. 22, no. 6, 2172, Mar. 2022.

## Slide 13
13
Thank you for your attention ! ! !
* This research was funded by JSPS Grant-in-Aid for Early-Career Scientists Grant Number JP20K14737

## Slide 14: 2. IEEE 802.15.6 UWB PHY
Pulse option
Single pulse option: A single pulse transmitted per symbol
Burst pulse option: A concatenation of pulses transmitted per symbol
  This option improves the received power by correlating multiple pulses while decreasing the uncoded bit rate as increases
Transmitting signal
Fig. Signal transmission example where the burst pulse option is used

## Slide 15: 2. IEEE 802.15.6 UWB PHY
frequency
bandwidth 499.2 MHz
3993.6 MHz
7987.2 MHz
・・・
Frequency spectrum
The UWB band is divided into two band groups: low band (channel 0-2) and high band (channel 3-10) which are divided into operating frequency channels with 499.2 MHz bandwidth
Orange colors are mandatory channels (Low Band: channel 1，High Band: channel 6)
The power spectral density emission limit is -41.3 dBm/MHz which is very low
0
1
2
Low Band
・・・
・・・
3
6
10
High Band

## Slide 16: 2. IEEE 802.15.6 UWB PHY
Frame format
SHR is divided into two parts: The first part is the preamble, intended for timing synchronization, packet detection, and carrier frequency offset recovery, and The second part is the start-of-frame delimiter (SFD) for frame synchronization
The PHR contains information about the data rate of the PSDU, length of the medium access control (MAC) frame body, pulse shape, burst mode, and so on
The PSDU contains the MAC protocol data unit (MPDU)

## Slide 17: 2. IEEE 802.15.6 UWB PHY
is the power of two
As increases, a uncoded bit rate decreases
Uncoded bit rate and received signal to noise ratio (SNR) are in a trade-off relationship