## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: Proposed ptmp Security Changes
Date Submitted: 2023-09-12
Source: Yael Luz, Ondas
Abstract: Recommended changes for security
Purpose: Discussion and agreement
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
15-23-0495-01-016t-ieee802-16t-ptmp-security

## Slide 2: Current security status in D0.93
Marked in red are changes in current contribution
PKMv1 – no changes in current contribution
PKMv2
  Two/three options:
    RSA (RSA/ECC)
      Between the BS and SS. No need for backbone network
      Optional mutual authentication
    EAP based: EAP-TLS or EAP-SIM
      With authentication server
      Mutual authentication
    TLS v1.3 authentication for DPP
      Between two SS. No need for backbone network
Supported cryptographic functions:
  RSA, ECC, DES, 3-DES, AES 128, AES-256, CMAC, HMAC, SHA-1, SHA-2, SHA-3

## Slide 3: Authentication change suggestion
Remove PKMv1
Remove PKMv2 RSA (or RSA/ECC)
  TLS v1.3 can be used when backbone network is not available
Remove EAP-SIM?
Security capabilities negotiation:
  Remove from registration (SBC-REQ), use the TLS capabilities negotiation
Remove functions that are not NIST approved: DES, short RSA, SHA-1, CMAC (CMAC is approved but not recommended)