## Slide 1: Balanced In Device Coexistence
Nov 2023
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 
Stephen Rodriguez | Cisco Systems |  | 
Federico Lovison | Cisco Systems |  | 

## Slide 2: Motivation
  Solving In-Device Coexistence (IDC) shouldn’t come exclusively or predominantly at any one wireless technology’s expense
  Just because a wireless technology is more polite and resilient doesn’t mean that the wireless technology should volunteer to be subordinated to less polite and/or more brittle technologies
  Rather, we should strive for a balanced proposal that all wireless technologies can get behind

## Slide 3: Landscape
Clients (and even APs) often contain multiple wireless technologies, and each wireless technology supports one or more services (e.g., 802.11 infrastructure connectivity + off-channel P2P): define WTS = Wireless Technology Service
Different wireless technologies have different characteristics
  Licensed / unlicensed
  2.4/5/6 GHz / nearby spectrum
  Narrow band / narrow band with hopping / wider band / ultra-wideband
  Channel access via CSMA/CA / basic LBT / locally scheduled / scheduled & coordinated
  Burst transmission
In-Device-Coexistence (IDC) is a challenge
  Critical reception on one WTS blocks transmission by another WTS …
  Reduced QoS, priority inversion (when hi priority traffic has to wait for lo priority traffic)
Between-Device Coexistence (BDC) is a challenge too
  Collisions at intended receivers, reduced MCS, reduced QoS, priority inversion

## Slide 4: Global Goals
We might want to optimize the wireless medium for one or more of:
  Security
    North-south with packet inspection & limited distribution, rather than east-west traffic
  QoS
    Higher priority traffic gets through on time with higher likelihood
  Power efficiency
    Shortest transmission and reception time, fewest collisions, lowest idle RX time
  Uniform user experience
… without regard to wireless technology in use
That is, working around the limitations of a wireless technology is an explicit non-goal; rather we are asking how the industry should try to guide the evolution of wireless technologies?

## Slide 5: Transmission Time Flexibility
If critical reception on one WTS blocks transmission by another WTS, then the fundamental tool for IDC is time slicing
  Sidebar: time slicing is good for power savings too: when a wireless technology is not in use then its resources can be put into sleep mode.
Time slicing implies:
  The transmission time of each WTS is flexible to adapt to the cases when the WTS doesn’t have locally highest priority
  Each WTS first verifies that a desired peer affected by IDC is available (e.g., RTS+CTS) before continuing to data transmission. Again, this requires that these WTS transmission times be flexible to adapt to the cases when the WTS has to defer due to the wireless medium being busy and/or IDC at the peer.
  For data transmission, flexibility in turn requires that peak data rate >> offered load.
  For location, flexibility in turn requires that the duration of a ranging exchange << 1 / required range update rate.
Bottom line: in a world with IDC (and/or with inter-device coex, especially in unlicensed spectrum), each WTS needs a plan to add support for flexible transmission times

## Slide 6: Basic Channel Access with an IDC-affected peer For all wireless technologies
  Transferring and consuming IDC constraints has challenges and overheads. We need a defense-in-depth solution that minimizes overheads and maximizes opportunities & resilience …
  Prior signaling to peers provide:
    Intended periodic unavailability windows, if possible
    Otherwise, a list of irregular unavailability windows, if possible
      Advance-warning means the scheduler doesn’t have to replan on a dime
      And a list is more efficient than a single power mode transition or a single unavailability window
    An indication that the device is subject to intermittent IDC (and another notification when the intermittent IDC ends for the foreseeable future)
    An indication of the nominal duration of a nominal availability window and a nominal unavailability window (see backup*) to help with retry scheduling
  For transmission to a peer with IDC, a WTS:
    Waits till the end of a reported unavailability window (if applicable)
    Defers while the channel is busy then backs-off
    Attempts RTS+CTS
      Upon success, the WTS completes the TXOP, then goto step 2.
      Upon failure, delay according to f(nominal availability window, nominal unavailability window, next unavailability windows if known) then goto step 2.
Semi-deterministic scheduling
Blind-but-not-stupid (re)tries

## Slide 7: Global QoS For 802.11 and other wireless technologies
  Traffic, regardless of WTS and spectrum, should be prioritized based on the priority (e.g., app/user priority, expiry imminence) of the traffic (e.g., expiry imminence).
    In the enterprise, priority includes app/user (and security posture matters too!)
    Especially interested in 2.4, 5, 6 GHz & nearby spectrum
  Traffic, regardless of WTS and spectrum, should not be prioritized based on the limitations of the wireless technology used to deliver it
  A device experiencing IDC should:
    Transmit / respond / be absent according to the traffic with higher priority
    Tag each unavailability window with its priority and interruptibility, so:
      Peers with lower priority traffic can honor higher priority or non-interruptible unavailability windows
      Peers with higher priority traffic can interrupt lower priority and interruptible unavailability windows
  A peer transmitting to a device experiencing IDC should include priority within an RTS (We define RTS++ as RTS with priority)
WTS1
WTS2
WTS3
WTS4
Device 1
Device 2
Data(VO)
Defer
RTS++(VI)
BO
Planned TXOP(BE)
CTS
Data(VI)
Ack
Defer
RTS++(BE)
BO
CTS
Data(BE)
WTS0
Device 0
WTS5
Device 3


## Slide 8: Gap Analysis for 802.11
The Good
CSMA/CA
Beacons, TBTT
(MU)RTS+CTS
TXOP duration limits
Triggered TXOP Sharing
Channel Usage
The Bad
(MU)RTS does not include priority of traffic to follow
Ack/BA at SIFS without RTS+CTS
Target Wake Time (TWT) or Restricted-TWT (R--TWT) with very short Service Periods (SPs)
P2P TWT (to signal periodic, fixed-duration absences) since no allowance for absence elongation
Discovering and using IDC unavailability windows, priority constraints
Gaps
P2P TWTs with priority
Report a list of irregular unavailability windows, with priority
Define an RTS++ frame with priority
AP scheduler compute sufficient to consume this new signaling

## Slide 9: Recommendation for colleagues working in Bluetooth / Thread / Zigbee / UWB / unlicensed cellular …
  Add:
  Contention-Based Protocol
    CBP is required by FCC for LPI devices operating in 6 GHz; let’s treat this as an opportunity, and motivation, and an independent suggestion to revisit support for contention; let’s get multiple-wireless technology IDC right
  Option for RTS++ (i.e., RTS with priority) + CTS before all transmissions to a peer affected by IDC
  Deferral (i.e., flexible transmission/reception times)
  Reporting a sequence (both periodic and irregular) of unavailability windows, with priority

## Slide 10: Summary
  Balanced in-device coexistence: based on priority not technology
  For wireless technologies occupying 2.4.5.6 GHz spectrum or nearby
  Defense in depth, with built-in priority:
  Plan A: Devices report availability and unavailability windows to its peer as tersely as possible:
    Periodic sequence of unavailability windows and/or a list of irregular unavailability windows; with priorities
  Plan B
    Peers can/should use RTS++ (i.e., RTS with priority) + CTS before payload traffic
    Recipient juggles WTSs according to priority; abandons an active interruptive or planned lower priority exchange if targeted for a higher priority exchange
  Plan C: a device indicates to its peer its mean availability and unavailability windows, so the peer can choose a reasonable next time to contend when and if RTS+++CTS fails

## Slide 11: Backup

## Slide 12: Nominal availability and unavailability windows enable smarter retry scheduling
  If busy with another WTS, how long does that busy period last?
  If another WTS is idle, how long does that idle period last?
  This information can help the peer device choose how long before it retries if a RTS fails
  E.g., IDC bursts are N msec long on average (mean unavailability burst duration), mean availability burst duration is M msec long on average.
    If N << M, if a peer has a failed RTS++, then the peer defers N msec before it tries again
    If N ~ M, if a peer has a failed RTS++, then the peer defers ~N/2 msec before it tries again
    If N >> M, if a peer has a failed RTS++, then,
      for high priority traffic, the peer defers ~M/4 msec at time, with many retries
      for low priority traffic, the peer tries randomly, with many retries, e.g., after traffic with other peers is attempted to avoid a priority inversion
Slide 12
Hart et al (Cisco Systems)
WTS1
WTS2
WTS3
Device 1
Device 2
RTS (VI)
TXOP(VO)
WTS4
Device 3
TXOP(VO)
TXOP(VO)
Mean unavailability time
Mean availability time
RTS (VI)
RTS (VI)
RTS (VI)
Too late: unlikely to succeed

Too soon: unlikely to succeed
More likely to succeed