## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Privacy address requirements for TG4ab
Date Submitted: 14th November, 2023
Source: Tero Kivinen Company -
E-Mail: kivinen@iki.fi
Re: Pre ballot TG4ab draft
Abstract:
Provide a listof requiremets of privacy addressing in TG4ab
Purpose: Trying to find out what are the requirements set .by TG4ab
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Sources
P802.15.4ab-pre-ballot-B.pdf contains section 10.35.9.2.1 Private addresses and this was used to find out what are the requirements for the TG4ab private addresses

## Slide 3: Address format
6-octet (48-bit) address with 12 bits of collision resistance.
  Meaning after few thousands of invocations of this functions there will be collisions where wrong device will be marked as resolved.
Requres cryptographically strong pseudo random number generator, which is used for every single frame
Every single frame has different source address.

## Slide 4: Question 1
Do we really need to use different privacy address for every single frame?
  The distance of the device to be measured does not really change that much, so most likely the timing of the frames will allow attacker to keep track who is who, even if the addresses are different every single time.

## Slide 5: Question 2
Is the 12-bit collision resistance really enough?
  This will mean that if you have two devices in the network then after only few thousands of frames they will generate same 24-bit RPA_hash that will match other devices RPA_hash and wrong source is assumed.

## Slide 6: Question 3
Why 48-bit addresses?
  We already have 16-bit and 64-bit addresses in the IEEE Std 802.15.4, so why we need to have new 48-bit addresses?

## Slide 7: Question 4
Is it really requirement to use CSPRNG when generating the addresses, especially how weak they are?
  When the addresses has so weak collision properties, using CSPRNG to generate them is overkill.

## Slide 8: Question 5
Is there a mechanism that will solve the issues caused by the collision in ranging addresses?