## Slide 1: Study Group SUN PHY Next Generation SUN PHY’s
Hybrid Meeting
January, 2024

## Slide 2: Agenda
FCC regulations discussion on how to evaluate that OFDM-LR with its sparse sub channel hopping actually is compliant with spread spectrum modulation measurement techniques defined in the FCC.

## Slide 3
Operating in the 902–928 MHz band:
  Fixed frequency < 0dBm
  20dB Bandwidth < 250kHz
    > 50 hopping frequencies, dwell time 400ms over a 20s period
    Peak conduction power < 1W (30dBm)
  20dB Bandwidth > 250kHz
    > 25 hopping frequencies, dwell time 400ms over a 10s period
    Peak conduction power < 125mW (21dBm)
  Systems using digital modulation techniques may operate in the 902–928 MHz, 2400–2483.5 MHz, and 5725–5850 MHz bands. The minimum 6 dB bandwidth shall be at least 500 kHz. Peak conduction power < 1W (30dBm)
FCC rule interpretation prepared for IEEE meeting (please always refer to official documents)
“Operation under the provisions of this Section is limited to frequency hopping and digitally modulated intentional radiators that comply with the following provisions:”

## Slide 4: FCC 15.247 rules are public
https://www.ecfr.gov/current/title-47/chapter-I/subchapter-A/part-15/subpart-C/subject-group-ECFR2f2e5828339709e/section-15.247

## Slide 5: How to test for TX power
Test methods are defined in ANSI C63, but which one?
So the FCC made a guide
There is 3 more pages… this is incredibly comprehensive… and all of the documents can be found on IEEE (Mentor)
https://apps.fcc.gov/kdb/GetAttachment.html?id=tylb5MMggvhIlVMK75RrRQ%3D%3D&desc=558074%20D01%2015.247%20Meas%20Guidance%20v05r02&tracking_number=21124
And this guides calls for ANSI 63.10

## Slide 6: There are 5 different PSD testing methods, we have found AVGPSK-1A to provide best results for OFDM Long Range
Link to document
https://ieeexplore.ieee.org/document/9340083

## Slide 7: Proposed OFDM-LR modes
Symbol Duration | Channel Spacing | # Active Tones O1 (1 MHz) | Data Rates (DSSS=2/4/6/8) | # Active Tones O2 (500 kHz) | Data Rates (DSSS=2/4/6/8) | # Active Tones O3 (250 kHz) | Data Rates (DSSS=2/4/6/8) | # Active Tones O4 (125 kHz) | Data Rates (DSSS=2/4/6/8)
120 us | 10.416 kHz | 104 | 2 / 1 / 0.7 / 0.5 | 52 | 2 / 1 / 0.7 / 0.5 | 26 | 2 / 1 / 0.7 / 0.5 | 14 | 2 / 1 / 0.7 / 0.5
60 us | 20.833 kHz | 52 | 4 / 2 / 1.4 / 1 | 26 | 4 / 2 / 1.4 / 1 | 12 | 4 / 2 / 1.4 / 1 | 6 | 4 / 2 / 1.4 / 1
30 us | 41.666 kHz | 26 | 8 / 4 / 3 / 2 | 12 | 8 / 4 / 3 / 2 | 6 | 8 / 4 / 3 / 2 | - | -
15 us | 83.333 kHz | 12 | 17 / 8 / 6 / 4 | 6 | 17 / 8 / 6 / 4 | - | - | - | -
Using SUN-OFDM as a baseline, the proposed OFDM-LR also includes a significant number of options to enable world wide deployment.
In the follow pages we are showing the FCC PSD measurements on
Symbol duration = 60us, Option 2, DSSS=6 => 550KHz wide signal with 1.4kbps effective data rate
Sensitivity on HW was measured at -124dBm @ 64 byte payload @ 10 % PER

## Slide 8: Proposed OFDM-LR synchronization
Synchronization sequence needs to have 0 dB PAPR
Synchronization sequence shall not limit sensitivity (better than -125 dBm)
In the trade-off between over-the-air time vs receiver complexity, over-the-air time has higher priority
10 ppm of XTAL accuracy
+/- 20 kHz of frequency offset tolerance
16 + 64 + 64 DBPSK symbols (1 symbol DBPSK = 120 us)
Total duration of 144 symbols, 17.28 ms
Equivalent of 4.32 information bytes @ 1.4 kbps
Synchronization sequence sent in one single tone
Preamble | SW | SW

## Slide 9: OFDM-LR vs CCS interference performance
Measured with 1% PER limit, wanted signal at 3 dB above sensitivity level |  | Interferer signal |  |  |  |  | 
 |  | LR-OFDM | LR-OFDM without a sync | LR-OFDM with new seed and no sync | LR-OFDM with new seed and sync on a different tone | Lora | CW
Wanted signal | LR-OFDM wanted | -9.3 dB | 1.2 dB | 8.2 dB | 8.8 dB | 12.0 dB | 17.6 dB
 | Lora wanted | 12.4 dB | 12.3 dB | 15.1 dB | 15.0 dB | -11.2 dB | 14.3 dB

## Slide 10: There are 5 different PSD testing methods, we have found AVGPSK-1A to provide best results
Measured at 27dBm total power, so at -124dBm sensitivity this will result in a link budget of 151dB

## Slide 11: PSD measurement including the preamble/sync word
Measured at 27dBm total power