## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: Toward consensus before resolving MMS ranging CIDs
Date Submitted: March 2024
Source: Carl Murray (Qorvo)
Abstract: Need agreement on MMS operation before related CIDs can be resolved
Follow-up on document 15-24-0120-00-04ab
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2: Need for Consensus
There are several inconsistencies currently in Draft C that need to be addressed through agreement on the requirements before the following CIDs can be resolved.
  The MMS CIDs listed below are a consequence of this but cannot be resolved individually because the text in inconsistent in some areas.
  CIDs in related groups and in page order
    Related to Figure 21 – UWB MMS ranging transmission
      318, 683, 894 and 52
    Distinction between NBA and ‘non’-NBA
      7
    MMS configurations
      684, 212, 901, 29, 80, 729, 81, 90, 91, 296
    Multiple transmissions
      624, 332
    Related docs of interest - 15-23-0509-04-4ab, 15-24-0025-01-04ab
Answering the questions raised in the following slides will allow me to propose resolutions for the above CIDs.

## Slide 3: The UWB MMS packet
Figure from Clause 16.2.11.1 (Draft C page 160)
The UWB packet can be utilized by any protocol
  It is currently used by the protocol defined in 10.38 UWB Multi-millisecond (MMS) operation
    The ranging PHY for this protocol is always UWB
    At least 2 of the 3 other phases (see next slide) of this protocol can be implemented by either NB and/or UWB
  The optional SYNC+SFD are necessary to enable protocol(s) to implement 10.38.12.5 UWB Only MMS Operating Parameter Sets.

## Slide 4: (Simplified) MMS Ranging Phases in 10.38
Initialization and Setup
Control
Ranging
Report
Ranging Cycle

## Slide 5: MMS Ranging Mechanisms currently allowed by Draft C Text (but with gaps and inconsistencies)
 |  | Init & Setup | Control | Ranging | Report
A | NBA | O-QPSK | O-QPSK | UWB | O-QPSK
B | NB + UWB report offload | O-QPSK | O-QPSK | UWB | UWB
C | NB + UWB control offload | O-QPSK | UWB | UWB | O-QPSK
D | NB init only | O-QPSK | UWB | UWB | UWB
E | UWB-driven | NS* | UWB | UWB | UWB
F | OOB mechanism | NS* | NS* | UWB | NS*
* Not Specified

## Slide 6: Areas that need Consensus - Q1
TG4ab needs to agree on the configurations that the standard will support in the text.
TG4ab agrees that the standard will support the following configurations
  A
  B ?
  C ?
  D ?
  E
  F ?
What category do configurations B, C and D belong (section 10.38.1, pg 42 – see next slide)?
TG4ab agree that the following configurations qualify as an HRP-ARDEV
  A, E, … any others ?

## Slide 7: Draft C text related to Q1 The following text is from clause 10.38.1 referenced in the previous slide
Pg 42

## Slide 8: Areas that need Consensus - Q2
TG4ab need to agree the UWB packet format in the Control phase
  Are these HPRF SP0 only packets?
  Note that there is no such thing as a SYNC+SFD only packet in clause 16
  See 15-24-0133-00-04ab for discussion on options (images below taken from this)
There is a one-to-one mapping between NBA and UWB-only. The NB protocols will map simply to UWB-only.
Currently not supported by Draft C as the text currently says that UWB-only must have SHR in ranging packet.
There is no clean mapping between NBA and UWB-only. The NB protocols will not map simply to UWB-only.
Currently not supported by Draft C as there is no SHR-only packet and there is no protocol/text supporting 2 packets per device in the control phase.
There is a one-to-one mapping between NBA and UWB-only. The NB protocols can map to UWB.
This configuration can be supported by Draft C with modifications
Are ranging SHRs interleaved like RSFs/RIFs?
Is the ranging SHR optional (configured statically)?
Does TG4ab want to allow the control phase packet to be either an SP0 packet or an SHR-only packet?

## Slide 9: Draft C text related to Q2

## Slide 10: Areas that need Consensus - Q3
TG4ab need to agree when the optional SYNC+SFD of the MMS packet is enabled
In configuration A there is no SYNC+SFD in the MMS packet
In configuration E the use of the SYNC+SFD in the MMS packet is configurable at initialization & setup and cannot be dynamically changed by short term parameters (i.e. within the ranging session)
In modes B, C, D and F … ?

## Slide 11: Areas that need Consensus - Q4
Need to agree if the configurations are static? (i.e. do not allow to dynamically switch between them)
  This would impact the short-term parameters in some way
    Currently short-term parameters in Management PHY config allows switching between various flavours of NBA
    What happens if ADV-RESP signals a Management PHY Config that the Initiator does not support? Is there a single mandatory mode for NBA that the Initiator can insist on?
TG4ab agree that dynamic switching between configurations will not be done

## Slide 12: Areas that need Consensus - Q5
Is the same UWB channel used for all phases?
  (e.g. do Report and Control use the same channel as ranging)?
Propose that TG4ab agree that when UWB is being used in MMS ranging that all phases using UWB use the same UWB channel

## Slide 13: Areas that need Consensus - Q6
What preamble code is used in the UWB SP0 packets?
  Note that the preamble code for the control and report packet is currently defined as a function of the ‘Sequence Code Index’ field in the Ranging PHY Config
    This field can contain length-127 and length-91 ternary codes but SP0 is HPRF only
    The current mapping does not take account of length-127 RSF codes
    The current mapping imposes a hard link between SP0 and the RSF codes
Propose extend the existing Sequence Code Index field mapping to map length-127 RSF codes to length-91 SP0 codes?

## Slide 14: Draft C text related to Q6
Pg 70
Pg 67

## Slide 15: Areas that need Consensus - Q7
What is the preamble code for the MMS Packet SYNC+SFD
  Currently this is not defined
  Note that the MMS Packet SYNC+SFD possibly should not ‘copy’ the SYNC and SFD of SP0 because SP0 is HPRF only whereas the RSF can be length-127 and length-91 codes
  This means that there could be a mix of ‘preamble’ codes in the MMS packet
Propose that the SYNC+SFD must have the same code as the RSF if the RSF is either length-127 or length-91 (i.e. Ipatov)
Propose that the SYNC+SFD should use the same formula as defined SP0 if the RSF is length-128 (i.e. complementary pairs)?

## Slide 16: Backup
 | SP0 | MMS Packet SYNC+SFD | RSF
Channel | undefined | R-PHY Config | R-PHY Config
Preamble Code | undefined | fn(SCI) | R-PHY Config
SYNC | M-PHY Config | undefined | N\A
SFD | M-PHY Config | undefined | N\A
Data Config0 | M-PHY Config | N\A | N\A
Data Config1 | M-PHY Config | N\A | N\A
M-PHY = Management PHY
R-PHY = Ranging PHY
SCI = ‘Sequence Code Index’ field of the R-PHY Config