## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [DraftC comment resolution proposals for LBT related comments (CIDs 40, 76, 276, 277, 278, 279, 280, 281, 282, 283, 284, 285, 286, 289, 290, and 291)]
Date Submitted: [April 22, 2024]
Source: [Alex Krebs (Apple)]
Email: a_krebs @ apple.com
Re: [Input to the Working Group]
Abstract: [Discussion and resolution proposals to LBT related comments of DraftC]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Content
LBT discussion (p.3-7)
  Quick catch up on regulatory & coex discussion
  Recap of LBT contribution(s) presented to 802.15.4ab
  Conclusions & recommended way forward
Comment resolution (p.8-18)
  Related 4ab/4me comments previously resolved
  DraftC comment resolution proposals

## Slide 3: Regulatory summary
UNII-3 (5725-5850 MHz) and UNII-5 (5925-6425 MHz) is shared unlicensed spectrum between 802.11 and 802.15.4ab and other wireless technologies in both ETSI and FCC regulatory domains
EC approved harmonized standards for 5.8 GHz
  ETSI EN 300 440 (Final draft v2.1.1, 2017): No LBT (802.11/.15, BT, ...)
  ETSI EN 301 893 (v2.1.1, 2017): v2.2.1 adding sub-band 4 currently in ENAP, raised 20 dBm output power limit for WB (802.11, 3GPP, ...)
6 GHz standard under active development in ETSI BRAN
  ETSI EN 303 687 (Early draft v1.1.3, 2024-02-23)
  market demand analysis, no preferential treatment of one wireless technology over another, consensus driven, one vote per company
  current status: active open work item (OWI) on NB/WB coexistence, no text draft for OWI yet, “very fruitful technical discussions”

## Slide 4: Contributions 802 & others
Only 1 contribution in IEEE 802.15.4ab
  Effect of no-LBT NB on 802.11 devices, Carlos Aldana (Meta), 15-23-284r2
36 contributions on LBT, eDAA/rDAA, SCD, and other methods presented in ETSI BRAN and 802.11 CoexSC since 2023
Document number | Title | Submitting entity
BRAN(23)119007 | Spectrum Sharing Wide-band vs Narrow-Band Wide-band vs Wide-band and more | Apple (UK) Limited
BRAN(23)121007 | VR simulation scenarios for narrowband-wideband coexistence studies | Meta Ireland
BRAN(23)121008 | IEEE 802.11 and Bluetooth Coexistence Simulations | Ericsson GmbH Eurolab
BRAN(23)121013 | NB simulation results comparison | Qualcomm Tech. Netherlands B.V
BRAN(23)122011 | Effect of LBT on the coexistence of narrowband and wideband systems | Meta Ireland
BRAN(23)121011r5 | NBFH test signal draft text | Ericsson France S.A.S
BRAN(24)123013 | Bluetooth isochronous audio with LBT | Qualcomm Tech. Netherlands B.V
BRAN(24)123011 | Balancing Wideband and Narrowband Frequency Hopping Channel Access Mechanisms for Operation in 6GHz | Ericsson GmbH Eurolab
BRAN(24)123017 | Secondary Channel Deferral LBT for narrow band frequency hopping systems | Ericsson LM
BRAN(24)123018 | Background for the first 6 GHz harmonised standard | Ericsson France S.A.S
BRAN(24)123020 | Response to BRAN(24)123013 | Ericsson France S.A.S
BRAN(24)123021 | NB channel access with LBT | Qualcomm Tech. Netherlands B.V
BRAN(24)123015r1 | NB interference on WB signal | Ericsson France S.A.S
BRAN(24)123008r1 | Enabling LBT for narrowband FHSS transmission | Intel Corporation SAS
BRAN(24)123010 | NB test signal issues | Qualcomm Tech. Netherlands B.V Intel Americas Inc. Broadcom (EU) Meta Ireland MediaTek Inc.
Year | DCN | Rev | Title | Authors
2024 | 360 | 3 | CCA Modes in 802.15.4 | Carlos Aldana (Meta)
2024 | 148 | 0 | NB Simulation Results Comparison | Carlos Aldana (Meta), Menzo Wentink (Qualcomm)
2024 | 130 | 0 | Effect of no-LBT NB on 802.11 devices: Part 2 | Carlos Aldana (Meta)
2023 | 1259 | 1 | Effect of no-LBT NB on 802.11 devices | Carlos Aldana (Meta)
2024 | 148 | 0 | NB Simulation Results Comparison | Carlos Aldana (Meta), Menzo Wentink (Qualcomm)
2024 | 122 | 0 | Bluetooth isochronous audio with LBT | Menzo Wentink (Qualcomm)
2023 | 2081 | 0 | BLE interference to XR/VR Wi-Fi | Menzo Wentink (Qualcomm)
2023 | 1622 | 0 | NBFH coexistence with Wi-Fi | Menzo Wentink (Qualcomm)
2023 | 1279 | 0 | NB with LBT | Menzo Wentink (Qualcomm)
2023 | 455 | 0 | Wi-Fi deferral for NB signals | Menzo Wentink (Qualcomm)
2023 | 454 | 0 | Impact of BT on WLAN performance | Menzo Wentink (Qualcomm)
2023 | 453 | 0 | NB overview | Menzo Wentink (Qualcomm)
2024 | 521 | 0 | Improving performance of LBT-enabled NB in UNII-3 band | Ratnesh Kumbhkar (Intel)
2024 | 7 | 0 | Proposal for Bluetooth and Wi-Fi Coexistence in 5 and 6GHz | Ratnesh Kumbhkar (Intel)
2023 | 1503 | 0 | Bluetooth Wi-Fi Coexistence: Channel Access Simulation Study | Ratnesh Kumbhkar (Intel)
2023 | 877 | 0 | Narrow Coex Studies | Stuart Thomas (Apple)
2024 | 603 | 2 | Balancing Wideband & Narrowband Frequency Hopping Channel Access Mechanisms for Operation in 6GHz | Sebastian Max (Ericsson)
2024 | 445 | 0 | Follow-up to IEEE 802.11-24/0055r0 Puncturing for Coexistence | Sebastian Max (Ericsson)
2024 | 55 | 0 | Evaluation of Puncturing for Coexistence of IEEE 802.11 and Bluetooth in 6 GHz | Sebastian Max (Ericsson)
2023 | 1999 | 0 | IEEE 802.11 Beacons and Bluetooth Coexistence Simulations | Sebastian Max (Ericsson)
2023 | 1477 | 1 | IEEE 802.11 and Bluetooth Coexistence Simulations | Sebastian Max (Ericsson)

## Slide 5: Previous IEEE discussion on 15-23-285
”Effect of no-LBT NB on 802.11 devices”, Carlos Aldana et al. (Meta)
  “For No LBT, a 3% duty cycle causes ~50% increase in P95 latency”
  simulation of BT as 100% duty cycle (p.7), impossible BT connection interval simulation parameters (p.8-10), NB operation only on 802.11 primary channels (p.19), ...
  no comparison with other methods
same simulation results presented at ETSI BRAN #122 and 802.11 CoexSC Panama F2F with diverging conclusions
  Meta Ireland (Claudio da Silva) points out in BRAN(23)112011 that LBT impact to NB is unknown and would still need to be assessed (link)
  802.11-24/148r0 removes mention of missing LBT impact assessment on NB for straw poll on in 802.11 only CoexSC session

## Slide 6: Is LBT really great?
CCA/EDT LBT is a rudimentary method to resolve packet collisions
  No conflict avoidance, only one packet survives, greedy TXOP wins
  LBT prioritizes 802.11 over BT traffic (11-23/1503r0 [R. Kumbhkar, Intel], 11-23/1477r1 [S. Max, Ericsson])
  BLE devices are generally not well suited to utilize LBT [Bluetooth Low Energy – Regulatory Aspects Document (RAD) v1.01, BT Regulatory Expert Group, March 2023]
eDAA and SCD were presented, aiming to efficiently manage coexistence by preventing packet collision before happening
  collaboration on eDAA/rDAA presented in 11-23/1503r0, concluding in ask to 802.11 to converge on realistic simulation scenarios and performance metrics for BT and WiFi
  thwarted by adding sub 10ms AR/VR WiFi latency requirements (11-23/1259r1)  effectively ending coex discussion by claiming LBT is the solution, w/o comparison
Despite ETSI BRAN(23)112011 noting no impact assessment of LBT to NB being provided, majority of 802.11 CoexSC participants vote at IEEE 802 Panama January 2024 in favor of mandating LBT to 802.15.4ab nevertheless
  Straw poll result in 802.11 CoexSC, January 16, 2024: Y/N/A: 44/13/0 (77%/23%/0%)
  Distribution of 802.11/.15 voting members as of January 2024: 723/136 (84%/16%)

## Slide 7: Recommended way forward
Coex discussion is more appropriately handled in ETSI
  Commit to finding the best coexistence solution with no hierarchy or priority given to either wide-band or narrow-band technology asserting both have equal rights to use the 5925-6425 MHz band within the bounds of regulation as stated in ECC Decision (20)01 and the subsequent implementing decision EU 2021/1067
Adding mandatory LBT/coex requirements to 802.15.4ab is nonsense
  risks voiding the 802.15.4ab standard by violating yet unknown 6 GHz regulatory rules (e.g. due to very specific CCA parameter definitions)
  deprioritizes 802.15.4ab behind all other 5.8 GHz 802.11, 3GPP, BT, ...
Reject 15.4ab comments submitted against draft C that
  assert LBT is the only way of spectrum sharing
  put the 4ab standard at risk of violating regulatory rules
  deprioritize access of 802.15 radios behind other wireless technologies operating in shared unlicensed spectrum

## Slide 8: Previous WG15 comment resolutions
15-23-591-01-4ab Draft B #235 (“Restrict 802.15.4ab BW in 6 GHz”, #236: ”Disallow 802.15.4ab access to 802.11 PSCs in 6GHz”
  unilaterally deprioritized access for 802.15 to unlicensed spectrum
  restricting NB bandwidth increases coexistence conflicts
  Rejected/withdrawn
15-23-497-22-4me (LB203): #r3-3 and #r3-5 (“add specific EDT values -80dBm/MHz”), #r3-4 (“add duty cycle restriction to CCA mode 4”)
  802.15.4-2020 specifically notes no mandatory values are defined in order to be able to “meet regulatory requirements” (P802-15-04me-D01, p.619)
  unilaterally deprioritized access for 802.15 to unlicensed spectrum
  Rejected/withdrawn

## Slide 9: 802.15.4ab Draft C resolution proposals

## Slide 10
~ LBT is good/great, mandatory LBT in UNII-3 w/wo DC
Name | Index # | Category | Page | Sub-clause | Line # | Comment | Proposed Change
Carlos Aldana | 276 | Technical | 51 | 10.38.4.2 | 6 | LBT is proven to be a great coexistence technique. Given that there is no mandatory coexistence technique for NB, LBT should be made mandatory. Replace "can" with "shall" and remove "the use of this may be mandated depending on local regulations" | As in comment
Carlos Aldana | 280 | Technical | 58 | 10.38.8.3 | 4 | LBT is proven to be a great coexistence technique. Given that there is no mandatory coexistence technique for NB, LBT should be made mandatory. Replace the sentence "LBT may be applied to all channels in the absence of regulatory constraints, for example, to improve coexistence with other spectrum users." with "LBT shall be applied to all channels to improve coexistence with other spectrum users". | As in comment
Li-Hsiang Sun | 40 | General | 29 | 10 | 3 | There are simulations in Nov 2023 802.15 and 802.11 sessions shown NB impact to wifi coex. Suggest to adopt a mandatory LBT for NB transmission if aggregated NB duty cycle is more than a threshold | as in comment
Pooria Pakrooh | 76 | Technical | 58 | 10.38.8.3 | 3 | NB coexistence with other technologies in UNII-3 and UNII-5 bands needs to be addressed. A good option is what has been suggested in DCN 285/Rev2, to mandate LBT for high duty cycle NB operation. | Change: "LBT shall be applied to channel numbers 50 to 249 according to regulatory constraints. LBT may be applied to all channels in the absence of regulatory constraints, for example, to improve coexistence with other spectrum users." To: "LBT shall be applied to channel numbers 50 to 249. LBT shall be applied to channels 0-49, for NB duty cycle >= TBD%."

## Slide 11
CIDs 276, 280, 40, 76 (see previous slide)
Proposed resolution: Reject
Disposition detail: The group assesses that
  no assessment has been presented to the group on how LBT would affect narrowband radios following the upcoming 802.15.4ab standard
  despite claiming LBT is great, no information has been presented by the commenters to show that LBT is generally favorable over the methods currently being discussed in other coexistence and regulatory standardization forums
  one-sided requirements (with, or without depending on duty cycle) only applicable to 802.15.4ab unjustly deprioritize 802.15.4ab radios from accessing unlicensed spectrum shared with other wideband radios following 802.11 or 3GPP standard and possibly narrowband radios following BT SIG, or other standards in the future

## Slide 12
Proposed resolution: Reject
Disposition detail
  The group assesses that the current text is accurate in stating that LBT shall be used for channels 50-249 subject to the existence of a regulatory requirement but may also be used in the absence of regulatory requirements to e.g. improve coexistence with other radios
  Regarding channel 0-49, the group assesses one-sided requirements only applicable to 802.15.4ab unjustly deprioritize 802.15.4ab radios from accessing shared unlicensed spectrum between 5725 MHz and 5850 MHz behind other wireless technologies
Name | Index # | Category | Page | Sub-clause | Line # | Comment | Proposed Change
Carlos Aldana | 279 | Technical | 58 | 10.38.8.3 | 3 | The statement "LBT shall be applied to channel numbers 50 to 249 according to regulatory constraints." should be clarified as the word "according" is ambiguous. After reading the subsequent sentence, I think the author meant "in the presence of regulatory constraints". If that's the case, then regulatory constraints are already mandating LBT and the aforementioned statement does not provides additional information. Replace with "LBT shall be applied to channel numbers 0 to 249." | As in comment

## Slide 13
see next slide
Name | Index # | Category | Page | Sub-clause | Line # | Comment | Proposed Change
Carlos Aldana | 277 | Technical | 57 | 10.38.8.3 | 15 | How long is the CCA duration? Figure 35 suggests 9us, but there is no text that says that. Please add text that specifies the minimum CCA duration. | As in comment
Carlos Aldana | 278 | Technical | 57 | 10.38.8.3 | 15 | What is the Energy Detect (ED) Threshold that should be used? Please specify. | As in comment
Carlos Aldana | 289 | Technical | 58 | 10.38.8.3 | 17 | In Figure 35, there is at least 100us of idle time between successive transmissions. There is no text that describes this idle time. Please add corresponding text that accomodates required idle time. | As in comment
Carlos Aldana | 290 | Technical | 58 | 10.38.8.3 | 17 | In Figure 35, there is at least 100us of idle time between successive transmissions. If the ranging slot duration is 300 RSTU (250us), will there be enough time to accommodate this idle time? If there is not enough time, what is expected behavior? | Please clarify
Carlos Aldana | 291 | Technical | 58 | 10.38.8.3 | 17 | In Figure 35, there is an upper bound of 95% of the ranging slot on the transmission duration. There is no text associated with this. Please add such text. | As in comment
Carlos Aldana | 286 | Technical | 58 | 10.38.8.4.2 | 18 | How does the initiator determine whether a channel is unavailable, unusable, or inefficient? Is it via passive scanning? If so, how long is the passive scanning duration? How accurate should this result be? What energy detect threshold should be used? All this needs to be specified. | As in comment

## Slide 14
Draft C p.57 shown on this slide
see next slide

## Slide 15
CIDs 277, 278, 286, 289, 290, 291 (see previous two slides)
Proposed resolution: Revise
Disposition detail:
  The group assesses that the currently provided draft text inappropriately mandates specific regulatory rules from the EU regulatory domain (of one specific frequency band) to all frequency bands globally
  Following the existing 802.15.4-2020 standard, the group agrees to remove all regulatory domain specific values from the draft text and to keep the existing language “according to regulatory constraints” instead, following e.g. P802-15-04me-D01, p.619)
  The group instructs the technical editor to remove text p.57 l.15 and following starting at “After completing the CCA” to p.60 l.2 (including Figure 35) and to remove [B3] from the bibliography (p.192)

## Slide 16
Proposed resolution: Revise
Disposition detail
  The group has revised the text before in correspondence to CIDs 21, 22, 25, 28, 164, and 166 in DCN 15-23-0575-02-4ab and assesses no further action is needed
Name | Index # | Category | Page | Sub-clause | Line # | Comment | Proposed Change
Carlos Aldana | 281 | Technical | 59 | 10.38.8.4.2 | 1 | Figure 36 has a typo in the WLAN 20 MHz channel list. "168" should be "165". | As in comment
Carlos Aldana | 282 | Technical | 59 | 10.38.8.4.2 | 2 | There is no text associated with "Scaling Factor" in Figure 36. | Please add text that describes this feature.

## Slide 17
Proposed resolution: Accept
Name | Index # | Category | Page | Sub-clause | Line # | Comment | Proposed Change
Carlos Aldana | 284 | Technical | 102 | 10.38.11.1 | 18 | The following 802.11 20 MHz channel center frequencies are likely to have a lot of traffic (probe request, beacons from 6GHz only APs, and probe responses) and should be removed from the initial macMmsNbChannelAllowList to prevent ranging outages: 5975, 6055, 6135, 6215, 6295, and 6375 MHz | Remove channels 66:73, 98:105, 130:137, 162:169, 194:201, 226:233 from the table

## Slide 18
Proposed resolution: Reject
Disposition detail
  The group assesses that isolated sub-band access to UNII-1 is unfavorable due to physical and regulatory constraints for 802.15.4ab narrowband radio
  The group assesses that prohibitive access restrictions in 5925-5945 MHz may apply subject to regulatory domain, e.g. due to concurrent GSM-R operation (European Rail Traffic Management System)
Name | Index # | Category | Page | Sub-clause | Line # | Comment | Proposed Change
Carlos Aldana | 283 | Technical | 147 | 11.1.3.15 | 11 | The following 20 MHz block of frequency is not used by 802.11 devices in UNII-1: 5150-5170 and could be added to the frequency list to increase the number of channels allocated for NB. | As in comment
Carlos Aldana | 285 | Technical | 147 | 11.1.3.15 | 11 | The following 20 MHz block of frequency is not planned to be used by 802.11 devices in UNII-5: 5925-5945. Redefine the UNII-5 frequencies so that k=50,…249 is replaced with 50,…57 | As in comment