## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Proposed Resolutions CIs 40 and 715
Date Submitted: 6 May 2024
Source: Benjamin A. Rolfe (Blind Creek Associates)
Contact:
Voice: +1 408 395 7207, E-Mail: ben.rolfe @ ieee.org
Re: TG4ab First Comment Collection
Abstract: Proposed resolutions to CI 40 and CI 715
Purpose: Resolve Comments.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2: CI 715
Clause: 10.38.10.3.6
Comment: The order of the octets in this field [PT data] are not specified
Proposed resolution: Replace text in with:
The PT Data field is a string of octets. Upon transmission, the value shall be set to the Msdu parameter in the MCPS-Data.request; upon reception, the content is provided to the higher layer in the Msdu parameter in the MCPS-Data.indication. The length of the octet string is determined by the PT Data Length field value.
Discussion: The order for strings is defined in the base standard.

## Slide 3: CI 40
Comment: There are simulations in Nov 2023 802.15 and 802.11 sessions shown NB impact to wifi coex. Suggest to adopt a mandatory LBT for NB transmission if aggregated NB duty cycle is more than a threshold
Clause: 10
Proposed Resolution: Revised
Resolution Detail: Add the following text to 10.38.8.1 following the first paragraph: “The expected data volume in initialization, control and report phases is low, resulting in very low activity factor in the narrow band channel. If higher activity factor is expected, use of one of the channel access methods that employ CCA to sense channel status can improve performance and reduce impact on other users of the channel.”
Discussion: The comment provides no specific duty cycle threshold, but suggests that limiting duty cycle is an effective coexistence mitigation with which we agree. When used for NBA MMS the expected data volume is often low and so will be activity in the NB channel, Adding informative text to clarify this. The standard provides multiple LBT schemes already; Specific requirements or recommendations are being provided in other contributions. This informative statement is technically accurate and not in conflict with other specific details such as setting CAA threshold and duration (being addressed in other contributions).