## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for TG15.4ad Channel Models]
Date Submitted: [14 May, 2024]
Source: [Joerg ROBERT] Company [TU Ilmenau/Fraunhofer IIS]
Address [Helmholtzplatz 2, Ilmenau, 98693, Germany]
E-Mail:[joerg.robert@ieee.org]
Abstract: []
Purpose: [Presentation in TG15.4ad]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Motivation
Comparison of different proposals requires simulations of the physical layer performance
Only using Additive White Gaussian Noise is not realistic due to multi-path components, especially relevant for OFDM

## Slide 3: Two Proposed Models
Additive White Gaussian Noise
  Packet Error Rate vs. SNR
3GPP Suburban Macro Channel Model (next page)
  Packet Error Rate vs. SNR

## Slide 4: 3GPP Suburban Macro Channel Model
Use of the 3GPP Spatial Channel model scenario “Suburban Macro” [1, sec. 5] – only the multi-path channel
Similar approach followed by 802.11ah
Model defines path-loss and multi-path for outdoor operation, here we are only interested in multi-path
Open source code and commercial implementations available
Additional parameters
  Frequency set to f=900MHz
  Speed set to v=3km/h (also to model effects like phase-noise)
  Use of single polarization with omni-directional antenna only
Additive White Gaussian Noise (AWGN) has to be added at the receiver side, relevant is Packer Error Rate vs. the SNR

## Slide 5: Literature
[1] Spatial channel model for Multiple Input Multiple Output (MIMO) simulations (Release 18), 3GPP TR 25.996, V18.0.0, Mar. 2024 https://www.3gpp.org/ftp/Specs/archive/25_series/25.996/25996-i00.zip