## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Fundamental Field Experiments of OFDMA Systems Using VHF-band in Urban Area]
Date Submitted: 14 May 2024
Source: Hiroshi Harada (Kyoto University)
Address Yoshidahonmachi. Sakyo, Kyoto, 606-8501, Japan
Voice: +81-75-753-5317 , E-Mail: hiroshi.harada@i.kyoto-u.ac.jp
Re: [Wireless Next Generation, Long Range extension enhancements to 802.15.4-2020]
Abstract: Introduce fundamental field experiments results of OFDMA systems using VHF-band in Urban Area. A part of this contribution was supported from the commissioned research (No.05101) by National Institute of Information and Communications Technology (NICT) , Japan.
Purpose: Provide basic information on dynamic range and transmission distance of OFDMA system in VHF
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Fundamental Field Experiments of OFDMA Systems Using VHF-band in Urban Area
July 12, 2023
Hiroshi Harada, Ph.D.
Reference: Hiroshi Harada, “Fundamental Field Experiments of OFDMA Systems Using VHF-band in Urban Area,” 2023 26th International Symposium on Wireless Personal Multimedia Communications (WPMC), Florida, USA, Nov. 2023

## Slide 3: Background
One use case of the 802.154ad group is the proposal of various applications using OFDM systems using the VHF band.
Also channel bandwidth exceeding 1 MHz as channel bandwidth has been proposed.
This presentation shows the characteristics of a 5 MHz OFDMA signal transmitted in the VHF band.

## Slide 4: Expected use cases of IEEE 802.15.4 SUN
H. Harada, K. Mizutani, J. Fujiwara, K. Mochizuki, K. Obata, and R. Okumura, “IEEE 802.15.4g based Wi-SUN Communication Systems,” IEICE Transactions on Communications, E100-B, No. 07, pp. 1032–1043, Jul. 2017.

## Slide 5: ARIB STD-T103/IEEE 802.16n
Duplex scheme
  Time division duplex (TDD)
Multiplexing/Multiple access scheme
  Uplink: OFDMA
  Downlink: OFDM+TDM
Channel plan
  5MHz/ch × 6 channels
Original channel estimation scheme [1] is equipped
[1] K. Makino, K. Mizutani, T. Matsumura, and H. Harada, “ Super-Large-Coverage Standardized Wireless Communication System and Its Implementation in VHF Band for IoT and V2X,” IEEE Open Journal of Vehicular Technology, pp. 667-680, Sept. 2023.

## Slide 6: Received power vs BER
BER of 10-6 is achieved when QPSK-OFDMA is used at a received signal power lower than -97 dBm

## Slide 7: Configuration of the outdoor experiment

## Slide 8: Measurement setup
Parameter | Specification
Base standard | ARIB STD-T103 Mode 1/IEEE 802.16n
Carrier frequency | 195 MHz
MCS | QPSK-OFDMA, R=1/2
DL: UL frame ratio | 26:21
Max TX rate | 2.3 Mbps (DL)
BS height | 56 m
TX power | 5 W (37 dBm)
TX antenna/Gain | Ground plane antenna / 2.15 dBi
Actual TX power | 34 dBm
MS antenna/ Gain | Whip antenna/ 2.15 dBi
MS height | 2.4 m
Diversity | Two-branch maximum ratio combining

## Slide 9: Received signal power characteristics
Received signal power characteristics (The line in red is a calculated received power by extended Hata model)
Measurement points in the area around BS (Map sourced by Geospatial Information Authority of Japan)
Received signal power of about -97 dBm, which is the required power to obtain a BER of 10-6 when using QPSK-OFDMA, is achieved over the entire area

## Slide 10: Delay spread characteristics
Delay spread characteristics
Measurement points in the area around BS (Map sourced by Geospatial Information Authority of Japan)

## Slide 11: Received signal power characteristics
Instantaneous BER characteristics
Measurement points in the area around BS (Map sourced by Geospatial Information Authority of Japan)

## Slide 12: Received signal power characteristics
Received signal power characteristics (The line in red is a calculated received power by extended Hata model)
Measurement points in the area around BS (Map sourced by Geospatial Information Authority of Japan)
Received signal power of about -97 dBm, which is the required power to obtain a BER of 10-6 when using QPSK-OFDMA, is achieved over the entire area of 10 km

## Slide 13: Delay spread characteristics
Delay spread characteristics
Measurement points in the area around BS (Map sourced by Geospatial Information Authority of Japan)

## Slide 14: Received signal power characteristics
Instantaneous BER characteristics
Measurement points in the area around BS (Map sourced by Geospatial Information Authority of Japan)

## Slide 15: Conclusion
When 5 MHz OFDMA signals are transmitted in the VHF band, a transmission of 10 km at 10 Mbps or more is possible.
The link budget is estimated to be around 130 dB at 37 dBm and 110 dB even at 10 dBm, as the reception sensitivity of this equipment is -97 dBm.