## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Ranging Report for DS-TWR with UWB MMS Packets
Date Submitted: August 2024
Source: Xiliang Luo, Vinod Kristem, Moche Cohen (Apple)
Address: One Apple Park Way, Cupertino, CA 95104, USA
E-Mails: xiliang_luo@apple.com
Abstract: Provide a description of the ranging reports for secure DS-TWR in the context of UWB MMS.
Purpose: Clarify the ranging reports in the context of UWB MMS ranging.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
        DOC: 15-24-0436-00-04ab

## Slide 2: Mixed MMS & RMARKERs for Ranging Integrity
        DOC: 15-24-0436-00-04ab

## Slide 3: Part-1: Measurements for UWB MMS Ranging Integrity
        DOC: 15-24-0436-00-04ab

## Slide 4: DS-TWR with 3 Pkts: Multiple Sets of RMARKERs
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
1
2
2
2
Ping1-Set2
Pong-Set1
Pong-Set2
Ping2-Set1
Ping2-Set2
Each set of RIF-RMARKERs include: Ping1, Pong, Ping2
Ping1-RMARKER from Initiator’s 1st MMS packet
Pong-RMARKER from Responder’s MMS packet
Ping2-RMARKER from Initiator’s 2nd MMS packet
2 Ping1-RMARKERs
from Initiator’s Packet 1
2 Ping2-RMARKERs
from Initiator’s Packet 2
        DOC: 15-24-0436-00-04ab

## Slide 5: Ranging Measurement Report: Type-1, Set#1
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
Pong-Set1
Ping2-Set1
RoundTrip1
Reply1
RoundTrip2
Reply2
1
        DOC: 15-24-0436-00-04ab

## Slide 6: Ranging Measurement Report: Type-2, Set#2
Device-A
Initiator
Device-B
Responder
2
2
Ping1-Set2
Pong-Set2
Ping2-Set2
RoundTrip2
Reply2
RoundTrip1
Reply1
2
        DOC: 15-24-0436-00-04ab

## Slide 7: Ranging Measurement Report: Type-3, Mixed Sets
Device-A
Initiator
Device-B
Responder
2
Ping2-Set2
RoundTrip2
Reply2
Ping1-Set1
1
Pong-Set1
RoundTrip1
Reply1
1
        DOC: 15-24-0436-00-04ab

## Slide 8: We Have All Timing after 3 Ranging Reports
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
1
2
2
2
Ping1-Set2
Pong-Set1
Pong-Set2
Ping2-Set1
Ping2-Set2
All relative timing is known wrt Ping1-Set1
        DOC: 15-24-0436-00-04ab

## Slide 9: DS-TWR with 2 Pkts: Multiple Sets of RMARKERs
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
1
2
2
2
Ping1-Set2
Pong-Set1
Pong-Set2
Ping2-Set1
Ping2-Set2
Each set of RIF-RMARKERs include: Ping1, Pong, Ping2
Ping1-RMARKER from Initiator’s 1st RIF Region: RIF-1,…,7
Pong-RMARKER from Responder’s MMS packet
Ping2-RMARKER from Initiator’s 2nd RIF Region: RIF-2,…,8
2 Ping1-RMARKERs
from RIF Region 1
2 Ping2-RMARKERs
from RIF Region 2
        DOC: 15-24-0436-00-04ab

## Slide 10: Ranging Measurement Report: Type-1, Set#1
Device-A
Initiator
Device-B
Responder
1
1
RoundTrip1
Reply1
RoundTrip2
Reply2
1
Pong-Set1
Ping1-Set1
Ping2-Set1
        DOC: 15-24-0436-00-04ab

## Slide 11: Ranging Measurement Report: Type-2, Set#2
Device-A
Initiator
Device-B
Responder
2
2
RoundTrip1
Reply1
RoundTrip2
(negative)
Reply2 (negative)
2
Pong-Set2
Ping1-Set2
Ping2-Set2
        DOC: 15-24-0436-00-04ab

## Slide 12: Ranging Measurement Report: Type-3, Mixed Sets
Device-A
Initiator
Device-B
Responder
1
2
RoundTrip1
Reply2
1
Reply1
RoundTrip2
Pong-Set1
Ping1-Set1
Ping2-Set2
        DOC: 15-24-0436-00-04ab

## Slide 13: We Have All Timing after 3 Ranging Reports
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
1
2
2
2
Ping1-Set2
Pong-Set1
Pong-Set2
Ping2-Set1
Ping2-Set2
All relative timing is known wrt Ping1-Set1
        DOC: 15-24-0436-00-04ab

## Slide 14: 2 Sets of RMARKERs Give 8 ToF Values
Initiator Ping1 | Responder Pong | Initiator Ping2 | ToF Value | Comments
Set1 | Set1 | Set1 | ToF_111 | Computed with Type-1 report
Set1 | Set1 | Set2 | ToF_112 | Computed with Type-3 report
Set1 | Set2 | Set1 | ToF_121 | Computed with timing values derived from Type-1,2,3 reports
Set1 | Set2 | Set2 | ToF_122 | Computed with timing values derived from Type-1,2,3 reports
Set2 | Set1 | Set1 | ToF_211 | Computed with timing values derived from Type-1,2,3 reports
Set2 | Set1 | Set2 | ToF_212 | Computed with timing values derived from Type-1,2,3 reports
Set2 | Set2 | Set1 | ToF_221 | Computed with timing values derived from Type-1,2,3 reports
Set2 | Set2 | Set2 | ToF_222 | Computed with Type-2 report
RIF validation ensures attacker cannot reduce all these 8 ToF values!
Distance-Bounding is ensured by
        DOC: 15-24-0436-00-04ab

## Slide 15: Summary of Ranging Reports -1-
Each set of RIF-RMARKERs include: Ping1, Pong, Ping2
  Ping1-RMARKER from Initiator
    From 1st MMS packet for 3 packet DS-TWR
    From the1st RIF Region, e.g., RIFs: 1, 2, …, A, for 2 packet DS-TWR
  Pong-RMARKER from Responder’s MMS packet
  Ping2-RMARKER from Initiator
    From 2nd MMS packet for 3 packet DS-TWR
    From the 2nd RIF Region, e.g., RIFs: 2, 3, …, B, for 2 packet DS-TWR
Two important sets for 3 packet DS-TWR
  Set-Early: set of early RIF-RMARKERs
    Ping1: Earliest RIF-RMARKER in 1st MMS packet from Initiator
    Pong: Earliest RIF-RMARKER in the MMS packet from Responder
    Ping2: Earliest RIF-RMARKER in 2nd MMS packet from Initiator
  Set-Late: set of late RIF-RMARKERs
    Ping1: Latest RIF-RMARKER in 1st MMS packet from Initiator
    Pong: Latest RIF-RMARKER in the MMS packet from Responder
    Ping2: Latest RIF-RMARKER in 2nd MMS packet from Initiator
        DOC: 15-24-0436-00-04ab

## Slide 16: Summary of Ranging Reports -2-
Each set of RIF-RMARKERs include: Ping1, Pong, Ping2
  Ping1-RMARKER from Initiator
    From 1st MMS packet for 3 packet DS-TWR
    From the1st RIF Region, e.g., RIFs: 1, 2, …, A, for 2 packet DS-TWR
  Pong-RMARKER from Responder’s MMS packet
  Ping2-RMARKER from Initiator
    From 2nd MMS packet for 3 packet DS-TWR
    From the 2nd RIF Region, e.g., RIFs: 2, 3, …, B, for 2 packet DS-TWR
Two important sets for 2 packet DS-TWR
  Set-Early: set of early RIF-RMARKERs
    Ping1: Earliest RIF-RMARKER in 1st RIF region of the MMS packet from Initiator
    Pong: Earliest RIF-RMARKER in the MMS packet from Responder
    Ping2: Earliest RIF-RMARKER in 2nd RIF region of the MMS packet from Initiator
  Set-Late: set of late RIF-RMARKERs
    Ping1: Latest RIF-RMARKER in 1st RIF region of the MMS packet from Initiator
    Pong: Latest RIF-RMARKER in the MMS packet from Responder
    Ping2: Latest RIF-RMARKER in 2nd RIF region of the MMS packet from Initiator
        DOC: 15-24-0436-00-04ab

## Slide 17: Summary of Ranging Reports -3-
Type-1 ranging report
  Reply time & Round-trip time are wrt the Set-Early of RIF-RMARKERs
Type-2 ranging report
  Reply time & Round-trip time are wrt the Set-Late of RIF-RMARKERs
Type-3 ranging report
  Reply time & Round-trip time are wrt the RIF-RMARKERs mixed from Set-Early & Set-Late
    Ping1 & Pong from Set-Early
    Ping2 from Set-Late
Next, we discuss how to report these time values …
        DOC: 15-24-0436-00-04ab

## Slide 18: Part-2: Ranging Reports with RMI IE in 4me
        DOC: 15-24-0436-00-04ab

## Slide 19: Use 4me RMI IE for MMS DS-TWR
RMI IE
  Ranging Measurement Information IE (RMI IE)
    Used to send ranging-related measurements to one or more devices
    RMI List Length: specifies the # elements in RMI List
  RMI List
    Reply Time and Round-trip Time fields: unsigned integer with time unit: Tc/128 = 15.65 ps with Tc=1/499.2 us
    4 bytes allow a maximum value of (2^32-1)*15.65/10^9 = 67 ms
        DOC: 15-24-0436-00-04ab

## Slide 20: Use 4me RMI IE for MMS DS-TWR
RMI IE configuration for DS-TWR in the case of UWB MMS
  RMI List Length = 3
  RMI List
    #1 element
      Type 1 ranging report
    #2 element
      Type 2 ranging report
    #3 element
      Type 3 ranging report
        DOC: 15-24-0436-00-04ab

## Slide 21: Suggested Changes in 4ab
10.29 Ranging: Page 37, after line 19, add the following
10.29.8.4 Ranging Measurement Information IE (RMI IE)
Add the following texts at the end of clause 10.29.8.4:
When performing DS-TWR with UWB MMS as described in 10.38, to ensure ranging integrity, multiple RMI List elements will be carried in one RMI IE. Meanwhile, both the RX-to-TX Reply Time field and the TX-to-RX Round-trip Time field shall be interpreted as signed integers that can convey either positive or negative relative timing differences.
        DOC: 15-24-0436-00-04ab

## Slide 22: Suggested Changes in 4ab
When performing DS-TWR with UWB MMS, multiple sets of RIF-RMARKERs could be defined to ensure ranging integrity. Each RIF-RMARKER set includes Ping1-RMARKER from Initiator, Pong-RMARKER from Responder, and Ping2-RMARKER from Initiator.
For DS-TWR with 3 UWB MMS packets, the Ping1-RMARKER is from Initiator’s 1st MMS packet and the Ping2-RMARKER is from Initiator’s 2nd MMS packet.
For DS-TWR with 2 UWB MMS packets, the Ping1-RMARKER is from the 1st RIF Region within Initiator’s MMS packet and the Ping2-RMARKER from the 2nd RIF Region within Initiator’s MMS packet.
RIF-RMARKER Set-Early refers to the set consisting of earliest RIF-RMARKERs. RIF-RMARKER Set-Late refers to the set consisting of latest RIF-RMARKERs.
When reporting measurements with RMI IE in 10.29.8.4, RMI List element #1 reports RX-to-TX reply time and TX-to-RX Round-trip time with respect to RMARKERs in Set-Early. RMI List element #2 reports RX-to-TX reply time and TX-to-RX Round-trip time with respect to RMARKERs in Set-Late. RMI List element #3 reports RX-to-TX reply time and TX-to-RX Round-trip time with respect to Ping1-RMARKER and Pong-RMARKER from Set-Early and Ping2-RMARKER from Set-Late. In this case, both the RX-to-TX Reply Time field and the TX-to-RX Round-trip Time field in Figure 10-214 of 10.29.8.4 shall be interpreted as signed integers.
10.38.6 UWB MMS report phase: Page 70, after line 14, add the following
        DOC: 15-24-0436-00-04ab

## Slide 23: Part-3: Ranging Reports with Compact Frames in 4ab
        DOC: 15-24-0436-00-04ab

## Slide 24: Use Compact Frames for MMS DS-TWR
4ab Draft1
  7.3.7 Compact frame format
    Compact Frame ID
      Identifies what is carried by the compact frame
    Relevant ones defined in Draft1
      ID=5: One-to-one Initiator Report
        Clause 10.38.9.9
      ID=6: One-to-one Responder Report
        Clause 10.38.9.10
        DOC: 15-24-0436-00-04ab

## Slide 25: Use Compact Frames for MMS DS-TWR
4ab Draft1
  10.38.9.9 One-to-one Initiator Report Compact frame
  10.38.9.10 One-to-one Responder Report Compact frame
        DOC: 15-24-0436-00-04ab

## Slide 26: Suggested Changes in 4ab
10.38.9.9 One-to-one Initiator Report Compact frame
  Page 99, line 23, line 24, update the texts as follows
The Message Control field value is set to 0x00 for SS-TWR. When performing DS-TWR, this field is set to 0xAB for DS-TWR with 2 UWB MMS packets and set to 0xCD for DS-TWR with 3 UWB MMS packets.
The Message Content field shall be formatted as shown in Figure 80 for SS-TWR. When performing DS-TWR, this field shall be formatted as shown in Figure 80.1.
        DOC: 15-24-0436-00-04ab

## Slide 27: Suggested Changes in 4ab
10.38.9.9 One-to-one Initiator Report Compact frame
  Page 100, after line 2, add the following figure
Figure 80.1 Format of the Message Content field in the One-to-one Initiator Report Compact frame when Message Control field value is 0xAB or 0xCD
Octets: 5 | Octets: 5 | Octets: 5 | Octets: 5 | Octets: 5 | Octets: 5 | 0/variable
RX-to-TX Reply Time 1 | TX-to-RX Round-trip Time 1 | RX-to-TX Reply Time 2 | TX-to-RX Round-trip Time 2 | RX-to-TX Reply Time 3 | TX-to-RX Round-trip Time 3 | Passthrough
        DOC: 15-24-0436-00-04ab

## Slide 28: Suggested Changes in 4ab
10.38.9.9 One-to-one Initiator Report Compact frame
  Page 100, line 3,4,5, update the texts as follows
The Round-trip Time field value in Figure 80 is an unsigned integer that reports the time difference for SS-TWR, measured at the initiator, between the RMARKERs of the initiator’s MMS fragments and the responder’s MMS fragments. The units of time are specified in 10.29.1.4 (Ranging counter time unit).
The values of the RX-to-TX Reply Time field and the TX-to-RX Round-trip Time field in Figure 80.1 are signed integers that report the time differences for DS-TWR with the units of time specified in 10.29.1.4.
When performing DS-TWR with UWB MMS, multiple sets of RIF-RMARKERs are defined to ensure ranging integrity. Each RIF-RMARKER set includes Ping1-RMARKER from Initiator, Pong-RMARKER from Responder, and Ping2-RMARKER from Initiator. For DS-TWR with 3 UWB MMS packets, the Ping1-RMARKER is from Initiator’s 1st MMS packet and the Ping2-RMARKER is from Initiator’s 2nd MMS packet. For DS-TWR with 2 UWB MMS packets, the Ping1-RMARKER is from the 1st RIF Region within Initiator’s MMS packet and the Ping2-RMARKER from the 2nd RIF Region within Initiator’s MMS packet. RIF-RMARKER Set-Early refers to the set consisting of earliest RIF-RMARKERs. RIF-RMARKER Set-Late refers to the set consisting of latest RIF-RMARKERs.
When reporting measurements with the Message Content field in Figure 80.1 for DS-TWR, RX-to-TX reply time 1 and TX-to-RX Round-trip time 1 are with respect to RMARKERs in Set-Early. RX-to-TX reply time 2 and TX-to-RX Round-trip time 2 are with respect to RMARKERs in Set-Late. RX-to-TX reply time 3 and TX-to-RX Round-trip time 3 are with respect to Ping1-RMARKER and Pong-RMARKER from Set-Early and Ping2-RMARKER from Set-Late.
        DOC: 15-24-0436-00-04ab

## Slide 29: Suggested Changes in 4ab
10.38.9.10 One-to-one Responder Report Compact frame
  Page 100, line 12, update the texts as follows
The Message Control field value shall be either 0x00, 0x10, 0xAB, or 0xCD.
        DOC: 15-24-0436-00-04ab

## Slide 30: Suggested Changes in 4ab
10.38.9.10 One-to-one Responder Report Compact frame
  Page 101, after line 2, add the following figure
Figure 83.1 Format of the Message Content field in the One-to-one Responder Report Compact frame when Message Control field value is 0xAB or 0xCD
Octets: 5 | Octets: 5 | Octets: 5 | Octets: 5 | Octets: 5 | Octets: 5 | 0/variable
RX-to-TX Reply Time 1 | TX-to-RX Round-trip Time 1 | RX-to-TX Reply Time 2 | TX-to-RX Round-trip Time 2 | RX-to-TX Reply Time 3 | TX-to-RX Round-trip Time 3 | Passthrough
10.38.9.10 One-to-one Responder Report Compact frame
  Page 101, after line 2, add the following texts
When the Message Control field value is 0xAB or 0xCD, the Message Content field shall be formatted as shown in Figure 83.1. The field value of 0xAB indicates DS-TWR with 2 UWB MMS packets and the field value of 0xCD indicates DS-TWR with 3 UWB MMS packets.
        DOC: 15-24-0436-00-04ab

## Slide 31: Suggested Changes in 4ab
10.38.9.10 One-to-one Responder Report Compact frame
  Page 101, line 3,4,5, update the texts as follows
The Reply Time field value in Figure 82 is an unsigned integer reporting the time difference for SS-TWR, measured at the responder, between the RMARKERs of the MMS fragments received from the initiator and the MMS fragments transmitted by the responder. The units of time are specified in 10.29.1.4 (Ranging counter time unit).
The values of the RX-to-TX Reply Time field and the TX-to-RX Round-trip Time field in Figure 83.1 are signed integers that report the time differences for DS-TWR with the units of time specified in 10.29.1.4.
When performing DS-TWR with UWB MMS, multiple sets of RIF-RMARKERs are defined to ensure ranging integrity as described in 10.38.9.9. When reporting measurements with the Message Content field in Figure 83.1 for DS-TWR, RX-to-TX reply time 1 and TX-to-RX Round-trip time 1 are with respect to RMARKERs in Set-Early. RX-to-TX reply time 2 and TX-to-RX Round-trip time 2 are with respect to RMARKERs in Set-Late. RX-to-TX reply time 3 and TX-to-RX Round-trip time 3 are with respect to Ping1-RMARKER and Pong-RMARKER from Set-Early and Ping2-RMARKER from Set-Late.
        DOC: 15-24-0436-00-04ab

## Slide 32: Part-4: Backup Slides
        DOC: 15-24-0436-00-04ab

## Slide 33: DS-TWR Recap 1: Ping Pong Ping
        DOC: 15-24-0436-00-04ab

## Slide 34: DS-TWR Recap 2: Ping Ping Pong
Ping-Ping-Pong is equivalent to Ping-Pong-Ping when treating timing values as negative numbers!
        DOC: 15-24-0436-00-04ab

## Slide 35: DS-TWR Recap 3: Pong Ping Ping
Ping-Ping-Pong is equivalent to Pong-Ping-Ping when treating timing values as negative numbers!
        DOC: 15-24-0436-00-04ab

## Slide 36: DS-TWR with 3 Pkts: Multiple Sets of RMARKERs
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
1
2
2
2
Ping1-Set2
Pong-Set1
Pong-Set2
Ping2-Set1
Ping2-Set2
Each set of RIF-RMARKERs include: Ping1, Pong, Ping2
Ping1-RMARKER from Initiator’s 1st MMS packet
Pong-RMARKER from Responder’s MMS packet
Ping2-RMARKER from Initiator’s 2nd MMS packet
        DOC: 15-24-0436-00-04ab

## Slide 37: DS-TWR with 3 Pkts: Multiple Sets of RMARKERs
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
1
2
2
2
Ping1-Set2
Pong-Set1
Pong-Set2
Ping2-Set1
Ping2-Set2
        DOC: 15-24-0436-00-04ab

## Slide 38: DS-TWR with 2 Pkts: Multiple Sets of RMARKERs
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
1
2
2
2
Ping1-Set2
Pong-Set1
Pong-Set2
Ping2-Set1
Ping2-Set2
Each set of RIF-RMARKERs include: Ping1, Pong, Ping2
Ping1-RMARKER from Initiator’s 1st RIF Region: RIF-1,…,7
Pong-RMARKER from Responder’s MMS packet
Ping2-RMARKER from Initiator’s 2nd RIF Region: RIF-2,…,8
RIF Region 1
RIF Region 2
        DOC: 15-24-0436-00-04ab

## Slide 39: DS-TWR with 2 Pkts: Multiple Sets of RMARKERs
Ping1-Set1
Device-A
Initiator
Device-B
Responder
1
1
1
2
2
2
Ping1-Set2
Pong-Set1
Pong-Set2
Ping2-Set1
Ping2-Set2
RIF Region 1
RIF Region 2
        DOC: 15-24-0436-00-04ab