## Slide 1: September 2024 Doc.: IEEE 802.15.4
subumission
Silde 1
Authors:
A New Generation of Active RFID （LDSW）for IoT Application
Date: 2024-9-12

## Slide 2: September 2024 Doc. IEEE 802.15.4
subumission
Silde 2
Abstract
LDSW (low duty cycle smart wireless) will meet the chanllenges identified in the IEEE PAR document.
LDSW tag is for identification as well as for IoT applications. It can connect & control sensors, contollers, and location modules, while it is in a very low duty cycle working mode of periodical sleeping and waking up monitoring for identification purpose.
It can handle various IoT applications in a cost-effective way. This includes dealing with high volume end devices, no matter they are at fixed location or in fast moving state, with their IDs known or not.
Any LDSW device can initiate a communication at any time by continously and uninterruptedly transmitting wake-up signals to target devices in a period of time longer than the sleep & wake-up cycle of the target devices , to wake them up and set a communication just in 1 second.
Doing synchronization only at any needed time. This is different from periodical beacon synchronization. It cuts down power & increases flexibility

## Slide 3: September 2024 Doc. IEEE 802.15.4
subumission
Silde 3
Background
  The information revolution is moving from the Internet to the IoT.
  However, there is a big gap between market needs and the reality
World Needs a Good IoT Standard
to Meet the Gap

## Slide 4: September 2024 Doc. IEEE 802.15.4
subumission
Silde 4
Basic IoT Data Information
They are characterized by “light data”, “Bursty”, “Asynchronous”and Transitive”,
comletely different from the one dealed by 3GPP

## Slide 5: September 2024 Doc. IEEE 802.15.4
廖成都西谷数字技术有限公司
IoT technologies Current Available
IEEE 802.15.4 Series (including LoRaWAN and Bluetooth):
Primarily used for sensor data collection; limited improvements have been made in RFID functionalities. This standard is well-suited for low-data-rate applications such as sensor networks, but has limitations in high-density, dynamic RFID environments.
Active RFID: Mainly used for identification and location tracking. It excels in environments where active monitoring and real-time localization are required, such as tracking assets across large areas or within complex infrastructures.
RedCap：
Aims to streamline 3GPP protocols to better fit Internet of Things (IoT) requirements. However, because 3GPP was originally designed for high-bandwidth applications like audio and video transmission, it typically utilizes synchronous communication protocols. These protocols are not suitable for typical IoT application scenarios, which are characterized by light, bursty, asynchronous, and transient data. Therefore, it is challenging to directly apply these synchronous protocols to IoT data, which often requires minimal latency and overhead.
None of them can meet all the basic functionalities required by IoT

## Slide 6: September 2024 Doc. IEEE 802.15.4
subumission
Silde 6
IEEE is Looking for the Solution --An unified IoT standard as defined in the following PAR document-- zengjiade
  《802.15.4f Active RFID PAR Submittal from the RFID Study Group》
  –Ultra-low energy consumption (low duty cycle)
  –Low PHY transmitter power
  –Both one-way and two-way communications (simplex and duplex transmission)
  –High tag density (large tag population of many thousands)--
  -( Reading & Writing in fast moving high desity tags)--added
  –Reader to tag and tag to tag (meshing) communication (unicast)
  –One to many communication (multicast)
  -(On demands synchronization) --added
  -（Multi-channel collaboration）--added
  –Authentication
  –Sensor integration
  –Accurate location determination capability
  –100m read range - (need even longer range >1000m)--added
  –Global availability (with our without licensing)
  –Narrow bandwidth PHY channels less than 3MHz wide
  –Capable of avoiding, or operating in the presence of interference from other
  devices operating within the Active RFID’s frequency band of operation
But not succeed yet. Please refer to: 《https://grouper.ieee.org/groups/802/15/pub/SGrfid.html》

## Slide 7: September 2024 Doc. IEEE 802.15.4
subumission
Silde 7
Challenges for 802.15.4
It needs better working effeciency, faster data transimission、and capable of handling more devices and dealing with diferent scenarios at very low power,......
Test from Dash-7 organization

## Slide 8: September 2024 Doc. IEEE 802.15.4
subumission
Silde 8
LDSW
Following are the explainations
LDSW is designed specially for IoT applications
with new topology、function & technology

## Slide 9: September 2024 Doc. IEEE 802.15.4
subumission
Silde 9
Star-Net - Connecting to Broadband Net
With peer to peer communication & data relay
Gateway reader can have as many channels as needed, and
connects both wideband and Narrow-band protocols together. Either one works effeciently
LDSW Net could be either a public narrow-band Net work serving the public or a pravite Net work

## Slide 10: September 2024 Doc. IEEE 802.15.4
廖成都西谷数字技术有限公司
LDSW Topology Explaination
LDSW adopts a gateway reader that bridges two different communication protocols' , effectively bridging synchronous communication protocols (such as in 3GPP) with asynchronous communication protocols like LDSW. This solution addresses the needs of application scenarios that have two completely different data transmission requirements. This method allows each protocol to operate in its ideal environment rather than forcing a merger that would weaken their functionality. It is rational to maintain the independence of these protocols, allowing them to perform optimally on their own instead of attempting to merge them into a single solution.
Point-to-point data relay methods are only used in remote areas where broadband networks do not exist, forming a chain-like topology structure connected to broadband networks.
A public narrow band IoT network or a private one The LDSW system, rely on the existing broadband networks, can either be a public narrow band IoT network, providing a variety of IoT information services to governments, enterprises, and the public; or it can be a local IoT network connected to WIFI, serving enterprises and institutions themselves.
Identified by IPV6 in the network All LDSW terminals will be identified by their unique IPV6 identity numbers, and telecom operators will charge them a network usage fee based on their usage of their network.

## Slide 11: September 2024 Doc. IEEE 802.15.4
subumission
Silde 10
Peer to Peer Communication
LDSW devices can be in a very low duty cycle mode of periodical sleeping and monitoring. Anyone can initiate a communication by continously and uninterruptedly transmitting wake-up signals to the target devices, in a time period longer than the sleep & wake-up cycle of target devices waking them up and building a communication just in 1 second. See page 14
Data relay in the remote area without mobile net

## Slide 12: September 2024 Doc. IEEE 802.15.4
subumission
Silde 11
New Concept of Active RFID
LDSW tag connects & controls sensors, contollers, and location modules.
It can handle various IoT applications at very low power and cost, no matter with high volume tags number or not, tags with fixed location or in fast moving, with knowing tags’ ID or not, ......

## Slide 13: September 2024 Doc. IEEE 802.15.4
subumission
Silde 12
Wide Range of IoT Applications
..................

## Slide 14: September 2024 Doc. IEEE 802.15.4
subumission
Silde 13
Explainations will follow
Key Technological Breakthroughs
  “DNA Check” -- Similar to IEEE 802.15.4 CCA mode 2
  “Multi-Channel Collaboration”
  -More channels are available at the same time in the same system
  “On demands synchronization”-- Dynamic timing
  Tag Interfacing with sensors & controller,....
  Micro code commands --Save power & get more flexibility

## Slide 15: September 2024 Doc. IEEE 802.15.4
subumission
Silde 14
“DNA Check” Illustration
Reader initiates a communication with LDSW tag

## Slide 16: September 2024 Doc. IEEE 802.15.4
subumission
Silde 15
Advantages of “DNA Check”
Cutting down power drastically
-- Average <10 uAs -Ultr-low power
Long rang tags consumes more power only in transmitting --Low power long range Star Net
Increasing work reliability
--Guaranteed to receive a correct package --Reliable
Very useful for wireless remote control
--Fast response in just 1 second

## Slide 17: September 2024 Doc. IEEE 802.15.4
subumission
Silde 16
Multi-Channel Collaboration
Readers can have as many transceiver modules as needed

## Slide 18: September 2024 Doc. IEEE 802.15.4
subumission
Silde 17
Advantages of “Multi-channel Collaboration”
Simplified LDSW system
All tags can communicate each other
Can handle fast moving high density tags
Speed up whole communication process
Siplex tags can be used as “dulplex even multi-plex”

## Slide 19: September 2024 Doc. IEEE 802.15.4
subumission
Silde 18
Synchronization only needed
Different from periodical beacon synchronization
It cuts down power & increases flexibility

## Slide 20: September 2024 Doc. IEEE 802.15.4
subumission
Silde 19
ApplicationA：accurate indoor location
Taking advantages of multi-channel collaboration & dynamic timing, simple low cost tags can be used for tag location

## Slide 21: September 2024 Doc. IEEE 802.15.4
subumission
Silde 20
ApplicationB：accurate outdoor location
Sending a command to turn on GPS to get location information, and turn GPS off right after received location information will save a lot of power
LDSW tag + GPS module = LDSW satellite location tag

## Slide 22: September 2024 Doc. IEEE 802.15.4
subumission
Silde 21
Summary
* LDSW is a new generation of active RFID, meeting all the requirements
identified in the PAR document:
“IEEE 802.15.4f Active RFID PAR Submittal from the RFID Study Group”.
* A Chinese national key IoT standard based on LDSW technology
《 Technical Requirements for Low duty cycle smart IoT tag communication system 》
will be published soon.
* LDSW has been accepted by ISO as the technical basis for a new
proposed active RFID international standard to replace ISO-18000-4
at the meeting : ISO/IEC JTC 1/SC 31/WG 4/SG 3 - Air Interface, Meeting Minutes
14 September 2010 Toulouse, FRANCE

## Slide 23: September 2024 Doc. IEEE 802.15.4
subumission
Silde 22
Thank You !

## Slide 24: September 2024 Doc. IEEE 802.15.4
subumission
Silde 22
Some sample applycations