## Slide 1: Results of the ThoR Project
Tetsuya Kawanishi
Waseda Univ.

## Slide 2
DISCLAIMER
The use of any particular/specific brands of components, equipment, or instruments as a part of the demonstration and presentation does not constitute an endorsement of those brands by IEEE, IEEE SA, or the IEEE LMSC.

## Slide 3: Overviews of ThoR Project
ThoR:TeraHertz end-to-end wireless systems supporting ultra high data Rate applications
A joint EU-Japan project to provide technical solutions for the data networks beyond 5G based on 300 GHz RF wireless links.
EC Coordinator: Prof. Thomas Kürner, TUBS
Japan Coordinator: Prof. Tetsuya Kawanishi, Waseda University
Start date: 01-Jul-2018
End date: 30-Jun-2022
Project cost: 1,498,879 EUR + 185,915,477 JPY

## Slide 4: ThoR Consortium
EU partners funded by the EC in Horizon 2020
TU Braunschweig (EC Coordinator), Germany
Deutsche Telekom, Germany
Fraunhofer IAF, Germany
Siklu Communications, Israel
University of Lille, France
University of Stuttgart, Germany
Vivid Components, UK
Japanese partners funded by NICT, Japan
Waseda University (Japanese Coordinator)
Chiba Institute of Technology
Gifu University
NEC Corporation
HRCP R&D Partnership

## Slide 5: ThoR approach: Demonstrating the Capability of 300 GHz Backhaul/ Fronthaul links
Photonic LO

## Slide 6: Networking Interface and Baseband Modem
In the ThoR hardware demonstrator two types of modems have been used:
  FDD modems
    oeprating at 70/80 GHz
    Up to for 4 2x2 GHz channels are aggregated
  TDD modems
    operating at 60 GHz and at a bandwidth of 2.16 GHz
    used to demonstrate, that IEEE Std 802.15.3e with an extension of the IFS value is working for backhaul applications
Source: ThoR Deliverable D3.5 available at https://thorproject.eu/results/deliverables/.Testing "Report of 60 GHz TRX Module"
The ThoR demonstrator uses a super-heterodyne concept where the RF signal of modems oeprating at 60 GHz and 70/80 GHz, respectively are used as the IF signal for the subsequent 300 GHz RF Front-end

## Slide 7: Concept of demonstration system using V-band modem
V Band
Input
Port2
2
：
1
combine
r
V Band
Input
Port1
1:2 splitter
V Band
Output
Port2
V Band
Output
Port1
802.15.3e 60GHz Wireless
Module
(60GHz RF, BB, MAC & IF)
TRX Signal Path 1
802.15.3e 60GHz Wireless
Module
(60GHz RF, BB, MAC & IF)
TRX Signal Path 2
300GHz Input
300GHz Out
TDD TRX1
TDD TRX2
CH2
CH3
30dB VAT
10GbE
LO
240.84GHz
LO
240.84GHz
V-band Modem
Up converter
Down converter
User data
PHY
Data link
LLC sublayer
MAC sublayer
PLCP sublayer
PMD sublayer
OSI Reference model
Almost common between 15.3d/e
Example of THz transceiver with V-band modems
Source: K. Kondou: “Development of the ThoR 60 GHz transceiver module” ThoR Final Workshop https://thorproject.eu/events/thor-final-workshop-and-demo/

## Slide 8: Examples of ThoR outcomes
Near-field measurements and antenna characterisation by Gifu University
300 GHz front end development by Fraunhofer IAF and Univ. Stuttgart
Development of a high power TWTA by NEC
Development of E-band modems by Siklu
Development of V-band modems by HRCP
Analysis of requirements for wireless transport links by Deutsche Telekom
Measurement of 300 GHz band high-gain antennas by CIT
E-band photonic LO development by University of Lille
Automatic planning algorithms for THz comms by TU Braunschweig
300 GHz link design and interference study by Waseda University

## Slide 9: Post ThoR Project
Japan Coordinator: Prof. Shintaro Hisatake, Gifu University
Project cost: 125M JPY
Project period: 2021-2023 (JPN fiscal year)
TDD-based transceiver

## Slide 10
RF output: 286.2GHz and 288.36GHz
Flexible waveguides (FWS)
TDD signals are converted into transmission and receiving signals through duplexers.

## Slide 11
300GHz outdoor units (ODUs)
ODU1
ODU2

## Slide 12: RSSI under snow condition
February 5th, 2024

## Slide 13: Link degradation due to weather condition
Gas attenuation
Rain drop attenuation
Antenna tilt due to wind

## Slide 14: Antenna tilt due to wind
With some margin
APT/AWG/REP-81
99.99%: 15m/s
0.4deg (20m/s)

## Slide 15: Example of 300GHz fixed wireless system
Transmission distance | 500 m
Bandwidth | 10 GHz
Radiation power | 10 mW
Antenna gain | 48.1 dBi
Antenna diameter | 104.7 mm
Roll off | 0.25
Bitrate | 16 Gb/s
Availability rate | 99.99%
Tolerable rain rate | 50 mm/h
Tolerable wind speed | 20 m/s
Transmission distance | 500 m
Bandwidth | 10 GHz
Radiation power | 10 mW
 | 48.1 dBi
Antenna diameter | 104.7 mm
Roll off | 0.25
Bitrate | 16 Gb/s
Availability rate | 99.99%
Tolerable rain rate | 50 mm/h
Tolerable wind speed | 20 m/s

## Slide 16: Conclusion
300 GHz outdoor transceivers have been developed for high-speed point-to-point fixed wireless links.
IEEE802.15.3e compliant 60 GHz transceivers are used as baseband and IF units.
Long-term transmission experiments under various weather conditions are underway.