## Slide 1
Terahertz Wireless Technology for Beyond 5G ~Ultra narrow spot wireless service & IEEE802.15.3d Test Environment ~
THz wireless technology, whose frequency bands are from 100GHz to 300GHz, will open a new huge market with its extreme throughput. However, users need to adapt to the “Ultra-narrow-spot” caused by its propagation characteristics.
Manufacturing the SoC for the THz wireless standard, IEEE 802.15.3d, is key to addressing the issue. This allows for (1) ultra-instantaneous link establishment, enabling data transmission to begin immediately as the device enters the coverage area, and (2) ultra-high-speed wireless data transmission over 100 Gbps. These capabilities enable the exchange of a huge amount of data in much less than a second.
Background
Features
Parameter | Value
Carrier Frequency Center | 60.48 GHz or 62.64 GHz
Bandwidth | 2.16 GHz
Data Rate | Up to 6 Gbps
Transmission Distance | cm to hundreds of meters
Link Establishment Time | < 2 ms
Supported Standards | IEEE 802.15.3e, TransferJet X
RF Connection Interface | WG-15 UG-385/U
Supported Interfaces | USB, 10 Gigabit Ethernet
Local Storage | > 256 GB (Module-mounted using UFS)
(1) Development of IEEE802.15.3e system (60GHz band) implementing ultra-short time link establishment protocol technology and promotion of experiments on mobile equipment
(2) Ultra-high-speed data transfer technology using ultra-wideband frequenciesPlans to construct an IEEE802.15.3d evaluation environment in which the IEEE802.15.3e system (60 GHz band) is frequency-converted to the 300 GHz band
Utilizing the 30 GHz to 100 GHz millimeter-wave band,
achieving effective data rates of several tens of Gbps
(IEEE 802.15.3e compliant systems).
Utilizing the 100 GHz to terahertz range,
achieving effective data rates from several tens of Gbps to over 100 Gbps
(IEEE 802.15.3d compliant systems).
95 mm
63 mm
Main specifications of IEEE802.15.3e compliant ultra-short time link established wireless module
(Cooperation: HRCP)
Terahertz Wireless Technology for Beyond 5G ~Ultra narrow spot wireless service & IEEE802.15.3d/e Hybrid Test Environment ~
DISCLAIMER
The use of any particular/specific brands of components, equipment, or instruments as a part of the demonstration and presentation does not constitute an endorsement of those brands by IEEE, IEEE SA, or the IEEE LMSC.
The recorded data was converted by the mmw transceiver into a modulated signal in the mmW band of the IEEE802.15.3e standard (CH2).
The modulated signals was up-converted to the THz-wave band of the IEEE802.15.3d standard (CH9) by THz CMOS TX.
The received signal was down-converted to a IEEE802.15.3e standard signal by THz CMOS RX, demodulated by the mmW transceiver, and output as a video data.
Control signals for sending and receiving video signals are performed between mmW transceivers.
Since the radio license is not yet obtained, THz propagation will be demonstrated using waveguide attenuators with 60 dB insertion loss.
Overview of the system
The center frequency of THz and mmW communications were 271.08 GHz (3d, ch9) GHz and 60.48 GHz (3e, ch2), respectively.
The symbol rate and data rate were 1.76 GHz and 3.52 Gbps, respectively.
Specifications
This work was supported in part by the Ministry of Internal Affairs and Communications of Japan (JPJ000254, Research and Development for Expansion of Radio Wave Resources)
mmW
transceiver
(Transfer Jet X)
Down link (271.08GHz)
THz-wave transmitter
THz-wave receiver
~2.0m
mmW transceiver
mmW transceiver
Recording!
Playback!!
Down link (271.08GHz)
Up link (60.48GHz)
In an anechoic chamber
Up link (60.48GHz)
THz-wave receiver
Synthesizer
x6
THz CMOS TX
LNA
ANT
mmW transceiver
mmW
transceiver
(Transfer Jet X)
ANT
ANT
CIR
CIR
ANT
THz CMOS RX
IC
multiplier
x6
BPF
Synthesizer
WG
LNA
BPF
11.7GHz
70.2GHz
60.48GHz
x2
271.08GHz
LO
IF
THz-wave receiver
f GHz
Ch2
IEEE 803.15.3e
57.24
BW(GHz)
2.16
59
60
61
62
63
64
58
57
65
66
65.88
THz + mmW
Hybrid !!
RF
RF
ANT
THz CMOS TX
mmW transceiver
AMP
AMP
BPF
x6
Synthesizer
THz-wave transmitter
ANT
THz CMOS TX
IC
multiplier
x6
BPF
Synthesizer
WG
AMP
BPF
11.7GHz
70.2GHz
60.48GHz
x2
271.08GHz
LO
IF
AMP
THz-wave transmitter
f GHz
252.72
BW(GHz)
2.16
8.64
12.96
17.28
270
280
290
300
310
320
260
250
321.84
Ch1~32
Ch49~56
Ch57~61
Ch62~63
Ch9
IEEE 803.15.3d
THz-wave transmitter
(in case)
THz-wave receiver
(in case)
60dB ATT
mmW transceivers
Demonstration setup (@IEEE 802 Wireless Interim, Jan 15, 2025)
S. Beppu, et al., EuMIC2024
Demonstration of THz wave (3d) + MMW (3e) Hybrid Wireless Communication System
Overview of the system
January 2025
        doc.: IEEE 802.15-25-0057-00-wng0