## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Possible Next Steps on NB Channel Access (CID 988)
Source: Carlos Aldana (Meta)
Address : [1 Hacker Way, Menlo Park, CA 94025]
E-Mail: [caldana (at) meta.com]
Re: Study Group 4ab: UWB Next Generation
Abstract: [This provides slides to aid discussion towards convergence on CID 988 resolution]
Purpose: [For information]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2: Summary of 15-24-407-07-4ab
Propose to use single CCA before every NB transmission

## Slide 3: Background
There were concerns with the 15-24-407 document that included:
Alex (Apple)
  EDT is too low for 14 dBm in 6 GHz
  In 15-24-407-07, we allow the ED threshold to be set to the value required by local regulations
Riku (NXP)
  Can we use Short Control Signaling (SCS) clause in ETSI that allows no-LBT for management and control frames?
    Example of Control frames in ETSI EN 303687 v1.1.6 (2024-12) : Ack and Block Ack
    The Report frames are clearly data frames and would not be allowed under SCS exception
    The SCS allowance for no-LBT could be removed in future ETSI BRAN meetings.

## Slide 4: Latest in ETSI BRAN
5% duty cycle no-LBT (BRAN(24)125012) is not accepted
2. eDAA proposed by Apple (BRAN(25)128007) is not accepted
3. Low Duty Cycle no-LBT proposed by NXP (BRAN(25)128008r1) is not accepted
4. Accepted Minutes (BRAN(25)128016r1) of ETSI BRAN #127 show that LBT-based channel access proposal in BRAN(24)124017r3 is accepted
  It is the only accepted NB channel access mechanism that allows for any kind of frames (e.g., data frames) to be TX.

## Slide 5: FCC
FCC mandates Contention Based Protocol (CBP) in FCC 15.407(d.6) (see Appendix)
  Part 15, Subpart E, Section 15.403
2. FCC website points to guides for obtaining certification
  only KDB 987594 is listed

## Slide 6: KDB 987594 details

## Slide 7: KDB 987594 details
NO SCS allowed in FCC
The NB device is centered at the same frequency as incumbent

## Slide 8: Summary of Previous Discussion
6 Options discussed at the last meeting:
Accept 15-24-407-07-4ab as is to resolve CID 988 and other coex related CIDs: 204, 275, 276, 967, 996, 977, 978, 979, 1356, 1358, 1359, 150, 94, 12, 13
  Consistent with both FCC and ETSI.
2 . Consider a second LBT within 50us (on another NB channel) if CCA is busy (Menzo)
  Consistent with FCC & ETSI and an improvement on 1. above
3. If Tx duty cycle < Y%, EDT is fixed at -75 dBm/MHz (regardless of Tx Power) else follow EDT in Slide 2
LBT as specified in 15-24-407-07-4ab doc is mandatory for NB operation in Section 10.38.7.3 (NBA UWB MMS) and 10.43.2 (UWB data offload to NB) except for device with Tx duty cycle less than X%.
If DC> 1/15%, then NB use frequency hopping over more than 15 channels to spread the interference over the full spectrum (Mickael)
  Similar to NXP proposal at ETSI, which allows for 6% duty cycle over 480 MHz, which was not accepted.
LBT mandatory for NB operation in Section 10.38.7.3 (NBA UWB MMS) and 10.43.2 (UWB data offload to NB) except for device with Tx duty cycle less than X% (Bin Tian)

## Slide 9: Discussion
802.15.4ab needs to define a mandatory LBT mechanism with additional considerations:
Energy detection threshold (one value or dynamic) (15-24-407-07)
Single CCA or allow for second CCA on another channel within 50us (15-25-99-00)
Other
  < 5% Duty-cycle?

## Slide 10: Appendix

## Slide 11: CBP FCC Test Example

## Slide 12: Incumbent Signal
Flat spectrum for ~ 10 MHz

## Slide 13: Another CBP FCC Test Example
NB device with FCC ID BCG-A3048 [link]

## Slide 14: AWGN waveform
It has flat spectrum for ~ 9 MHz

## Slide 15: Aggregate Duty cycle for no-LBT
The plot below shows the aggregate duty cycle when N NB pairs are near a 802.11 link.
We see that 2 / 3 NB nearby pairs using 125 MHz causes ~10% aggregate NB duty cycle on 80/40 MHz 802.11
We see that 2 / 3 / 6 NB nearby pairs using 480 MHz causes ~10% aggregate NB duty cycle on 320/160/80 MHz 802.11