## Slide 1
  OmniRAN – 3GPP SaMOG
Document Number:
  IEEE 802.16-12-0660-00-Shet
Date Submitted:
  2012-11-10
Source:
  Antonio de la Oliva
  Carlos Jesus Bernardos
  (UC3M)
  Ivano Guardini
  Loris Marchetti
  (Telecom Italia)
Re:
Use Case for OmniRAN
Base Contribution:
  None.
Purpose:
  Describe potential use of OmniRAN in the 3GPP SaMOG context . This document is for discussion
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Copyright Policy:
The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: OMNIRAN-3GPP SaMOG
Antonio de la Oliva (UC3M)
Ivano Guardini (Telecom Italia)
Carlos J. Bernardos (UC3M)
Loris Marchetti (Telecom Italia)

## Slide 3: 3GPP SaMOG
3GPP defines how to connect a Trusted Non-3GPP network to the Evolved Packet Core (EPC)
  Current mechanisms being defined in the S2a Mobility Based on GTP & WLAN access to EPC (SaMOG)
This presentation aims at explaining current approaches and possible functionalities to be addressed in OMNIRAN

## Slide 4: 3GPP SaMOG, What is it?
SaMOG is defining how to connect the Gateway controlling the Trusted Non-3GPP network (WLAN) and the EPC
This is done through the S2a reference point, currently implemented by extending GTP/PMIP tunnels from PGW to Trusted WLAN Access GW (TWAG)

## Slide 5: Trusted Non-3GPP Network
3GPP does not define what is it, neither its internal mechanisms
Common understanding:
  Connection beetween UE and TGW is a L2 transport
  UE sees the TWAG as the AR
  This L2 transport can be implemented through several mechanisms (e.g., VPN, VLAN)

## Slide 6: Limitations of SaMOG R11
The key requirement of R11 SaMOG is to keep standard 802.11 UEs unmodified
Hence several limitations arise:
  Lack of IP address preservation (no IP mobility)
  Terminal cannot indicate an APN when connecting to the WLAN (the terminal is connected to default APN pre-configured on the TWAG or in the service profile on AAA/HSS)
  Terminal cannot establish multiple connections to multiple PDNs
  Terminal cannot access simultaneously resources in the WLAN and the EPC

## Slide 7: Trusted Non-3GPP network features out of 3GPP control
In order to use the Non-3GPP access as efficiently as possible there are several functionalities which are out of scope from 3GPP:
  L2/L3 triggers: Link Up/Down, L3 Attach/Dettach
  Connection control
  Resource management: Resource allocation/modification/release
  Policy enforcement functions
  Security functions

## Slide 8: Features potentially provided by OMNIRAN
In a nutshell, OMNIRAN can define how the Trusted Non-3GPP Network behaves up to the TWAG
Need to define how to perform the L2 transport (VLANs, tunneling, e.g. SoftGRE)
Extra features required for SaMOG R12:
  handover indication to enable IP address preservation
  transport of the APN
  extension of the L2 transport to the TWAG to support simultaneous access to multiple PDNs

## Slide 9: SaMOG R12
In R12, there is no more a constraint regarding modifications to the terminal
  IP address preservation for a single PDN connection
  Multiple PDN connections support over WLAN/S2a
  Concurrent support of NSWO and PDN connections
  Attach to non-default APN
Notes: Non Seamless WLAN Offload

## Slide 10: SaMOG R12 and OMNIRAN
The extra functionalities required by R12 SaMOG can also take advantage of the OMNIRAN interface
Missing functionalities:
  Logical interface at the UE, data and control
    Support for the allocation of the same IP address on different physical interfaces on the UE (e.g. 3GPP and 802.11)
  Information transfer between UE and network
    APN, handover indication
  Extension of the L2 transport to the TWAG to support simultaneous access to multiple PDNs.
Notes:   Independent bearer per APN
    L2 isolated link
    Point to point links as PMIP rules

## Slide 11: Summary
Work at the 3GPP SaMOG groups and OMNIRAN can be complementary
  OMNIRAN would need to define how the Trusted Non-3GPP network behaves according to requirements from 3GPP
  Work can be done for both network and terminal sides
  The use of OMNIRAN can open the door to the use of more IEEE 802 technologies as part of the operator´s RAN in a managed way