## Slide 1
  Considerations for Wireless SCB
Document Number:
  IEEE 802.16-13-0004-00-000r
Date Submitted:
  2013-01-09
Source:
  Yung-Han Chen, Jiann-Ching Guey, Jen-Shun Yang, Ching-Tarng Hsieh, ITRI .
Re:
Call for Contributions: IEEE Std 802.16 Amendment for Small Cell Backhaul (SCB) Applications (IEEE 802.16-12-0678-02-Gdoc)
Base Contribution:
  None.
Purpose:
  Deployment contributions of wireless small cell backhaul for discussion
Notice:
  This document does not represent the agreed views of the IEEE 802.16 Working Group or any of its subgroups. It represents only the views of the participants listed in the “Source(s)” field above. It is offered as a basis for discussion. It is not binding on the contributor(s), who reserve(s) the right to add, amend or withdraw material contained herein.
Copyright Policy:
The contributor is familiar with the IEEE-SA Copyright Policy <http://standards.ieee.org/IPR/copyrightpolicy.html>
Patent Policy:
  The contributor is familiar with the IEEE-SA Patent Policy and Procedures:
      <http://standards.ieee.org/guides/bylaws/sect6-7.html#6> and <http://standards.ieee.org/guides/opman/sect6.html#6.3>.
  Further information is located at <http://standards.ieee.org/board/pat/pat-material.html> and <http://standards.ieee.org/board/pat >.

## Slide 2: SCB Deployment Considerations
Factors to consider in different deployment scenarios
  Carrier frequency
    Identify potential frequency bands below 6GHz
    Propagation characteristics of identified bands
  Range/coverage area
  Indoor/outdoor; antenna elevation
Step1: Initial assessment of system performance for each scenario
  Channel statistics/characteristics
  Per link peak rate
  System throughput
Step 2: Requirement
  Antenna configuration
  Transmission technology
  Receiver technology
Iterate a few times between step 1 and step 2
backhaul band
access band
backhaul band
access band
vs
System throughput should match total traffic generated by all access nodes

## Slide 3: P2MP GPON Design Reference
A (very challenging) design reference for point to multi-point wireless backhaul
2.488 Gbps downstream 1.244 Gbps upstream
  Aggregated at Optical Line Terminal (OLT)
  Shared in time by 8, 16, 32 or 64 Optical Network Terminals (ONT) act to be Feeder Nodes
Metro
1
2
n
1
2
n
1
2
n
1
2
1
2
1
2
Upstream (US)
- TDMA
Downstream (DS)
- TDM
ONT #1
ONT #2
ONT #n
1:N split
(N=8,16,32,64)
Remote
Node (RN)
Drop
Feeder
(Trunk)
OLT
1
:
N
Feeder Node 1
Feeder Node 2
Small Cells
Small Cells
Replaced by
IEEE 802.16
GPON reference architecture

## Slide 4: Considerations of Capacity Requirements
Use cases
  Point-to-point
  Point-to-multiple-point
    What is the max. number of multiple points the standard can support?
Min. and Max. DL/UL throughout per link
  TDD DL & UL symmetric or asymmetric?
  As a backhaul application, should it guarantee Min. bandwidth and Max. latency?
Example
  Max. DL/UL throughput per link: 10Mbps/10Mbps
    Depends on operational requirements such as coverage and services
  Max. number of multiple points: 4
    A master feeder needs to handle 4 slaves’ DL/UL links, so the total throughput required by the master feeder is no less than 40Mbps/40Mbps
  Configure PHY/MAC profiles of the master feeder to support the required total throughput
    Bandwidth to use
    MCS
    Number of streams (MIMO)
    BW request and QoS strategies
    Others…

## Slide 5: Issues of Multiple Hops
Issue 1: based on the existed IEEE 802.16 TDD architecture, a middle hop should support Tx and Rx simultaneously
  For example, if Site B is a client of Site A, and Site C is a client of Site B, then Site B needs to enable Tx mode (UL to Site A) and Rx mode (UL from Site C)
Issue 2: the site that is closer to the feeder might be the bottleneck
  For example, Site A (closer to the feeder) needs to handle the traffic of Site A, Site B and Site C
Issue3: more hops, longer latency
  For example, Site C will suffer longer latency
The frame structure of protocol might be re-defined to solve these issues.
Bottleneck
Latency
Small cell BS
Small cell BS
Small cell BS
Site A
Site B
Site C