## Slide 1: Geolocation for cognitive access
William Webb/Andy Gowans
July 2010

## Slide 2: Overview
Where we are in the UK
Update on location technologies work that we have recently completed
Next steps towards implementation

## Slide 3: Sensing likely not to be viable
Cognitive / white space devices started out assuming sensing would be used to determine free channels
During 2008 and 2009 the FCC and Ofcom separately evaluated the appropriate sensing parameters needed to offer a high level of protection to licence holders
  FCC work predominantly based on lab trials (-114dBm)
  Ofcom work based on modelling backed up by measurement (-126dBm)
Similar results achieved by both UK and ECC
  Ofcom derived slightly lower sensing thresholds than the FCC
  SE43 have come up with similar results to Ofcom
FCC concluded that sensing alone was not yet proven and that geolocation needed to be used as well
  But noted they would test any device that claimed to be able to work by sensing alone
Ofcom published a statement on cognitive devices using sensing with associated parameters
  But put publication of the any UK legislation on hold until demand materialised
  Industry told us that building consumer devices able to meet these levels not viable
SE43 work on-going still looking at issues around geolocation, sensing and beacons.

## Slide 4: The focus turned to geo-location
We issued a discussion document asking:
  What information should devices supply to the database?
  What information should the database return?
  How will the database be populated?
  Which organisations should be responsible for populating, hosting, managing and validating the database?
For the most part there was reasonable consensus and constructive input over all of these areas
The FCC has put out a call for a database supplier and is currently evaluating responses
ECC (SE43 etc.) work on-going but may influence future UK decisions
Standards bodies looking at writing suitable standards (IEEE 802 etc.)
No ETSI group has as yet started working on suitable HS for TVWS devices.

## Slide 5: There is still much uncertainty as to how the industry structure will work out
Not clear who would set up the database nor how any funding requirements would be met
Unclear if standards being developed will actually result on products in the marketplace.
Unclear whether a national, regional or global structure will appear or whether multi-country standardisation will be needed
Hence, our preference is not to be too prescriptive at this stage but to be prepared to intervene if needed
  Allow any number of databases
  Allow closed and open databases
  Consider funding issues if they arise

## Slide 6: Overview
Where we are in the UK
Update on location technologies work that we have recently completed
Next steps towards implementation

## Slide 7: White space devices
Protecting TV viewers
  Have presented to SE43 an example of possible methodology using DTT receive level predictions from UK planning tools for broadcasting.
  100 x 100m pixels used
  See ECC PTSE43 paper no SE43(10)94
80 km
Figure: BT Research
Notes: Boundaries only defined and only known to a km or so, so 100m accuracy adequate
Even small features of the order of a few km (small bar = 4km)
AND
Away from boundaries channels to be protected won’t change (channels in adjacent areas usable well inside boundary). So large area around transmitter sites where poor accuracy (few kms) will be ok.

## Slide 8: White space devices
Protecting PMSE users
Operational area
Exclusion zone
Separation distance
separation distance ~ 1km
accuracy needed ~ 40m (67%)
Notes: Report showed examples where CEP-67 of better than 100m would be required.

## Slide 9: White space devices
Operational area
Exclusion zone
Separation distance
Protecting PMSE users – is high accuracy important?
  Reduce accuracy to 100m instead of 40m
  Increases size of exclusion area from 1 sq.km to 1.2 sq.km
  Applies at most to ~3000 PMSE locations & only when GPS not available
  Reduction in availability of white space spectrum likely very small
separation distance ~ 1.1km
Notes: “Reduction” in white space needs weighting by demand/population
NB Knowing WSD is indoors / outdoors could be useful in terms of knowing that building loss applies and exclusion area can be minimised.

## Slide 10: White space devices – location summary
Objective – to identify key requirements
    Based on user expectations & regulatory requirements
Where and when is accuracy important?
    Protecting TV viewers – 100m but can be much poorer in some places
    Protecting PMSE users - <100m in some situations
    But does it really matter? Possibly not.
Reliability & Integrity
    Need large errors to be rare
    Important in ensuring low probability of interference
Height
    Would allow smaller exclusion areas or greater WSD transmit power
    But height information is less easily obtained

## Slide 11: Conclusions – Location technologies (1 of 2)
No one location technology solution fits all applications
Future GNSS developments over the next ten years will not solve the indoor positioning problem, although a greater satellite density will help today’s marginal cases, plus the deployment of GPS beacons would create location hotspots indoors
If we had ‘position roaming’ amongst the UK cellular networks, then the potential for cellular location not-spots would be reduced. If all cellular location devices monitored all networks then Cell-ID alone could be made more accurate from a fingerprint of which Cell-IDs were visible at any given location
Combination solutions will be increasingly important, such as with GPS, Wi-Fi, RFID, sensor networks, UWB etc. Higher accuracy ‘location hotspots’ could thus be created;

## Slide 12: Conclusions – Location technologies (1 of 2)
A combination of positioning technologies will enable location in many more environments, but the differing levels of trustworthiness of the location reports from different sources may be harder to establish
Information on accuracy at high confidence levels is lacking for consumer positioning systems
Information on accuracy for consumer positioning system is often given for a standard operating environment. More information is needed on the performance of positioning systems in more challenging, real world environments
Consumer devices are unable to report accuracy in real time, as they move between different operating environments. To increase the trustworthiness of these reports, user level integrity monitoring schemes are needed. Such schemes may check consistency across multiple positioning technologies and/or inertial sensors.

## Slide 13: Conclusions for WSDs
A WSD should not cause interference to licensed users, thus where a WSD position fix is unreliable it should fail safe
WSD location accuracy can be traded against the size of the exclusion zone around a licensed user
Height information would benefit WSDs although its omission results in only a small penalty. However, it is only via the omission of the height requirement that a good match with any location technology is possible
GSM and broadcast based location technologies were best matched to WSDs
Cell-ID is widely deployed in the UK today, but other cellular and broadcast location techniques are not yet deployed. This means that Cell-ID is presently the best matched location technology for WSD applications, although its accuracy is lower than required for best efficiency in some scenarios.

## Slide 14: Our view on where this leaves us
We do not need to set a particular locational accuracy – if devices respond with their predicted accuracy at, eg 95% certainty, then the database can set the exclusion levels accordingly
Devices are likely to use a range of location technologies depending on their location and specification and hence flexibility will be important
Locational accuracy will need to be derived from the type of technology used plus additional information (such as the number of satellites visible) likely coupled to a “look-up table”
There is generally insufficient information currently available to populate such a look-up table especially at certainty levels >67%
  Cognitive community (and/or regulators) needs to undertake necessary research

## Slide 15: Overview
Where we are in the UK
Update on location technologies work that we have recently completed
Next steps towards implementation

## Slide 16: National versus International issues
Usage varies across many European countries
  Degree of protection for DTV (eg indoors / outdoors)
  Whether PMSE usage is registered
Regulators likely to have a different bias between protection of incumbents and facilitation of innovative new services
Usage models for cognitive may differ
  Rural broadband may be more important in some countries
  Degree of eg WiFi coverage differs
Need a framework that allows the same device to be used throughout Europe (and ideally the world) enabling roaming, economies of scale, etc
Need to optimise the balance between harmonisation and ability to tailor to national circumstances

## Slide 17: The UK viewpoint
Harmonise
Database addresses (so a device knows who to contact)
Format of information sent from the device
Format of information received by the device
Leave to national regulators
Means of populating the database
Number of databases, ownership, geographical extent
Parameters used to populate database
  Propagation models
  Building penetration losses
  Required C/I ratios for devices
  Required locational accuracy and use of that information
Everything else!

## Slide 18
What elements do we think you need to harmonise in WSD standards?
Database addresses (so a device knows what to contact)
  Regulator may provide a link to approved database(s)
  No information at this point. Depends upon the database providers chosen.
  Possibly a method of authentication between the device and database.
Format of information to be sent from the device
  Device identifier (manufacturer and model number)
  Location and location accuracy.
  Type of Device has been suggested also (e.g. fixed, mobile, master, slave etc.)
  Device height (if available or relevant)
Format of information received by the device
  In band power levels (if not assumed or set at a nominal maximum by the regulator)
  Out of band power level (if not assumed or set at a nominal maximum by the regulator)
  Channel number(s) or Frequency(s) available.
  Whether sensing of incumbents is also required as additional requirement or not.
  Period before next database contact.

## Slide 19
5
6
2
3
4
1
Ofcom list of databases
PMSE usage database
DTT coverage database
Geolocation database (3rd party)
Slave
Master
Provided by Ofcom or associated party

## Slide 20: We need to issue a Statutory Instrument to enable access
We need to write an SI that exempts geo-location devices from licensing
  This will be novel and will require some careful thought
Need powers that enable us to “police” databases to ensure their correctness and to be able to shut them down if necessary
  Still examining whether we have legal powers to do this
Aiming to consult on possible forms for these in the coming months (resources permitting!)
If the consultation goes well we could move to issue the SI perhaps before the end of 2010
  But there could be many factors that lead to a delay
European Harmonised Standards activity for eg information exchange would make it simpler to set up and manage WSD in a stable regulatory environment.