## Slide 1: Update on European/UK Regulatory situation on cognitive access in the White Spaces
Andy Gowans/Mika Kasslin/Rich Kennedy
March 2011

## Slide 2: Overview
Where we are in the Europe/UK
Update on Conclusions so far in Europe/UK
Next steps towards implementation

## Slide 3: The story so far in Europe
European Commission
  RSPG published Report and subsequent Opinion on Cognitive Radio (includes sections on White spaces in the Broadcast bands) for more info see http://rspg.groups.eu.int/_documents/documents/meeting/rspg24/rspg_10_348_ct_opinion_final.pdf
  This may lead to further work being proposed by the European Commission to be taken through the Radio Spectrum Committee .
CEPT/ECC
  ECO have published ECC Report 159 –Cognitive radio systems in the “white spaces” in 470 790 MHz which was completed in the WGSE PT43. See http://www.erodocdb.dk/doks/doccategoryECC.aspx?doccatid=4
  WGFM have set up a correspondence group to work on frequency management activities for cognitive radio send mail to :listserv@list.ero.dk?Subject=Subscribe CG_CRS.
  WGRA have set up a correspondence group to work on regulatory and enforcement issues in relation to cognitive access to “white spaces” in 470 – 790 MHz send mail to :listserv@list.ero.dk?Subject=Subscribe%20WS_CR
ETSI
  ETSI Technical Committee on Reconfigurable Radio Systems (TC-RRS) have started work items looking at system requirements documents etc. for white spaces.
  TC-BRAN may also have an interest in this area in the future also.

## Slide 4: The story so far in UK
OFCOM consultations so far :
  Digital Dividend – cognitive access – Feb to May 2009 – see http://stakeholders.ofcom.org.uk/consultations/cognitive/?a=0
  Digital Dividend – Geolocation for Cognitive Access – Nov 2009 – Feb 2010 http://stakeholders.ofcom.org.uk/consultations/cogaccess/
  Implementing Geolocation - Nov 2010 to Date – see http://stakeholders.ofcom.org.uk/consultations/geolocation/ still collating responses but expect to send out a response soon
OFCOM also co-ordinating activities with:
  Regulatory work in EC and CEPT/ECC
  Standards activities in ETSI, IEEE 802, IETF Paws

## Slide 5
ECC Report 159 Covered
Assumptions on WSD characteristics
Protection of Broadcasting Service
Protection of PMSE systems
Protection of Radio Astronomy Service (608-614 MHz)
Protection of ARNS (645-790 MHz)
Protection of Mobile/Fixed Services in adjacent bands
Requirements to WSDs under Geo-location control
Estimated amount of White Space spectrum

## Slide 6: Overview
Where we are in the Europe/UK
Update on Conclusions so far in Europe/UK
Next steps towards implementation

## Slide 7: Conclusions So Far – ECC Report 159
Conclusions on Broadcast Service protection
  Spectrum sensing, if employed by a stand-alone WSD (autonomous operation) is not reliable enough to guarantee protection of nearby DTT receivers. However, a collaborative sensing may help.
  Operation of a WSD assisted by a geo-location database is currently the most feasible option
  Geo-location database would provide a WSD with information on the available frequencies and the associated maximum power values that the WSD is permitted to use
  Is left to administrations to decide whether to set or not fixed maximum permitted power limits for WSDs
Conclusions on PMSE protection
  Spectrum sensing appears to be problematic
  Geo-location database appears to be the most feasible approach
    Practical questions related to registration of PMSE data
    Different PMSE regulatory regimes across CEPT countries
  Disable beacon approach may provide a “bubble of protection” in locations where PMSE equipment is in use but no practical solutions proposed as yet.
  National or area specific safe-harbour channels not used by DTT and reserved for PMSE use seem a good idea to cover casual or temporary unregistered use.
General Conclusions
  Still more work to be done on suitable protection for ARNS and Fixed/Mobile bands in adjacent bands (below 470MHz and above 790MHz).
  Basis for the principles and requirements for operation of WSDs under the geo-location database have been proposed
  Information to be exchanged between a WSD and a geo-location database have been identified and proposed
  Administrations should have flexibility to adopt the geo-location framework suitable for their national circumstances

## Slide 8: Overview
Where we are in the Europe/UK
Update on Conclusions so far in Europe/UK
What do we need to look at going forward with a view towards implementation

## Slide 9: National versus International issues
Usage varies across many European countries
  Degree of protection for DTV (eg indoors / outdoors)
  Whether PMSE usage is registered
Regulators likely to have a different bias between protection of incumbents and facilitation of innovative new services
Usage models for cognitive may differ
  Rural broadband may be more important in some countries
  Degree of eg WiFi coverage differs
Need a framework that allows the same device to be used throughout Europe (and ideally the world) enabling roaming, economies of scale, etc
Need to optimise the balance between harmonisation and ability to tailor to national circumstances

## Slide 10: Ofcom viewpoint
Harmonise
Database addresses (so a device knows who to contact)
Format of information sent from the device
Format of information received by the device
Conformance Standard for declaring conformity with the R&TTE Directive
Leave to national regulators
Means of populating the database
Number of databases, ownership, geographical extent
Parameters used to populate database
  Propagation models
  Building penetration losses
  Required C/I ratios for devices
  Required locational accuracy and use of that information
Everything else!

## Slide 11: WHAT?
European harmonised conformance standard
ECC Report 159 and Ofcom Consultation give some examples of the data elements that regulators would like to see exchanged between database and the WSD. But WSD manufacturer’s are only responsible for ensuring compliance with the R&TTE Directive, so
what about guidance on conformance? This normally means compliance with a European Harmonised Standard written by ETSI. The HS will need to include the master set of European regulators requirements!
HS as a minimum should include conformance tests to assess :
    frequency accuracy
    location information provided by WSD
    location accuracy provided by WSD
    WSD maximum Transmit EIRP/power level given by the database
    WSD ACLR values/spectrum mask
    Spurious emission levels (both Tx and Rx)
    Validation request periodicity
Could also include conformance tests to assess:
    Extra requirements for allowing dispensations for Master or slave devices
      can the overall accuracy of the measurements of the master and slave locations can be combined into a single overall accuracy for a coverage area? How do we asses this?
    Extra requirements for allowing dispensations for Fixed or mobile use?
      how to do test taking into account an antenna or not?
Section 2

## Slide 12: Some of the Big Issues/ Questions?
ECC Report 159 and Ofcom Consultation give some examples of the data elements that regulators would like to see exchanged between database and the WSD. But WSD may have to differentiate between different national requirements (i.e. as they may only need to provide or act on a sub set of the full data set from the HS). So how complicated do we want these requirements to be?
Big issues - Questions :
Does the database need to differentiate between Fixed and Mobile?
Does the database or the standard need to differentiate between Master and Slave WSD?
Do we need to set the a maximum power level related to type of usage?
Should we allow for a Manual interface to enable the user to provide limited extra information (e.g. Antenna details, fixed/mobile or indoor/outdoor usage)
What use is a device identifier if it is not linked to an assumption (e.g. ACLR value)?
How de we deal with the geo-location accuracy problem?
Section 2

## Slide 13: Some of the Big Issues/ Questions?
Timescales going forward.
Big issues - Questions :
How long to get to stable ETSI harmonised Standard? (12-18 Month ?)
How long before PMSE and other adjacent band technical requirements will be finalised?
(6-12 month?)
When will any of the European administrations have a regulatory environment for database in place?
Will the EC issue any mandates/spectrum decision in order to facilitate use of Broadcast “white spaces in EU member states? Will there be an CEPT/ECC deliverable on spectrum usage for Broadcast “white spaces”?
Section 2