## Slide 1: RR-TAG (802.18) to 802.11 Liaison
Date: 19 January 2018
Authors:

## Slide 2: Items Reviewed/Discussed in the RR-TAG
Americas updates
    New spectrum bill proposed (S.1682)
      Includes a section on rule making on the unlicensed use of 5925 to 7125 MHz.
      Has gone no where.
    ISED consultation on harmonizing TVWS with the US
      Nothing of note to comment on.
    ISED consultation on Spectrum Outlook 2018 - 2022
      Walked though the 23 questions and ID'd ones we may want to comment on .
      No mention of the 6 GHz band
      Comments due 16 February 2018

## Slide 3: Items Reviewed/Discussed in the RR-TAG-2
EMEA updates
6 GHz activity
  EC mandate, RSCOM17-53rev1, now final and is limited to 5925-6425 MHz.
  ERM SR Doc, TR 103 524 has some opposition, still expecting to get published end of January.
  3GPPP RAN#78 (RP-172804) study item, looking at 5925 – 7125 GHz also.
  CEPT ECC SE45 and FM57 had their first meetings.
    SE45 Introduced RLAN parameters as contained in the SRDoc ETSI TR 103 524.
    FM57 discussed the opportunity to prepare a questionnaire and obtain information on the actual deployment and technical and operational parameters of FS in the 6 GHz range.

## Slide 4: Items Reviewed/Discussed in the RR-TAG-3
EMEA updates cont.:
60 GHz activity
  ETSI SR doc, TR 103 583 being worked on with some points on ITS channelization
Ofcom fixed wireless consultation looking at 6 and 60 GHz
  Fixed wireless links could change over the next 5-10 years.
  Asking different things for 57-66, 64-66 and 66-81GHz bands.
  And looking to move 1.4 GHz users to the 6 GHz band.
  Walked though the 11 questions and ID'd ones we may want to comment on. Refined at Ad Hoc on Wednesday.
  Approved on Thursday.

## Slide 5: Items Reviewed/Discussed in the RR-TAG-4
ETSI standards
  EN 301 893, 5GHz, has a new work item looking at several things.
    Including, Energy Detection Threshold, Receiver requirements with the blocking, and general text clarity
  EN 302 567, 60 GHz, not in OJEU yet, possibly by end of February
    Including OOB/Mask, Rx performance and test methods.
APAC updates
  ACMA LIPD class licensing consultation
    One of note is alignment with FCC in 57-66 GHz
  HKCA: Performance specification for radio equipment operating in the 920-925 MHz band for the provision of public tele services

## Slide 6: Additional
IEEE SA
Reviewed/commented on recent draft of the IEEE SA Board of Governors Position Statement on Additional Spectrum Needed (for IEEE).
  This is a continuation of reviewing/commenting an earlier draft at the November 2017 Plenary.
Ofcom Presentation
  Andy Gowans from Ofcom had a presentation on what is going on at Ofcom.
  https://mentor.ieee.org/802.18/dcn/18/18-18-0012-01-0000-ofcom-update-for-ieee-802.pptx

## Slide 7: Documents Approved
Documents Approved
  Agenda for the week
    https://mentor.ieee.org/802.18/dcn/18/18-18-0008-02-0000-rr-tag-irvine-interim-meeting-agenda-january-2018.pptx
  Orlando minutes
    https://mentor.ieee.org/802.18/dcn/17/18-17-0140-01-0000-meeting-minutes-nov-2017-orlando.docx
  Teleconference minutes
  Ofcom Fixed Wireless Consultation
    https://mentor.ieee.org/802.18/dcn/18/18-18-0009-02-0000-ofcom-questions-and-answers-fixed-wireless-spectrum-strategy.ppt
  IEEE SA BOG Additional Spectrum Needed Position Statement
    https://mentor.ieee.org/802.18/dcn/18/18-18-0010-01-0000-sa-use-of-spectrum-draft-position-06dec17.docx

## Slide 8: Next
Americas
  - Work on ISED consultation for Spectrum Outlook 2018 - 2022
EMEA
  6 GHz license exempt sharing
  60 GHz SR Doc. etc.
APAC
  Anything new that comes up.
Ongoing:
  Monitor / support ITU contributions, FCC comments, etc.

## Slide 9: 802.18 Meeting Close
The RR-TAG adjourned in AM1 on Thursday.
Will hold weekly, as needed, teleconferences, 14:30 ET Thursdays.
  Scheduled through 26 April 2018
  Next teleconference planed for 25 January 2018, 1430et/1130pt
    Call in information: 18-16/0038-08 (or latest)
    All notices are sent through the 802.18 listserver reflector.
The next face to face meeting of the 802.18 RR-TAG will be the Plenary 06-08 March 2018, Hyatt Regency O’Hare, Rosemont, Illinois, USA