## Slide 1: A Future For Unlicensed Spectrum
Date: 2018-05-31
Authors:

## Slide 2: Introduction
Regardless of everything we do to develop new, better, faster wireless technologies, the available spectrum has a hard limit
We can continue to go higher in frequency, but there are shortcomings in range, power requirements and cost
Technology breakthroughs are always possible, but infrequent
Where is the better answer: Unused and underused spectrum
Regulator recognition of this is key
All references to unlicensed, which is an FCC term, also refers to license exempt, as used elsewhere
Agenda

## Slide 3: White Spaces
DARPA Project XG tried to take advantage of unused spectrum
  www.daml.org/meetings/2005/04/pi/DARPA_XG.pdf
  Sensing across a range of frequencies could locate unused segments for a specific location and time, i.e. White Spaces
  Perfect identification of unused spectrum required, and very difficult using only sensing
In 2006, the FCC looked at this WRT the TV bands
  The digital transition could make a lot of spectrum available for unlicensed use
  However, the decision to auction the 600 MHz band severely limited the number of available channels

## Slide 4: TV White Spaces
To take advantage of this FCC “offer”, IEEE 802 developed two new standards
  802.11af for Local Area Networks (WLAN)
  802.22 for Regional Area Networks (WRAN)
The key to the success of this consumer technology was low cost based on Wi-Fi economies of scale as semiconductor companies could count on large markets
Unfortunately, with places like New York, Los Angeles and Chicago with one or fewer TVWS channels available, interest in developing silicon waned
TVWS – R.I.P. (at least foe WLANs)

## Slide 5: Rethinking White Spaces
The limited expectations for TVWS resulted in a loss of interest in all White Spaces
Based on location and time, there are still vast amounts of White Space, but with technical challenges
  Meeting technical and regulatory challenges has always been an IEEE 802 focus
  The key to rethinking White Spaces is identifying the challenges and meeting them
So what are the challenges?
  Technical: Efficient operation across a wide range of frequencies
  Regulatory: Getting help from regulators to enable use of all White Spaces

## Slide 6: Addressing the Technical Challenges
Today’s low cost technologies cannot efficiently address a wide range of frequencies
Radio components such as PAs, LNAs, and antennas are optimized for relatively narrow frequency ranges
Different frequency bands can have different regulatory limits on bandwidth, power, etc.
Breaking the radio out into a separate module can support multiple bands with today’s technologies
  Immediately applicable for last-mile wireless
Technology advances can address WLAN with Wi-Fi-like economies of scale

## Slide 7: Basic Architecture & Application

## Slide 8: Radio Module Features
Band specific radio, PA, LNA and antenna
  Bandwidth selected for efficiency/cost of RF components
  Selectable efficiency
    For cost reduction – wider bandwidth coverage with a single module at lower efficiency
Memory device with regulatory database information relative to the specific band
  Pre-programmed
  Internet updateable
  Contains MAC parameters for the specific band
Communicates with MAC module
  MAC setup
  Periodic regulatory updates from the Internet
  Checks for energy on white space channels and reports to central database
Optional additional radio for In-Service Monitoring (ISM)

## Slide 9: MAC Module Features
Standard 802.11 or 802.22 MAC
Regulatory controls
  Interface with Radio module
    to get MAC parameters for the specific band
    to provide updates to database memory
  Interface with the database via the Internet
    to get database updates
    to relay detected database errors, inaccuracies

## Slide 10: Much Work Needed
Only the basic concepts are addressed here
Separation of the radio module will require standards work
To make this workable for low-cost WLAN use, advances are needed
  Frequency adjustable antennas need to be made practical for this application
  Wide-range, efficient approach to LNA, PA design
I suggest we develop a position paper on why IEEE 802 believes that database control of spectrum access is a future requirement, and regulators need to start that development now

## Slide 11: Addressing the Regulatory Challenges
Far more daunting are the regulatory challenges
  Regulators hesitant to upset the status quo, i.e. fixed allocation of spectrum with traditional protections against interference
  Incumbents resist any sharing, no matter how effective technology is in protecting them from interference
  Incumbents who have paid for spectrum do not want to deal with “freeloaders”
TVWS database proven effective
CBRS database being tested; 6 GHz band sharing will need a database
AI can significantly add to protection of incumbents and effective sharing

## Slide 12: What We Must Do
Convince regulators that unlicensed spectrum is important, and this is the only way it can continue to support wireless applications
Show the importance of unlicensed spectrum
  Benefit to the economy
  Benefits to education
  A means to get everyone connected to the Internet, in an economical way
Develop a plan of action on engaging AI in spectrum management, and show the benefits
We must start NOW!

## Slide 13: Questions?