## Slide 1: Outdoor UWB Regulation of Japan
Authors:

## Slide 2: Background
The first UWB regulation of Japan
  Released in August 2006
  Indoor-only operation
  Additional conditions on data rate, AC mains power supply, etc.
Main revisions in the past
  Extension of DAA exemption at low band in 2008
  Extension of DAA exemption at low band in 2010
  Repealing conditions on data rate at UWB high band in 2014
  Repealing conditions on AC mains power supply in 2014

## Slide 3: Indoor Spectrum
  Low band: 3.4 - 4.2 GHz
    average@-41.3 dBm/MHz; peak@0 dBm/50 MHz
    Data rate requirement
    DAA requirement
  High band: 7.25 – 10.25 GHz
    average@-41.3 dBm/MHz; peak@0 dBm/50 MHz

## Slide 4: New Released Outdoor Spectrum
The most recent revisions
  Released on May 20, 2019
  Admitting outdoor operation
  Using EIRP definition
Outdoor spectrum
  High band only: 7.587 – 8.4 GHz
  average@-51.3 dBm/MHz : 7.587 – 7.662 GHz
  average@-41.3 dBm/MHz : 7.662 – 8.4 GHz
  peak@0 dBm/50MHz: 7.587- 8.4 GHz

## Slide 5: Others
Official English version of the new revisions is not available
Details of the new revisions will be incorporated into an ARIB Standard.
An English version of the ARIB Standard will be available.
ARIB: Associations of Radio Industries and Businesses