## Slide 1: Latest Positions of APT on selected WRC-19 agenda items after APG19-5
Author:

## Slide 2: Background
This slide deck summarizes the latest preliminary positions of Asia Pacific Telecommunity (APT) and on the following WRC-19 agenda items: 1.12, 1.13, 1.15, 1.16, 9.1 issue 9.1.5, and 10 (related to 6 GHz) after the end of the APG 19-5 meeting that was held in Tokyo, Japan, from July 31 to August 6, 2019 [1].

## Slide 3: Preliminary APT Common Proposals
At the APG19-5 meeting, Preliminary APT Common Proposals (PACP) with consensus approach were developed [3].
Consensus approach does not allow overriding the views supported by less number of APT members
  In such cases, PACP was either developed with TBD or not developed. APG will continue elaborating the view on such cases in APG coordination meeting during WRC-19.

## Slide 4: APT Common Proposals
The PACP is currently under an adoption process of 38 APT members
  PACP is become APT Common Proposal (ACP) once the following two conditions are met:
    Supported by more than 25% of the APT members, i.e., 10 members
    Not opposed by more than 50% of the members who support, i.e., 5 members

## Slide 5: Item 1.12 (1)
To consider possible global or regional harmonized frequency bands, to the maximum extent possible, for the implementation of evolving Intelligent Transport Systems (ITS) under existing mobile-service allocations, in accordance with Resolution 237 (WRC-15).

## Slide 6: Item 1.12 (2)
From the CPM report [2]:
  1/1.12/4 Methods to satisfy the agenda item
  1/1.12/4.1 Method A – No change to the Radio Regulations and suppress Resolution 237 (WRC-15).
  1/1.12/4.2 Method B – No change to the Table of Frequency Allocations in the Radio Regulations, and add a new WRC Resolution to encourage administrations to use 5 850-5 925 MHz, or parts thereof, as global harmonized evolving ITS frequency bands. Other harmonized frequency band(s) for evolving ITS applications refer to the most recent version of Recommendation ITU-R M.2121.
  1/1.12/4.3 Method C – No change to the RR Table of Frequency Allocations and to add a new WRC Resolution to encourage administrations to use globally and regionally harmonized frequency bands for ITS applications through reference to ITU-R Recommendation(s). Suppress Resolution 237 (WRC-15).

## Slide 7: Item 1.12 (3)
Summary of the APT positions:
APT Members are of the view that there are needs for harmonization of spectrum use in existing mobile service allocations for evolving ITS.
APT Members support possible harmonization of frequency bands in existing mobile service allocations for the implementation of evolving ITS.
APT Members support the consideration of the 5850-5925 MHz frequency band, or parts thereof, as a global harmonization frequency band for evolving ITS.
APT members also support the consideration of examples of ITS frequency bands in current use as listed in the Annex of Recommendation ITU-R M.2121 for regional harmonized ITS frequency bands.

## Slide 8: Item 1.12 (4)
Summary of the APT positions (cont’d):
APT Members agree that no changes are needed for the Table of Frequency Allocations for harmonization of spectrum use of ITS.
APT Members are also of the review that evolving ITS should not be restricted to, nor exclude, any particular evolving ITS technology, including LTE based V2X and its evolution technologies.
APT Members are also of the view that the use of the frequency bands by ITS should not adversely affect other primary services to which these frequency bands are allocated should not claim protection from other primary services including the uplinks of FSS earth station.
APT Members support the suppression of Resolution 237 (WRC-15).

## Slide 9: Item 1.13 (1)
To consider identification of frequency bands for the future development of International Mobile Telecommunications (IMT), including possible additional allocations to the mobile service on a primary basis, in accordance with Resolution 238 (WRC‑15).

## Slide 10: Item 1.13 (2)
From the CPM report [2]:
  2/1.13/4.10 Item J: Frequency band 66-71 GHz
  2/1.13/4.10.1 Method J1: NOC
  2/1.13/4.10.2 Method J2: Identification of the frequency band 66-71 GHz for IMT in accordance with the following two alternatives (see [2]) and removal of the frequency band from RR No. 5.553
  2/1.13/4.10.3 Method J3: To continue studies on the possibility of identification in the frequency band 66-71 GHz for IMT with a WRC Resolution
  2/1.13/4.10.4 Method J4: Identification of the frequency band 66-71 GHz for IMT in accordance with the following two alternatives (see [2]) and retention of the frequency band in RR No. 5.553

## Slide 11: Item 1.13 (3)
From the CPM report [2]:
  2/1.13/4.11 Item K: Frequency band 71-76 GHz
  2/1.13/4.11.1 Method K1: NOC
  2/1.13/4.11.2 Method K2: Identification of the frequency band 71-76 GHz for IMT in accordance with the following two alternatives (see [2])

## Slide 12: Item 1.13 (4)
Summary of the APT positions on 66-71 GHz:
APT Members support identification of the frequency band for IMT.
However, APT Members are still investigating method and condition(s) to be adopted when identifying this band for IMT.
Summary of the APT positions on 71-76 GHz:
APT Members agree to further investigate whether this band could be considered for IMT identification at WRC-19.

## Slide 13: Item 1.15 (1)
To consider identification of frequency bands for use by administrations for the land-mobile and fixed services applications operating in the frequency range 275-450 GHz, in accordance with Resolution 767 (WRC-15).

## Slide 14: Item 1.15 (2)
From the CPM report [2]:
  1/1.15/4.1 Method A: No change to the Radio Regulations.
  1/1.15/4.2 Method B: Modifying the existing footnote RR No. 5.565 is proposed for FS/LMS applications in portions of the 275-450 GHz frequency range.
  1/1.15/4.3 Method C: This method suggests adding a new footnote to identify the 275-450 GHz frequency range for use by FS/LMS applications, while protecting EESS (passive) and RAS using the evolving guidance of ITU-R Recommendations and Reports, taking into account that there are no service allocations above 275 GHz.
  1/1.15/4.4 Method D: Adding a new footnote RR No. 5.D115 is proposed for land mobile and fixed service applications: 275-296 GHz, 306-313 GHz, 320-330 GHz and 356-450 GHz.

## Slide 15: Item 1.15 (3)
From the CPM report [6] (con’t):
  1/1.15/4.5 Method E: Adding a new footnote RR No. 5.E115 and modifying the existing footnote RR No. 5.565 are proposed for FS/LMS applications in portions of the 275-450 GHz band.
  1/1.15/4.6 Method F: Adding a new footnote RR No. 5.F115 is proposed for FS applications in portions of the 275-450 GHz band and for LMS applications in the entire 275-450 GHz frequency band.
  1/1.15/4.6 Method G: Adding a new footnote RR No. 5.G115 is proposed for FS/LMS applications in portions of the 275-450 GHz band.

## Slide 16: Item 1.15 (4)
Summary of the APT positions:
APT Members support to consider identification of frequency bands for use by the land mobile and fixed service applications operating in the frequency range 275-450 GHz, taking into account the study results conducted by the relevant ITU-R WPs, provided that the protection of passive services identified in RR No. 5.565 is ensured.
APT Members support to add a new footnote to the relevant part of the Radio Regulations for the land mobile service and fixed service.
APT Members support NOC to RR No. 5.565.
In the frequency bands identified for RAS in RR No. 5.565, namely 275-323 GHz, 327-371 GHz, 388-424 GHz, and 426-442 GHz, separation distance and/or avoidance angles between RAS stations and FS stations should be considered depending on the deployment environment of the FS stations.

## Slide 17: Item 1.16 (1)
To consider issues related to wireless access systems, including radio local area networks (WAS/RLAN), in the frequency bands between 5 150 MHz and 5 925 MHz, and take the appropriate regulatory actions, including additional spectrum allocations to the mobile service, in accordance with Resolution 239 (WRC-15).

## Slide 18: Item 1.16 (2)
From the CPM report [2] on Frequency band A (5150-5250 MHz):
  2/1.16/4.1.1 Method A1: No change to the RR
  2/1.16/4.1.2 Method A2: Revision to Resolution 229 (Rev.WRC-12) to enable outdoor RLAN operations including possible associated conditions for new e.i.r.p. limits
  2/1.16/4.1.3 Method A3: Revision to Resolution 229 (Rev.WRC-12) to enable outdoor RLAN operations by applying the same conditions of use as defined for the 5250-5350 MHz frequency band in resolves 4 of Resolution 229 (Rev.WRC-12)
  2/1.16/4.1.4 Method A4: Revisions to Resolution 229 (Rev.WRC-12) to facilitate limited RLAN outdoor operation and RLAN in-vehicle (cars and trains) usage operation with associated e.i.r.p. levels
  2/1.16/4.1.5 Method A5: Revisions to Resolution 229 (Rev.WRC-12) to enable in-car use of RLAN operation with e.i.r.p. up to 40 mW
  2/1.16/4.1.6 Method A6: Revision to Resolution 229 (Rev.WRC-12) to enable outdoor RLAN operations including associated conditions for new e.i.r.p. limits and out-of-band emission limits

## Slide 19: Item 1.16 (3)
From the CPM report [2] on Frequency band B (5250-5350 MHz):
  2/1.16/4.2.1 Method B: No change to the RR
From the CPM report [2] on Frequency band C (5350-5470 MHz):
  2/1.16/4.3.1 Method C: No change to the RR

## Slide 20: Item 1.16 (4)
From the CPM report [2] on Frequency band D (5725-5850 MHz):
  2/1.16/4.4.1 Method D1: No change to the RR
  2/1.16/4.4.2 Method D2: A new Regional primary MS allocation
  2/1.16/4.4.3 Method D3: Accommodate WAS/RLAN in a new footnote
From the CPM report [2] on Frequency band E (5850-5925 MHz):
  2/1.16/4.5.1 Method E: No change to the RR

## Slide 21: Item 1.16 (5)
Summary of the APT positions:
APT Members are of the view that the protection of incumbent services including their current and planned use in the frequency bands 5150-5250 MHz, 5250-5350 MHz, 5350-5470 MHz, 5725-5850 MHz, and 5850-5925 MHz should be ensured, without unacceptable constraints on these services.
In the frequency bands 5250-5350 MHz, 5350-5470 MHz, and 5850-5925 MHz, APT Members support NOC to the Radio Regulations for the use of WAS/RLAN to protect incumbent services.

## Slide 22: Item 1.16 (6)
Summary of the APT positions (cont’d):
In the frequency band 5150-5250 MHz, APT Members do not support Methods A2, A4, A5, and A6. In addition, there is no consensus on either Method A1 or A3. APT Members support further consideration and investigation on the possibility of outdoor WAS/RLANs operation under the condition that incumbent services including the further development of these services are fully protected
  2/1.16/4.1.1 Method A1: No change to the RR
  2/1.16/4.1.3 Method A3: Revision to Resolution 229 (Rev.WRC-12) to enable outdoor RLAN operations by applying the same conditions of use as defined for the 5250-5350 MHz frequency band in resolves 4 of Resolution 229 (Rev.WRC-12)
In the frequency band 5725-5850 MHz, APT Members support to allocate it to the mobile service on a primary basis in Region 3.

## Slide 23: Item 9.1 issue 9.1.5 (1)
Resolution 764 (WRC-15) - Consideration of the technical and regulatory impacts of referencing Recommendations ITU-R M.1638-1 and ITU-R M.1849-1 in Nos. 5.447F and 5.450A of the Radio Regulations.

## Slide 24: Item 9.1 issue 9.1.5 (2)
From the CPM report [2]:
  Approach A updates both footnotes by removing the references and replacing them with the sentence “Resolution 229 (Rev.WRC-12) applies”.
  Approach B updates both footnotes by removing the references to the Recommendations and replacing them with a reference to RR No. 5.446A.

## Slide 25: Item 9.1 issue 9.1.5 (3)
Summary of the APT positions:
APT Members support Approach A by referencing Resolution 229 (Rev. WRC-12) in RR No. 5.447F and 5.450A as a long term solution that would avoid reopening the issue of reassessing technical and regulatory impacts when referencing new versions of the ITU-R Recommendations in the future, while creating no additional constraints to the mobile service, and also ensuring protection of the radiolocation service.

## Slide 26: Item 10 (1)
To recommend to the Council items for inclusion in the agenda for the next WRC, and to give its views on the preliminary agenda for the subsequent conference and on possible agenda items for future conferences, taking into account Article 7 of Convention.

## Slide 27: Item 10 (2)
Summary of the APT positions on 6 GHz band:
APT Members support to consider identification for IMT in the frequency range 7025-7125 MHz in accordance with Resolution [ASP-AI10-IMT] (WRC-19);
In addition to the 7025-7125 MHz frequency band, the 5925-6725 MHz frequency band was also considered for which consensus is yet to be reached at this stage.

## Slide 28: Reference
[1] https://www.apt.int/APTAPG
[2] Report of the CPM on technical, operational and regulatory/procedural matters to be considered by the World Radiocommunication Conference 2019, March 2019, Available at https://www.itu.int/md/R15-CPM19.02-R-0001/en
[3] https://www.apt.int/sites/default/files/Upload-files/APG-19/WRC-19/PACP_WRC-19_Updated.zip