## Slide 1: APAC update – November 2019
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between September and November 2019.

## Slide 3: Australia ACMA (1)
Consultation on Spectrum Sharing: Overview and New Approaches
  Closed on September 27, 2019
  https://www.acma.gov.au/consultations/2019-10/new-approaches-spectrum-sharing-consultation-252019
  To provide an overview of spectrum sharing concepts as they currently exist and outline new approaches to spectrum sharing arrangements, including examples of sharing arrangements being either introduced or considered internationally. This is intended to provide a common information base against which new proposals for spectrum sharing can be considered.
  List of submissions:
    https://www.acma.gov.au/sites/default/files/2019-11/ifc-25-2019-submissions.zip

## Slide 4: Australia ACMA (2)
Consultation: Compliance priorities 2020 to 2021
  Submission deadline: December 5, 2019
  https://www.acma.gov.au/consultations/2019-11/compliance-priorities-2020-2021-consultation
  Note the compliance priorities for 2019 to 2020 are as follows:
    Telco consumer safeguards
    Small cell base stations for 4G and 5G
    Unsolicited communications
    News
    Gambling
    Interference and licencing compliance

## Slide 5: Indonesia MCIT (1)
Short range device requirements are updated since July 2019:
  https://sertifikasi.postel.go.id/home/news?id=65
  SRD consists of the following categories: (a) Bluetooth (b) Telecommunication device with transmit power less than 10mW (commonly called low power device) (c) RFID (d) NFC (e) IEEE 802.15.4 based WPAN (f) Intelligent transport system (g) Other SRD telecommunication equipment

## Slide 6: Indonesia MCIT (2)
Short range device requirements are updated since July 2019 (Cont’d):
  https://sertifikasi.postel.go.id/home/news?id=65
  Technical characteristics and conformance requirement of IEEE 802.15.4 based WPAN is shown in page 14.
  It does not explicitly mention WLAN but it would be parts of “Other SRD telecommunication equipment” operating at the frequency bands as listed in pages 15 - 19, including 920-923 MHz, 2400-2483.5 MHz, 5150-5250 MHz, 5250-5350 MHz, 5725-5825 MHz.

## Slide 7: Japan MIC (1)
Update on the technical conditions of radar systems operating at 60 GHz band
  http://www.soumu.go.jp/menu_news/s-news/01kiban14_02000401.html

## Slide 8: Existing Technical Conditions (as shown in IEEE 802.11-15/0594r0)
 | Maximum antenna power of 10 dBm | Antenna power in excess of 10 dBm
Frequency band | 57-66GHz | 57-66GHz
Unit channel | Not specified | Not specified
Radio channel | Not specified | Not specified
Antenna power | 10 dBm max. | More than 10 dBm and not in excess of 24 dBm
Equivalent isotropic radiated power | Not specified | 40 dBm max.
Antenna gain | 47 dBi max. | If the antenna power is in excess of 10 dBm, 10dBi or more in the direction of emission.
Modulation system | Not specified | Not specified
Carrier sense | Not specified | Must incorporate an interference reduction with a carrier sense.
Occupied bandwidth | Not specified up to 9 GHz. | Not specified up to 9 GHz.
Allowable value of unwanted emission intensity | 55.62 GHz max.: -30 dBm/MHz max. More than 55.62 GHz and not in excess of 57 GHz: -26 dBm/MHz max. More than 66 GHz and not in excess of 67.5 GHz: -26 dBm/MHz More than 67.5 GHz: -30d Bm/MHz max. | 55.62 GHz max.: -30 dBm/MHz max. More than 55.62 GHz and not in excess of 57 GHz: -26 dBm/MHz max. More than 66 GHz and not in excess of 67.5 GHz: -26 dBm/MHz max. More than 67.5 GHz: -30 dBm/MHz max.
Allowable deviation of antenna power | 50% upper limit and 70% lower limit | 50% upper limit and 70% lower limit
Allowable deviation of frequency | Specified frequency band or ±500 ppm | Specified frequency band or ±20 ppm
Limit of secondary radio waves emitted from receiving devices | Less than 1 GHz: 4 nW/100 kHz max. 1 GHz min.: 20 nW/1 MHz max. | 1 GHz min.: 4 nW/100 kHz max. 1 GHz min.: 20 nW/1 MHz max.

## Slide 9: Proposed Technical Conditions
 | mmW radar without carrier sense | mmW radar with carrier sense | Low power data communications
Usage | Radiolocation | Radiolocation | Data communications
Frequency band | 57-64 GHz | 57-66 GHz | No change from the current technical conditions
Antenna power | 10 dBm max. | Not exceed 24 dBm max. | 
Equivalent isotropic radiated power | 13 dBm max. | 40 dBm max. | 
Antenna gain | Not specified | 10 dBi above | 
Modulation system | Frequency modulation, continuous wave | Not specified | 
Occupied bandwidth | 7 GHz | 9 GHz | 
Allowable value of unwanted emission intensity | 55.62 GHz max.: -30 dBm/MHz max. More than 55.62 GHz and not in excess of 57 GHz: -26 dBm/MHz max. More than 64 GHz and not in excess of 67.5 GHz: -26 dBm/MHz More than 67.5 GHz: -30dBm/MHz max. | 55.62 GHz max.: -30 dBm/MHz max. More than 55.62 GHz and not in excess of 57 GHz: -26 dBm/MHz max. More than 66 GHz and not in excess of 67.5 GHz: -26 dBm/MHz max. More than 67.5 GHz: -30 dBm/MHz max. | 
Others | Within 10% of the time, during which radio waves can be emitted within 33 milliseconds Should have a function to stop the emission of the waves | Carrier sense | 
Allowable radio wave exposure to human body (power density) | 2mW/cm2 per 1cm2 of any body surface |  | 
Interference avoidance | By identifying the modulation method and other characteristics of the received radio wave, it is possible to distinguish between the reflected wave of the radio wave transmitted by the local station and the radio wave transmitted by another wireless station. |  | 
Conditions required for the system | The high frequency section and modulation section cannot be opened easily. In addition, when the high-frequency unit and the modulation unit are housed in separate cases, measures must be taken to maintain the identity of the transmitter and these two units cannot be opened easily. |  | 

## Slide 10: Philippines DICT
DICT holds nationwide simultaneous Free Wi-Fi for All launch
  https://dict.gov.ph/dict-holds-nationwide-simultaneous-free-wi-fi-for-all-launch/
  32 Internet sites across 17 regions in the Philippines were simultaneously launched on October 8 through the Department of Information and Communications Technology’s Free Wi-Fi for All program.

## Slide 11: Vietnam MIC (1)
MIC seeks comments from the public on the compulsory standards applied on digital signatures and digital signature authentication services on mobile devices
  Closed on November 5, 2019
  https://dict.gov.ph/dict-holds-nationwide-simultaneous-free-wi-fi-for-all-launch/
  Best-effort translation:

## Slide 12: Vietnam MIC (2)
In 2016, Vietnam MIC circulated a draft that revises the regulation on license-exempt frequency bands. It is now effective and the detail is available at:
  http://mic.gov.vn/Pages/VanBan/14306/1_VBHN-BTTTT.html
Selected highlights:
  Increase the maximum RF output power allowed of WLAN devices operating at 2.4 GHz up to 200mW.
  Wide Band Communication Device is a radio device that is used in IMT-Advanced wideband transmission applications using the bands 5150-5350 MHz and 5470-5850 MHz at the bandwidth of at least 20 MHz or for access with the rate of up to Gigabit/s in WLAN or WPAN operating in the 57- 66 GHz frequency band.

## Slide 13: Vietnam MIC (3)
Selected highlights (Cont’d)
  WLAN devices can operate at the following bands: 2400 - 2483.5 MHz, 5150 - 5250 MHz (indoor only), 5250 - 5350 MHz (subject to DFS/TPC), 5470 - 5725 MHz (subject to DFS/TPC), 5725 - 5850 MHz, and 57- 66 GHz.
  Updated regulation on devices with operating frequency up to 246 GHz including automotive radars and UWB devices.
  Replace the operating frequencies of RFID from 920-925 MHz to 918-923 MHz band.
  Remove the operating frequencies of 866 ~ 868 MHz allocated for RFID. The RFID products operating at these bands which have been manufactured or imported before enforcing date of this Circular can still be used in Vietnam, but must be stopped if cause harmful interference to licensed bands.