## Slide 1: APAC update – March 2020
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between January and March 2020.

## Slide 3: Asia-Pacific Telecommunity (APT)
Calendar of events in 2020 is significantly revised
  https://www.apt.int/sites/default/files/2020/03/CALENDAR_OF_APT_EVENTS_FOR_THE_YEAR_2020-v2.2.pdf
  Of possible interest to us includes:
    The 26th Meeting of the APT Wireless Group (AWG-26)
      Tentatively postponed to June 8-12, Bangkok, Thailand
    The 1st Meeting of the APT Conference Preparatory Group for WRC-23 (APG23-1)
      Tentatively held on July 8-10, Xi’an, China

## Slide 4: Australia ACMA
Consultation: Amendment to EME arrangements
  Closed on March 12, 2020
  https://www.acma.gov.au/consultations/2020-01/amendment-eme-arrangements-consultation-042020
  To ask for public opinions in adopting IEC TR 63170 into the ACMA Standard as a measurement method for devices operating between 6 GHz and 100 GHz.
    IEC TR 63170 is a technical report that describes measurement techniques and test approaches for evaluating the local and spatial average incident power density of wireless devices operating in close proximity to the user between 6 GHz and 100 GHz

## Slide 5: New Zealand RSM
Gazette notice: Radiocommunications (Radio Standards) Notice 2020
  https://gazette.govt.nz/notice/id/2020-go115
  This notice describes the performance standards required to be met by different classes of radio product, and the unwanted emission power limit for any transmitter not covered by those standards. Additionally, limits of unwanted emissions are specified for Low Power FM transmitters. The notice also assigns the level of conformity applying to the products covered by each standard.
  There are updates in applicable standards for different classes of radio products.

## Slide 6: India DOT TEC
Consultation on Indian Telecom Security Assurance requirements of Mobile Handset
  DOT had amended the license agreement by incorporating the provisions of Security Testing and certification of Telecom equipment’s with the Telecom Service Providers. This Testing and Certification of the telecommunication equipment’s shall be done for ensuring compliance with the respective Essential Requirements (ER) documents of TEC. Essential Requirements consists of i) EMC/EMI Requirements ii) Safety Requirements iii) Security Requirements iv) Technical Requirements v) Other Requirements.
    http://www.tec.gov.in/pdf/Whatsnew/Mobile%20Device%20ITSAR%2027-02-2020(1).pdf
    http://www.tec.gov.in/pdf/Whatsnew/Prescribed_cryptocontolsforITSARFrozen08112019.pdf

## Slide 7: Japan MIC
Consultation: Electronic Signatures and Certification Services
  Closed on February 26, 2020
  https://www.soumu.go.jp/menu_news/s-news/01cyber01_02000001_00059.html
  To ask for public opinions in updating its rules for electronic signatures and certification services. In particular, one proposal is to remove SHA-1 from its Guidelines on Accreditation of Specific Certification Business. And another is to increase the prime factor from 1024 to 2048 in its Enforcement Regulations on Electronic Signatures and Authentication Business.