## Slide 1: Introduction to FCC-20-76-A1: Modernizing and Expanding Access to the 70/80/90 GHz bands
Author:

## Slide 2: Abstract
It is a high-level summary of the recent FCC’s Notice of Proposed Rulemaking and Order related to 70/80/90 GHz band.
For details, please refer to
  https://mentor.ieee.org/802.18/dcn/20/18-20-0104-02-0000-fcc-proposed-rule-modernizing-and-expanding-access-to-the-70-80-90-ghz-bands.docx
  https://www.federalregister.gov/documents/2020/07/06/2020-14064/modernizing-and-expanding-access-to-the-708090-ghz-bands

## Slide 3: Frequency bands of interest
71-76 GHz
81-86 GHz
92-94 GHz
94.1-95 GHz
All are subject to 47 CFR Part 101.1501 to Part 101.1527 (Fixed Microwave Services) at https://www.law.cornell.edu/cfr/text/47/part-101

## Slide 4: Existing Allocations (Co-Primary Basis)
Band | Non-Federal Use | Federal Use
71-74 GHz | Fixed, Fixed Satellite, Mobile, and Mobile Satellite | Fixed, Fixed Satellite, Mobile, and Mobile Satellite
74-76 GHz | Fixed, Fixed Satellite, Mobile, Broadcasting, and Broadcasting Satellite | Fixed, Fixed Satellite, and Mobile
81-84 GHz | Fixed, Fixed Satellite, Mobile, Mobile Satellite, and Radio Astronomy | Fixed, Fixed Satellite, Mobile, Mobile Satellite, and Radio Astronomy
84-86 GHz | Fixed, Fixed Satellite, Mobile, and Radio Astronomy | Fixed, Fixed Satellite, Mobile, and Radio Astronomy
92-94 GHz, 94.1-95 GHz | Fixed, Mobile, Radio Astronomy, and Radiolocation | Fixed, Mobile, Radio Astronomy, and Radiolocation

## Slide 5: Existing service rules for non-federal use (point to point, non-broadcast service)
A two-pronged, non-exclusive licensing regime
  An entity may apply for a nationwide, non-exclusive license for the entire 12.9 gigahertz of the 70/80/90 GHz bands.
  A licensee may operate links after completing coordination with Federal operations through NTIA’s database and after providing an interference analysis to one of the third-party database managers.
As of March 23, 2020:
  658 active non-exclusive nationwide licensees
  18,770 registered fixed links

## Slide 6: Motivation this rulemaking and order
To facilitate the provision of wireless backhaul for 5G, as well as the deployment of broadband services to aircraft and ships, while protecting incumbent operations in the 70/80/90 GHz bands.
NOTE – The Commission is revisiting in this rulemaking its decision in the 2017 Spectrum Frontiers Order not to allow mobile service in the 70/80/90 GHz bands, given the evolution in technology.

## Slide 7: Scope of this rulemaking and order
Propose changes to the antenna standards applicable to the 70 GHz and 80 GHz bands and seek comment on whether similar changes are necessary in the 90 GHz band;
Should the Commission make changes to its current link registration rules for the 70/80/90 GHz bands to eliminate never-constructed links from the database?
Proposes to authorize point-to-point links to endpoints in motion in the 70 GHz and 80 GHz bands and to classify those links as a “mobile” service;
  Seek comment on any technical and operational rules that would be needed to allow these new service offerings in the 70 GHz and 80 GHz bands and to mitigate interference to incumbents and other proposed users of these bands and in adjacent bands.
Should the Commission adopt a channelization plan in the 70 GHz and 80 GHz bands?

## Slide 8: Relevant to IEEE 802?
Even though this notice of proposed rulemaking and order focuses on 5G backhaul and the communications to ships and aircrafts, it did ask whether any changes of Part 101 rules necessary to accommodate other potential uses of the 70/80/90 GHz bands, and whether any other rule changes help to promote innovative use of the 70/80/90 GHz bands.

## Slide 9: 5G Backhaul: Antenna Rules
Existing rule:
  The Commission’s rules currently apply a single category of antenna standards to the 70 GHz band and the 80 GHz band.
Proposed change:
  Increase the maximum beamwidth by 3 dB points from 1.2 degrees to 2.2 degrees, reduce minimum antenna gain from 43 dBi to 38 dBi and to retain the proportional EIRP reduction requirement.
  Seek comment on whether the current stricter co-polar and cross-polar discrimination requirements are now unnecessary.
  Seek comment on whether the Commission allow ±45 degree polarization (also known as slant polarization) in the 70 GHz and 80 GHz bands.
  Seek comment on whether to adopt an additional antenna standard, Category B, applicable to the 70 GHz and 80 GHz bands, which could permit less restrictive use under certain circumstances than the proposed modified antenna standards (which would be the accompanying Category A standards).
  Seek comment on whether any of the changes discussed in this Notice or other changes should apply to the 90 GHz band.

## Slide 10: 5G Backhaul: Link Registration Rules
Existing rule:
  Licensees in the 70/80/90 GHz bands must complete construction and bring into regular use registered links within 12 months of the date on which a third-party database manager registers the link.
  Currently, the Commission relies on licensees to notify database managers to withdraw unconstructed links from the database.
Proposed change:
  Should the Commission require 70 GHz and 80 GHz band registrants to file a certification of construction when a link has been placed in operation?
  Should different rules apply for registrants in the 90 GHz band?
  What changes, if any, should the Commission make to its rules to ensure that registrations accurately reflect actual use of the 70/80/90 GHz bands?

## Slide 11: Communications to Ships and Aircrafts: Authorization Framework
Existing rule:
  Point-to-point links to endpoints in motion are not allowed to operate in the 70/80/90 GHz bands.
Proposed change:
  Propose to authorize point-to-point links to endpoints in motion in the 70 GHz and 80 GHz bands under Part 101 rules.
  Seek comment on whether the introduction of these new types of services in these bands would affect existing point-to-point microwave services or the potential for deployment of other non-Federal and Federal services in the bands, and how to continue to protect co-primary and adjacent Federal operations.
  Seek comment on what changes to the 70/80/90 GHz coordination, licensing, and registration framework would be necessary to permit the operation of links to endpoints in motion under Part 101.105.
  Propose to continue licensing use of the 70 GHz and 80 GHz bands on a non-exclusive, nationwide basis, and require coordination and registration of all air- and sea- based links/links between antennas in motion,

## Slide 12: Communications to Ships and Aircrafts: Technical & Operational Rules
Proposed change:
  Increase the maximum allowable mobile EIRP for 71–76 GHz and 81–86 GHz from +55 dBW to +57 dBW.
  Increase the maximum transmitter power from 3 watts (5 dBW) to 5 watts (7 dBW).
  Increase the maximum transmitter power spectral density from 150 mW per 100 MHz to 500 mW per 100 MHz.
  Seek comments on not only the proposed changes but also on whether the technical rules would increase the potential for harmful interference to those vehicular radars operating in the 76-81 GHz band as well as passive services in the 86-92 GHz band.

## Slide 13: Communications to Ships and Aircrafts: Channelization plan
Existing rule: None
  The Commission eliminated the 1.25 GHz segments in 2005 that necessitate development of a channel plan.
Proposed change:
  Seek comment on whether the Commission develops a channel plan for the 70 GHz and 80 GHz bands. Would establishing a channel plan restrict the development of innovative equipment for the bands, as the Commission feared in 2005?
  Seek comment on whether authorizing links to endpoints in motion requires the Commission to adopt a formal channel plan for the 70/80/90 GHz bands.
  If the Commission were to adopt a channel plan, then what channel plan should it use?
  Should the Commission revise section 101.109(c) of the Part 101 rules to specify a maximum bandwidth less than 5,000 MHz for the 70 GHz and 80 GHz bands? Should the Commission increase the minimum bit rate of 0.125 bits per second per Hz to, for example, 1 bit per second per Hz?

## Slide 14: Communications to Ships and Aircrafts: Others
Seek comments on
  Are any other rule changes necessary to accommodate other potential uses of the 70/80/90 GHz bands?
  Would any other rule changes help to promote innovative use of the 70/80/90 GHz bands?