## Slide 1: APAC update – July 2020
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between May and July 2020.

## Slide 3: Korea MSIT
Consultation on Revision of the Table of Frequency Allocation on 5 GHz and 6 GHz
  Comments due on August 24, 2020. For details:
    http://english.msip.go.kr/web/msipContents/contentsView.do?cateId=_law4&artId=2942267
  Motivation:
    To enable high-quality data service and accelerate the adoption of 5G convergence services using 5G-class unlicensed technology (e.g, WiFi 6E, 5G NR-U) in the 6 GHz band.
  Proposed change:
    Allow specific low-power wireless access systems including wireless LAN to be operated in the 5725-5850 MHz and 5925-712 MHz frequency bands by amending K37E in the Table of Frequency Allocation.

## Slide 4: Korea MSIT
Frequency band | Usage
5725-5850 MHz Fixed, Wireless detection, Mobile 5.150 5.453 | Low power wireless data communication system K37F Object detection sensor K40A Low power wireless access system including wireless LAN K37E
5925-6700 MHz Fixed Fixed satellite (Earth to Space)(Space to Earth) 5.441 5.458B | Broadcasting K151 Fixed microwave relay K151A UWB K125B Low power wireless access system including wireless LAN K37E K151D
7075-7190 MHz Fixed Mobile | Broadcasting K151 Fixed microwave relay K151A UWB K125B Low power wireless access system including wireless LAN K37E K151D

## Slide 5: Korea MSIT
Consultation on Revision of the Table of Frequency Allocation on 5 GHz and 6 GHz (cont’d)
  Proposed change to K37E:
    The frequency bands of 5150 to 5350 MHz, 5470 to 5850 MHz and 5925 to 7125 MHz are used as low power wireless devices (for wireless access systems (WAS) including wireless LANs) and apply frequency sharing technology according to the relevant ITU-R recommendations.

## Slide 6: Korea MSIT
Consultation on revised technical standards for radio equipment in 5 GHz and 6 GHz bands
  Comments due on August 24, 2020. For details:
    http://english.msip.go.kr/web/msipContents/contentsView.do?cateId=_law4&artId=2942268
  Motivation:
    To enable high-quality data service and accelerate the adoption of 5G convergence services using 5G-class unlicensed technology (e.g, WiFi 6E, 5G NR-U) in the 6 GHz band.
    NOTE – the same motivation as the previous consultation.

## Slide 7: Korea MSIT
For radio equipment in 5925-6425 MHz:
Occupied frequency bandwidth | Power density including absolute antenna gain | Remarks
0.5 MHz min 20 MHz max | 1 dBm/MHz or less | The power density including the absolute gain of the antenna should be an average value Drones are prohibited. Built-in wireless devices used in automobiles are allowed to operate in 6085-6425 MHz.
20 MHz min 40 MHz max | -2 dBm/MHz or less | 
40 MHz min 80 MHz max | -5 dBm/MHz or less | 
80 MHz min 160 MHz max | -8 dBm/MHz or less | 

## Slide 8: Korea MSIT
For indoor wireless devices in 5925-7125 MHz:
Occupied frequency bandwidth | Power density including absolute antenna gain | Remarks
160 MHz | 2 dBm/MHz or less | The power density including the absolute gain of the antenna should be an average value Limited to equipment that is installed and operated by being connected to the power in the building or connected to another equipment. Prohibited use in vehicles such as automobiles, aircraft, railroads, ships, and drones

## Slide 9: Korea MSIT
New conditions:
  Frequency tolerance deviation should be within ±20×10-6.
  Out-of-band emission should have an average power density of –27 dBm/MHz or less, including the absolute antenna gain. For peak value, it should be less than -34 dBm/MHz at a frequency outside the 5925-6425 MHz band.
  Modulation type should be digital.
  Listen before talk should be used.