## Slide 1: APAC update – November 2020
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between July and November 2020.

## Slide 3: Australia ACMA (1)
Proposed update to the Australian Radiofrequency Spectrum Plan
  Information
    https://www.acma.gov.au/consultations/2020-08/proposed-update-australian-radiofrequency-spectrum-plan-consultation-272020
    Consultation closes on September 29, 2020
  Abstract:
    The proposed changes reflect changes to the ITU Radio Regulations because of the decisions of WRC-2019. They include new identifications for IMT (mobile broadband), maritime and satellite services, some minor editorial changes and clarification of a number of Australian footnotes, and updates reflecting domestic changes that have occurred over the past four years.
    The ACMA typically updates the Spectrum Plan following each WRC.

## Slide 4: Australia ACMA (2)
Proposed update to the Australian Radiofrequency Spectrum Plan (Cont’d)
  The proposed table of frequency allocation and the associated footnotes with tracking changes is posted:
    https://www.acma.gov.au/sites/default/files/2020-08/Draft%20Australian%20Radiofrequency%20Spectrum%20Plan%202021.docx
  List of submissions publishes on November 10:
    https://www.acma.gov.au/sites/default/files/2020-11/Submissions%20to%20IFC%2027%202020.zip
  The Australian Radiofrequency Spectrum Plan 2017 remains in force until it is revoked and a new Spectrum Plan is published.

## Slide 5: Australia ACMA (3)
New arrangements for low interference potential devices
  Information:
    https://www.acma.gov.au/sites/default/files/2020-09/Variation-to-the-LIPD-Class-Licence-consultation-paper.docx
    https://www.acma.gov.au/sites/default/files/2020-09/Draft-Radiocommunications-Low-Interference-Potential-devices-Class-Licence-Variation-Notice-2020-No-1.docx
    https://www.acma.gov.au/sites/default/files/2020-09/Notice-under-subsection-136-of-Radiocommunications-Act-1992-of-proposed-variation-of-LIPD-Class-Licence-2015.docx
    Consultation closes on October 26, 2020

## Slide 6: Australia ACMA (4)
New arrangements for low interference potential devices (Cont’d)
  Abstract
    ACMA plans to introduce new arrangements to support 5G, the IoT and other new technologies related to the following spectrum bands by updating the Radiocommunications (Low Interference Potential Devices) Class Licence 2015 (a.k.a. LIPD Class License):
      Wireless broadband in the 24.25–25.10 GHz band
      IoT devices in the 928–935 MHz band and VHF high bands
      Radiodetermination devices in the 10.50–10.55 GHz band.

## Slide 7: Australia ACMA (5)
New arrangements for low interference potential devices (Cont’d)
  Of interest to us: IoT devices in the 928–935 MHz band
    The ACMA completed a review of arrangements in the 803–960 MHz band in November 2015. The ACMA is proposing to implement decisions relating to the introduction of arrangements for IoT devices in the 928–935 MHz band from the November 2015 paper in this update to the LIPD Class Licence. These arrangements will support low-power wide-area network (LPWAN) rollouts, which include a range of emerging monitoring and control technologies.

## Slide 8: Australia ACMA (6)
New arrangements for low interference potential devices (Cont’d)
  Of interest to us: IoT devices in the 928–935 MHz band (cont’d)
    Technical conditions for fixed telecommand or telemetry transmitters:
      Authorised on a non-exclusive basis.
      EIRP not to exceed 25 mW (14 dBm).
      Radiated power spectral density (PSD) not to exceed -14.5 dBm/kHz.
      A maximum duty cycle of 0.1 per cent be applied to transmitters operating under these provisions averaged over one hour on any given frequency.

## Slide 9: Australia ACMA (7)
New arrangements for low interference potential devices (Cont’d)
  Of possible interest to us: IoT devices in the VHF band
    The ACMA released the discussion paper Internet of Things Applications in the VHF High Band in July 2020. In this paper, it was proposed to establish arrangements similar to those in place in Europe for the 169.4–169.4875 MHz, 169.4875–169.5875 MHz, and 169.5875–169.8125 MHz frequency segments

## Slide 10: Australia ACMA (8)
New arrangements for low interference potential devices (Cont’d)
  Of possible interest to us: IoT devices in the VHF band
    Technical conditions for telecommand or telemetry transmitters:
      EIRP not to exceed 16.4 mW.
      ≤ 0.1 % duty cycle for 169.4–169.4875 MHz and 169.5875–169.8125
      ≤ 0.001% duty cycle except for 00:00 h to 06:00 h local time where the duty cycle limit is ≤ 0.1% for 169.4875–169.5875 MHz

## Slide 11: Australia ACMA (9)
Amendment to the Short Range Devices Standard – consultation
  Information:
    https://www.acma.gov.au/sites/default/files/2020-11/Amendments-to-the-SRD-Standard-consultation-paper.docx
    https://www.acma.gov.au/sites/default/files/2020-11/Radiocommunications-Short-Range-Devices-Amendment-Standard-2020-No-1.docx
    Consultation closes on December 18, 2020

## Slide 12: Australia ACMA (10)
Amendment to the Short Range Devices Standard – consultation (Cont’d)
  Background:
    The LIPD Class Licence authorises the operation of specified devices, while the Short Range Devices Standard regulates the technical performance of devices supplied to the Australian market.
    The Short Range Devices Standard specifies that the applicable standard for devices is either the standard listed in the LIPD Class Licence or, if no standard is listed, the Standards Australia standard “AS/NZS 4268:2012 Radio equipment and systems—Short range devices—Limits and methods of measurement”, which specifies minimum performance requirements and methods of measurement for short-range devices (AS/NZS 4268).

## Slide 13: Australia ACMA (11)
Amendment to the Short Range Devices Standard – consultation (Cont’d)
  Proposal
    To update the reference from AS/NZS 4268:2012 to AS/NZS 4268:2017
    To allow the use of international test method standards as alternatives to AS/NZS 4268 by referencing four generic ETSI standards and the FCC Rules:
      ETSI EN 300 220-1
      ETSI EN 300 330
      ETSI EN 300 440
      ETSI EN 305 550-1
      FCC Rules Title 47 (Telecommunications) Part 15-Radio Frequency Devices.

## Slide 14: China MIIT
Mandatory national standards for approval: Electromagnetic radiation exposure limit of mobile communication terminal devices
  Background
    China MIIT plans to replace the existing national standard GB 21288-2007 with GB 21288-2020, which is applicable to mobile communication terminal devices that work between 100 kHz and 300 GHz and are within 20cm of the human body when in use.
  Information:
    https://www.miit.gov.cn/zwgk/wjgs/art/2020/art_fe0b39c37fb94f15bb13c45d9e205110.html
  GB 21288-2020
    https://www.miit.gov.cn/cms_files/filemanager/oldfile/miit/n1146295/n7281310/c8113089/part/8113160.zip

## Slide 15: Japan MIC (1)
Call for opinions on the draft frequency allocation plan
  Information (consultation closes on September 18, 2020):
    https://www.soumu.go.jp/menu_news/s-news/01kiban09_02000370.html
  Abstract:
    Based on the decisions of WRC 2019, partial amendments to the ITU Charter and the Radio Regulations attached to the Convention will come into effect on January 1, 2021. Domestic changes over the past few years are also included. Main changes include:
      Frequency allocation for NAVDAT in the 415-526.5kHz band
      Frequency allocation to space operations on non-geostationary satellites for short-term missions in the 137-138MHz and 148-149.9MHz bands
      Frequency allocation for the use of VHF data exchange system on satellites
      Introduction of Iridium satellite system as a new satellite system of GMDSS.

## Slide 16: Japan MIC (2)
Call for opinions on the draft frequency allocation plan
  Decision is made on October 12, 2020, with some minor changes:
    https://www.soumu.go.jp/menu_news/s-news/01kiban09_02000381.html

## Slide 17: Korea MSIT (1)
Consultation on partial revision (draft) of “Korea Frequency Distribution Table”
  Information:
    http://english.msip.go.kr/web/msipContents/contentsView.do?cateId=_law4&artId=3001321
    Consultation closes on September 30, 2020
  Proposal:
    To revise the footnote K125B in allowing UWB communications from 3.735 to 4.8 GHz and 6.0 to 10.2 GHz to 4.2 - 4.8 GHz and 6.0 - 10.2 GHz

## Slide 18: Korea MSIT (2)
Announcement on releasing 6 GHz band for unlicensed use
  Information:
    https://www.msit.go.kr/web/msipContents/contentsView.do?cateId=_policycom2&artId=3140715
  In the announcement:
    The MCIT made an administrative notice on related technical standards in June of this year that collects opinions between June 20, 2020 and August 24, 2020.
    Anyone can freely use the entire 6 GHz indoors under 250 mW.
    Connections between devices such as tethering are in the 5925 – 6445 MHz band. It can be used without distinction between indoors and outdoors

## Slide 19: Korea MSIT (3)
RECAP: Consultation on revised technical standards for radio equipment in 5 GHz and 6 GHz bands
  Comments due on August 24, 2020. For details:
    http://english.msip.go.kr/web/msipContents/contentsView.do?cateId=_law4&artId=2942268
  Motivation:
    To enable high-quality data service and accelerate the adoption of 5G convergence services using 5G-class unlicensed technology (e.g, WiFi 6E, 5G NR-U) in the 6 GHz band.
    NOTE – the same motivation as the previous consultation.

## Slide 20: Korea MSIT (4)
RECAP: Consultation on revised technical standards for radio equipment in 5 GHz and 6 GHz bands (Cont’d)
  For radio equipment in 5925-6425 MHz:
Occupied frequency bandwidth | Power density including absolute antenna gain | Remarks
0.5 MHz min 20 MHz max | 1 dBm/MHz or less | The power density including the absolute gain of the antenna should be an average value Drones are prohibited. Built-in wireless devices used in automobiles are allowed to operate in 6085-6425 MHz.
20 MHz min 40 MHz max | -2 dBm/MHz or less | 
40 MHz min 80 MHz max | -5 dBm/MHz or less | 
80 MHz min 160 MHz max | -8 dBm/MHz or less | 

## Slide 21: Korea MSIT (5)
RECAP: Consultation on revised technical standards for radio equipment in 5 GHz and 6 GHz bands (Cont’d)
  For indoor wireless devices in 5925-7125 MHz:
Occupied frequency bandwidth | Power density including absolute antenna gain | Remarks
160 MHz | 2 dBm/MHz or less | The power density including the absolute gain of the antenna should be an average value Limited to equipment that is installed and operated by being connected to the power in the building or connected to another equipment. Prohibited use in vehicles such as automobiles, aircraft, railroads, ships, and drones

## Slide 22: Korea MSIT (6)
RECAP: Consultation on revised technical standards for radio equipment in 5 GHz and 6 GHz bands (Cont’d)
  New conditions:
    Frequency tolerance deviation should be within ±20×10-6.
    Out-of-band emission should have an average power density of –27 dBm/MHz or less, including the absolute antenna gain. For peak value, it should be less than -34 dBm/MHz at a frequency outside the 5925-6425 MHz band.
    Modulation type should be digital.
    Listen before talk should be used.

## Slide 23: Korea MSIT (7)
Consultation on the partial revision (draft) of “Korea Frequency Distribution Table”
  Information:
    http://english.msip.go.kr/web/msipContents/contentsView.do?cateId=_law4&artId=3069996
    Consultation closes on October 31, 2020
  Abstract:
    In order to update the global frequency after the decision of WRC 2019 and in consideration of domestic frequency usage conditions.
  Of possible interest to us are the following frequency bands:
    5150 – 5350 MHz , 5350 – 5850 MHz
    64 – 76 GHz (IMT)

## Slide 24: Malaysia MCMC
Usage of Personal Radio Service Device(s)
  Information
    https://www.mcmc.gov.my/skmmgovmy/files/65/6517f91b-9628-4781-a718-d315cf9c485a.pdf
  Abstract
    Effective from January 1, 2023, personal radio service device(s) operating in the 477.0125 MHz to 477.4875 MHz and 477.5250 MHz to 477.9875 MHz frequency bands will longer be permitted.
  Note
    It is the third amended notice.

## Slide 25: New Zealand RSM (1)
Dedicated spectrum band plans and licensing for unmanned aircraft
  Information
    https://www.aviation.govt.nz/assets/airspace-and-aerodromes/navigation/CAA_MBIE_Discussion_Document_Unmanned_Dedicated_Radio_Spectrum_August_2020_final.pdf
    Consultation closes on October 31, 2020.
  Abstract
    The Civil Aviation Authority (CAA), in conjunction with RSM, have a developed a position paper on opening up a new band of spectrum at 5 GHz for unmanned aircraft command and control.
    This paper looks at potential band plans, as well as access regimes for unmanned aircraft flown under civil aviation rules.

## Slide 26: New Zealand RSM (2)
Dedicated spectrum band plans and licensing for unmanned aircraft (Cont’d)
  Problem statement:
    The status quo of all Unmanned Aircraft (UA) or “Drones” operating on shared, non-protected spectrum is not sustainable.
    Currently, command and controls links for unmanned aircraft operations typically operate in the frequency ranges 2400-2483.5 MHz, 5150-5350, and 5470-5875 MHz.
  Proposal
    To move unmanned aircraft operations to part of the C-band (5030-5091 MHz).
    To examine potential licensing options to manage any dedicated spectrum.

## Slide 27: Singapore IMDA (1)
Consultation: Security Requirements for Residential Gateways
  Information:
    https://www.imda.gov.sg/regulations-and-licensing/Regulations/consultations/Consultation-Papers/2020/Security-Requirements-for-Residential-Gateways
    Consultation closes on May 15, 2020
  Proposal that is of interest to us:
    Paragraphs 4.4 (Wireless Access Protection) and 4.5 (Data Protection) maybe of interest to Wi-Fi community:
    E.g., 4.4b: The Residential Gateway shall use AES encryption, with at least WPA2 protection by default. If weaker security protection such as WEP or WPA is chosen by users, warning(s) of the higher security risk to use these encryption algorithms shall be displayed.

## Slide 28: Singapore IMDA (2)
Consultation: Security Requirements for Residential Gateways (Cont’d)
  Decision is made on October 12, 2020:
    A residential gateway can use other secure encryption algorithms including AES.
    While the setup of a guest network helps further protect the residential gateway, it may not be widely used currently by user. IMDA do not mandate for residential gateways to have this feature.
    Data elements used by residential gateways need not be encrypted as long as they are salted and hashed. IMDA will leave it to manufacturers to decide whether to encrypt the data elements.

## Slide 29: Singapore IMDA (3)
Consultation: Security Requirements for Residential Gateways (Cont’d)
  Decision paper:
    https://www.imda.gov.sg/-/media/Imda/Files/Regulations-and-Licensing/Regulations/Consultations/2020/Security-Requirements-for-Residential-Gateways/2020-10-12-RGConsultation-DecisionPaper.pdf?la=en
  Technical specification:
    https://www.imda.gov.sg/-/media/Imda/Files/Regulation-Licensing-and-Consultations/ICT-Standards/Telecommunication-Standards/Radio-Comms/IMDA-TS-RG-SEC.pdf?la=en
  Key cybersecurity requirements:
    https://www.imda.gov.sg/-/media/Imda/Files/News-and-Events/Media-Room/Media-Releases/10/Key-Cybersecurity-Requirements-by-IMDA.pdf?la=en

## Slide 30: Thailand NBTC
Public hearing on radio and television broadcasting stations that are exempt from obtaining a license
  Information:
    Link (involve Thai language in the URL)
    Consultation closes on October 16, 2020
  Proposal:
Frequency (MHz) | EIRP (watts)
500 – 2,000 | 0.5
2,000 – 300,000 | 2

## Slide 31: Vietnam MIC (1)
Legal document: “National technical regulation on wideband data transmission equipment operating in the 2.4 GHz band”
  Purpose:
    This latest national technical regulation specifies essential radio requirements and conformance test procedures for wideband data transmission equipment operating in the 2.4 GHz band. It is intended to supersede the 2011 standards.
  Information:
    https://mic.gov.vn/Pages/VanBan/14605/35_2020_TT-BTTTT.html
    https://mic.gov.vn/Upload_Moi/VanBan/QCVN-54-FINAL-.DOCX
    Date issued: November 6, 2020
    Effective date: January 7, 2021

## Slide 32: Vietnam MIC (2)
Legal document: “National technical regulation on Short Range Device (SRD) - Radio equipment to be used in the 1 GHz to 40 GHz frequency range”
  Purpose:
    This latest National technical regulation specifies essential radio requirements and conformance test procedures for licence exempt Short Range Devices (SRDs) operating in the frequency bands within the range of 1 GHz to 40 GHz.
  Note: Frequency bands of SRD are listed as follows:
    2400 – 2483.5 MHz, 5725 – 5850 MHz
    2446 – 2454 MHz
    24.00 – 24.25 GHz

## Slide 33: Vietnam MIC (3)
Legal document: “National technical regulation on Short Range Device (SRD) - Radio equipment to be used in the 1 GHz to 40 GHz frequency range” (Cont’d)
  Information:
    https://mic.gov.vn/Pages/VanBan/14604/34_2020_TT-BTTTT.html
    https://mic.gov.vn/Upload_Moi/VanBan/3.-QCVN-74-2020-SRD-1-40-GHZ-2.11.2020.DOCX
    Date issued: November 6, 2020
    Effective date: January 7, 2021