## Slide 1: APAC update – November 2021
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between September 2021 and November 2021.

## Slide 3: APT Wireless Group (1)
The 3rd Meeting of the APT Conference Preparatory Group for WRC-23 (APG23-3)
  November 8 – 13, 2021
    Virtual meeting
  Objectives:
    review the results of the APG23-2 meeting
    update APT preliminary views on WRC-23 Agenda Items based on input contributions from APT Members
    consider the progress in ITU-R Study Groups in relation to WRC-23 Agenda items, and take necessary actions as appropriate
    review the activities of other regional organizations, in particular, their preliminary views/positions with a view to fostering inter-regional cooperation

## Slide 4: APT Wireless Group (2)
The 3rd Meeting of the APT Conference Preparatory Group for WRC-23 (APG23-3)
  Objectives (Cont’d)
    review of issues related to RA-23 and develop preliminary views of APT, if any
    contribute, where necessary, to the activities of APT Preparatory Group related to PP-22 with respect to the issues relevant to the purview of the APG
    finalize review of the Working Methods of APG in relation to preparation for RA-23 and WRC-23 and submit draft amendments accordingly to the APT Management Committee
    discuss APT preparations for the ITU Inter-regional Workshop on WRC-23 Preparations.

## Slide 5: Australia ACMA
Radio local area networks (RLANs) in the 6 GHz band - consultation 37/2021
  Submission deadline: November 19, 2021
    https://www.acma.gov.au/consultations/2021-10/radio-local-area-networks-rlans-6-ghz-band-consultation-372021
  Of interest to us:
    Lower 6 GHz band/proposed update to the LIPD Class Licence
    Possibility of upper 6 GHz band/higher power RLAN devices
    Possible updates to existing LIPD arrangements for RLANs in the 5150–5250 MHz frequency band to reflect outcomes of WRC-19.

## Slide 6: China MIIT (1)
Updated regulation and technical requirements on 2400 MHz, 5100 MHz, and 5800 MHz
  Effective from January 1, 2022, and the transition period is ended on October 15, 2023:
    https://www.miit.gov.cn/zwgk/zcwj/wjfb/tz/art/2021/art_e4ae71252eab42928daf0ea620976e4e.html
    https://www.miit.gov.cn/zwgk/zcjd/art/2021/art_f9d24f82c2b24a16b357ae883f21a65e.html

## Slide 7: China MIIT (2)
Updated regulation and technical requirements on 2400 MHz, 5100 MHz, and 5800 MHz
  Of interest to us on management perspective:
    To simplify the administrative licensing process, only outdoor radio stations with higher power levels are required to get a license to be installed. Others do not need to obtain a radio station license.
    Wireless LAN equipment with the function of public network IP address allocation should support the IPv6 protocol. The IPv6 address allocation function is turned on by default.
    Radio stations (stations) that set up and use the 2400 MHz, 5100 MHz and 5800 MHz frequency bands should also comply with the relevant regulations in specific industry sectors.

## Slide 8: China MIIT (3)
Updated regulation and technical requirements on 2400 MHz, 5100 MHz, and 5800 MHz
  Of interest to us on technical perspective:
    Introduce new technical requirements for multiple antennas, e.g., the specific calculation methods of synthetic gain and shaping gain
    Update the unwanted emission limit requirements
    Introduce the requirements on interference avoidance

## Slide 9: Japan MIC
Call for opinions regarding the review of the “frequency reorganization action plan”
  Submission deadline: October 13, 2021
    https://www.soumu.go.jp/menu_news/s-news/01kiban09_02000418.html
  Of interest to us:
    MIC recommended to allocate 1 GHz for unlicensed uses by 2025. The frequency band under consideration is 6 GHz.
    MIC recommended that nearly 30 MHz spectrum is allocated for V2X by 2025. The frequency band under consideration is 5.9 GHz.
    MIC recommended to continue studying the possibility of allocating 7025 MHz to 7125 MHz band to 5G by referring to the studies of ITU-T and 3GPP.

## Slide 10: Korea MSIT
Partial revision of the frequency distribution table of Korea (No. 2021-76)
  Effective from October 8, 2021
    https://www.soumu.go.jp/menu_news/s-news/01kiban09_02000418.html
  For this latest update:
    6605 MHz – 6765 MHz and 6945 MHz – 7100 MHz are allocated for fixed repeater frequencies for broadcasting relay until further notice;
    6245 MHz – 6605 MHz and 6765 MHz to 6945 MHz are used for broadcasting relay service until further notice

## Slide 11: Malaysia MCMC
Updated mandatory standard for EMF (electromagnet field beam) from new radio communications
  Effective from November 1, 2021:
    https://www.mcmc.gov.my/skmmgovmy/media/General/pdf/PIR_Revision_MS_EMF.pdf
  Of interest to us:
    The new mandatory standard has been updated with the latest EMF exposure limits based on the International Commission’s guidelines on Non-Ionizing Radiation Protection (ICNIRP) published in 2020.
    It also refers to international benchmarks that take into account current and future technologies to strengthen aspects of implementation, monitoring and evaluation of EMF.

## Slide 12: Vietnam MIC (1)
Regulations on the list of radio equipment exempted from the license to use radio frequencies, attached technical and operating conditions
  Effective from November 28, 2021:
    https://www.mic.gov.vn/Upload_Moi/VanBan/08TT.PDF
  Of interest to us (thanks Jay for the information below):
    Addition of new equipment types including:
      Wireless charging devices in the bands of 100 – 190 kHz, 326.5 kHz, 340 kHz, 353 – 373.5 kHz, 1.64 – 1.78 MHz, 6.765 – 6.795 MHz
      LPWAN devices in the bands of 433.05 – 434.79 MHz and 920 – 923 MHz
    Addition of new frequency bands for RF products including:
      2400 – 2483.5 MHz and 5725 – 5850 MHz for remote control devices
      7238.4 – 9000 MHz for UWB devices
      5.725 – 5.850 GHz; 8.5 –10 GHz; 57– 64 GHz; 75 – 85 GHz for radio telemetry devices (Short range measurement radars installed in the tank)
      57– 64 GHz for non-specific short-range devices

## Slide 13: Vietnam MIC (2)
National technical regulation on radio access equipment operating in the 5 GHz band
  Effective from May 1, 2022:
    https://www.mic.gov.vn/Upload_Moi/VanBan/11.2021.TT-BTTTT.PDF
  Of interest to us:
    Specific operation frequency bands are as follows:
      5150 MHz – 5350 MHz
      5470 MHz – 5850 MHz
    This updated technical regulation is based on ETSI EN 300 893.

## Slide 14: Vietnam MIC (3)
National technical regulation on Short Range Device (SRD) - Radio Equipment to be used in the 40 GHz to 246 GHz frequency range
  Effective from July 1, 2022:
    https://www.mic.gov.vn/Upload_Moi/VanBan/10.2021.TT-BTTTT.PDF
  Of interest to us:
    Specific operation frequency bands are as follows:
      57 GHz – 64 GHz;
      61.0 GHz – 61.5 GHz;
      122 GHz – 123 GHz;
      244 GHz – 246 GHz.
    This updated technical regulation is based on ETSI EN 305 550.

## Slide 15: Vietnam MIC (4)
National Technical Regulation on Radar Equipment Operating in the Frequency Range 76 GHz to 77 GHz for Ground Based Vehicle
  Effective from July 1, 2022:
    https://www.mic.gov.vn/Upload_Moi/VanBan/09-TT.PDF
  Of interest to us:
    This national technical regulation specifies requirements for short-range radio equipment for ground based vehicle, for example: active cruise control systems, collision warning systems, transmitting systems, blind spot detection, parking assistance, backup assistance and other future applications.
    This updated technical regulation is based on ETSI EN 301 091 and EN 303 396.