## Slide 1: APAC update – January 2022
Author:

## Slide 2: Background
This slide deck provides a high-level overview of the activities in APAC (related to Wi-Fi and WPAN) between December 2021 and January 2022.

## Slide 3: Hong Kong HKCA (1)
Creation of a Class Licence for Regulating the Use of and Trade in 6 GHz Devices for Wireless Local Area Network and Variation to the Class Licence for Provision of Public Wireless Local Area Network Services
  Consultation closed on December 24, 2021
    https://www.coms-auth.hk/filemanager/en/content_711/cp20211126_e.pdf
  List of submissions to the consultation:
    https://www.coms-auth.hk/en/policies_regulations/consultations/completed/tele_services/index_id_2362.html

## Slide 4: Hong Kong HKCA (2)
  Summary
    HKCA proposes the maximum EIRP of 24 dBm (250 mW) for indoor use; and 14 dBm (25 mW) for outdoor use.
    HKCA proposes to update its relevant specification HKCA 1081 by referencing ETSI EN 303 687.
    HKCA notes that some countries and regions designate the entire 6 GHz band for Wi-Fi. Wi-Fi devices from these countries and regions that “could operate in the 6425 – 7125 MHz band, if illegally imported and used in Hong Kong, would cause in-band interference to the future 5G services”. In view of this, the consultation seeks public opinions to impose compulsory certification requirements for APs to ensure that “such devices to be used in Hong Kong should comply with the relevant specification (i.e. HKCA 1081), in particular that they do not operate in the 6425 – 7125 MHz band which may be used for 5G services in Hong Kong in the future.”

## Slide 5: India DoT (1)
The Use of Low Power Equipment in the Frequency Band 865-868 MHz for Short Range Devices (Exemption from Licence) Rules, 2021
  Published in the Gazette of India on December 13, 2021, and in the DoT website on December 16, 2021:
    Link
  Selected summary
    No licenses shall be required
    These rules shall not be applicable to the wireless equipment which has been type approved under the Use of low power equipment in the frequency band 865-867 MHz for (RFID) Radio Frequency Identification Devices (Exemption from Licensing Requirement) Rules, 2005, and shall be effective till the end of its life.
    Technical specifications for different types of devices are provided.

## Slide 6: India DoT (2)
The of Very Low Power Radio Frequency Devices or Equipments for Inductive Applications (Exemption from License) Rules, 2021
  Published in the Gazette of India on December 21, 2021, and in the DoT website on December 29, 2021:
    Link
  Selected summary
    No licenses shall be required for the purpose of usage of very low power radio frequency devices or equipments for Inductive Applications (including wireless charging through inductive process) in the frequency bands mentioned below, on non-interference, non-protection and shared and non-exclusive basis
    Technical specifications between 9 kHz and 30 MHz are provided in the table therein. Definitions of Inductive application are also provided.

## Slide 7: Japan MIC
Call for opinions on 2 technical reports:
  Technical conditions for 5GHz band weather radar
  Technical conditions for 9.7GHz band general-purpose weather radar
  Consultation period: January 15 ~ February 14, 2022
    Link

## Slide 8: Korea MSIT (1)
Administrative notice (2021-0931) related to a partial revision of table of frequency allocation
  Consultation period: November 17, 2021 to January 16, 2022
    Link
  Summary
    There is an increasing use of the 76–81 GHz frequency band for object detection sensors in various application fields, such as collecting biometric information.
    The proposed change is to enable radar devices to operate in the 70 GHz band by updating the domestic note K40A that allows the 76 to 81 GHz frequency band to be used for object detection.

## Slide 9: Korea MSIT (2)
Administrative notice (2021-0933) related to a partial revision of technical standards
  Consultation period: November 17, 2021 to January 16, 2022
    Link
  Summary
    It is related to the administrative notice 2021-0931 with proposed technical requirements as shown in the next page.

## Slide 10: Korea MSIT (3)
Administrative notice (2021-0933) related to a partial revision of technical standards
  Selected proposed technical requirements
    Peak power: 100mW or less (including antenna absolute gain)
    Average power density is -16 dBm / MHz
    Spurious emission limit:
      Less than 1 GHz: -36 dBm with reference bandwdith of 100 kHz
      1 GHz or larger: -30 dBm with reference bandwidth of 1 MHz
    It is prohibited to use in moving objects such as automobiles, aircraft, ships, railways.
    This device is intended for use in buildings. If it is installed within a radius of 2 km from the radio astronomical antenna, prior consultation with the observatory is required.

## Slide 11: Korea MSIT (4)
Administrative notice (2021-1009) related to a partial revision to wireless devices for wireless stations that can be open without notification
  Consultation period: December 22, 2021 to February 21, 2022
    Link
  Proposed changes are shown in red as follows:
Frequency band (MHz) | Antenna supply power density or radiated power | Notes
5925 ~ 6425 | 25mW or less | Including antenna absolute gain.
5925 ~ 6425 | 250mW or less | Wireless devices used in subway/passenger cars. Including antenna absolute gain.
5925 ~ 7125 | 250mW or less | Wireless devices used in buildings. Including antenna absolute gain.

## Slide 12: Korea MSIT (5)
Administrative notice (2021-1010) related to a partial revision to technical standards for radio equipment for radio stations that can be open without notification
  Consultation period: December 22, 2021 to February 21, 2022
    Link
  Proposed changes are shown in red as follows:
Frequency band (MHz) | Occupied frequency bandwidth | Power density including antenna absolute gain | Notes
5925 ~ 6425 | 160 MHz or less | 2dBm/MHz or less | The power density including the absolute gain of the antenna should be an average value. Limited to devices installed and operated by being connected to the power source in subway/passenger cars, or devices communicating with this device.

## Slide 13: New Zealand RSM (1)
Draft five year spectrum outlook 2022-2026
  Consultation period: November 29, 2021 to February 28, 2022
    Link
  3 main questions RSM ask for opinions:
    Have we identified the range of technological advancements and probable new demands relevant to New Zealand?
    Have we prioritised the right issues that we will need to actively manage through our work programme (to the extent this is possible to predict now)?
    Are there other matters that we should cover?

## Slide 14: New Zealand RSM (2)
Draft five year spectrum outlook 2022-2026
  Of interest to us:
    4 main technological areas and the corresponding priorities on spectrum are presented:
      Satellites
      Cellular mobile – 5G
        Page 15: RSM will continue to proactively engage in ITU, APT and international trade matters relating to spectrum including monitoring and responding to developments in the 6.425 – 7.125 GHz band for mobile and Wi-Fi.
      IoT / M2M
        Page 16: The standardisation of wireless technology is creating a trend of convergence around wireless 3GPP and IEEE standardised technologies to replace proprietary technologies and land mobile systems in some sectors.
      Private networks

## Slide 15: New Zealand RSM (3)
Draft five year spectrum outlook 2022-2026
  Of interest to us (Cont’d #2)
    Spectrum sharing
      Page 22: We will continue to monitor the demand for different tools and levers to allow more innovative approaches to spectrum sharing.
      Consider sharing models when developing future spectrum bands is one of the RSM’s planned work plan priorities
    User of higher frequencies
      Page 22: This includes the frequency ranges recently identified for mmWave 5G in the 26 GHz, 40 GHz and 66-71 GHz bands
      Page 22: There is growing interest in the use of even higher frequency ranges (eg above 100 GHz) with the latest technological advancements.
      Monitor use of multigigabit wireless systems in the 66-71 GHz range is one of the RSM’s planned work plan priorities

## Slide 16: New Zealand RSM (4)
Draft five year spectrum outlook 2022-2026
  Of interest to us (Cont’d #3)
    Licensing approaches enabling new technologies
      Consider updates to General User Licences, particularly for short-range devices and monitor developments in the use of 6 GHz for Wi-Fi 6E is one of the RSM’s planned work plan priorities
      Consider a General User Licencing regime when developing higher frequency bands is another RSM’s planned work plan priority in this category.