## Slide 1: IEEE 802.18 45 GHz Ad Hoc Proposal
Date: 2022-08-04
Authors:
August 2022
Notes: September 2012

## Slide 2: Abstract
August 2022
IEEE is an international organization, and as such should consider developing the Ultra High Reliability standard in a way that makes it universally available. There are mmWave bands that offer sufficient spectrum to support future throughput requirements that are or could be made available globally. The 45 GHz band (42.5 – 48 GHz) meets these requirements and should be included as part of the UHR SG and be supported by an Ad Hoc RR-TAG group.
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 2

## Slide 3: Executive Summary
IEEE is an international organization
In 2012, TGad was developing a 60 GHz standard in spectrum not available in China
As a result, a parallel project, TGaj was required to make this standard an international standard
The 6 GHz band is also not available in China and limited elsewhere, where the burgeoning Fiber Internet market has increasing throughput demands
The next generation after 802.11be should do its best to provide a standard that may be used globally
IEEE 802.11aj used spectrum in the 45 GHz band
IEEE 802.18 should review opportunities in mmWave bands from 24 – 71 GHz, and providing the UHR SG our findings and recommendations
August 2022
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 3

## Slide 4: Problem Statement #1
Fiber deployment is increasing and increasing potential internet speeds
  FTTR is becoming a major focus in China and elsewhere
Throughput projections will surpass 802.11be capabilities
  As they pass the 100 Mbps range, mmWave bands begin to look more suitable
  Increased use of the 6 GHz band with 320 MHz wide channels will quickly create congestion, even in 1.2GHz of spectrum; we are pushing mid-band limits
August 2022

## Slide 5: Problem Statement #2
The recent and future 802.11 standards focus on the 6 GHz band
  This band is limited to ~500 MHz in many regulatory domains
  China and other countries have no spectrum available for unlicensed use in this band
  IEEE 802.11 created the 11aj standard for operation in the 45 GHz band (CMMW) and should consider it for future 802.11 standards
  IEEE 802.11 has created two standards that operate in 60 GHz bands
mmWave band spectrum can support these requirements for years to come
  Over 5 GHz of spectrum could be made available globally in mmWave bands
August 2022

## Slide 6: mmWave Bands Ad Hoc Activities
Detailed incumbent study in 24 – 71 GHz [45 GHz and 60 GHz bands]
Determine if and where regulations may need changes
Support UHR SG mmWave band discussions and provide regulatory expert opinions on best opportunities
August 2022

## Slide 7: Motion Options (Rich, Hassan and Joe)
Move to create a RR-TAG Ad Hoc committee to study mmWave spectrum bands between 24 and 71 GHz for opportunities to provide the IEEE 802.11 Ultra High Reliability Study Group (UHR SG) with recommendations based on global availability, projected regulatory hurdles and applicability that meets the goals of the Study Group, e.g., high reliability, coverage, and throughput.
Move to create a RR-TAG Ad Hoc committee to study mmWave spectrum bands 45 GHz and 60 GHz for opportunities to provide the IEEE 802.11 Ultra High Reliability Study Group (UHR SG) with recommendations based on global availability, current/projected regulatory status and applicability that meets the goals of the Study Group.
Move to create a RR-TAG Ad Hoc committee to study mmWave spectrum bands between 24 and 71 GHz to provide insight on global availability and projected regulatory hurdles for these bands. The resulting study should be provided to the IEEE 802.11 Ultra High Reliability Study Group (UHR SG) and other 802 WGs to increase their understanding of available mmWave spectrum.
Move to create a RR-TAG Ad Hoc committee to study mmWave spectrum bands 45 GHz and 60 GHz to provide insight on global availability and current/projected regulatory status for these bands. The resulting study should be provided to the IEEE 802.11 Ultra High Reliability Study Group (UHR SG) and other 802 WGs to increase their understanding of available mmWave spectrum.

## Slide 8: Motion
Moved by:
Seconded by:
Vote: Y N A

## Slide 9: References
US FCC Table of Frequencies
  https://transition.fcc.gov/oet/spectrum/table/fcctable.docx
European Table of Frequency Allocations
  https://docdb.cept.org/download/2ca5fcbd-4090/attachments/2013_ERCRep025.pdf
  ECO Frequency Information System (cept.org)
ITU-R Radio Regulations
  https://www.itu.int/pub/R-REG-RR
August 2022