## Slide 1: IEEE 802.18 RR-TAG Update UWB Regulation Framework in Europe
Date: 08 July 2023
Authors:

## Slide 2: Status of UWB regulation
New regulation framework presented in November 2022 in Bangkok (IEEE 802.18-22/0141) in force as ECC decision (06)04
CEPT Report 84 has been published and transferred to the EU commission as part of the permanent UWB mandate of the EU commission to CEPT
Updated EC decision expected including enhancements in the band 6.0 GHz to 8.5 GHz until end of 2023
No significant changes to sensor regulation expected since ECC decision (07)01 has not be rework on ECC level
New period of UWB regulation update start by end 2023

## Slide 3: Main points of new regulation 2022 (ECC/DEC/(06)04)
Vehicular application in the band 6.0 GHz to 8.5 GHz
Fixed outdoor in the band 6.0 GHz to 8.5 GHz
Indoor applications up to -31.3dBm/MHz when connected to networked
Some duty cycle and antenna limitations apply

## Slide 4: New activities in Europe towards an extended UWB framework up to 10.6 GHz 07/2023
4

## Slide 5: New investigation in SE24 towards band extension
LS from WGFM to WGSE to start investigations: https://cept.org/Documents/wg-fm/78560/fm-23-082annex43_ls-to-wg-se-on-uwb-in-85-106-ghz
Band extension work to include band 8.5 GHz to 10.6 GHz including:
  Fixed out-door
  In-door with -31,3dBm/MHz
  Vehicular applications
Outdoor usage might be controversial due to X-Band radar systems civil and military
Indoor seems to be less of an issue

## Slide 6: Other topics for next regulation update cycle
Update sensor regulation ECC/DEC/(07)01 to include the 2023 generic possibilities
  Increased indoor power
  Fixed out-door with some operational limitations (and “re-consider” options from former versions of ECC/DEC/(07)01)
Investigate possible fixed in-door in the band 4.2 GHz to 4.8 GHz
  Initial work on SRDoc in ETSI has started: https://portal.etsi.org/webapp/WorkProgram/Report_WorkItem.asp?WKI_ID=63521

## Slide 7: UWB in ETSI
ERM TGUWB is working on a set of UWB related harmonized standards
  https://portal.etsi.org/tb.aspx?tbid=729&SubTB=729#/
Main topic:
  measurements under environmental profile conditions
  https://portal.etsi.org/webapp/WorkProgram/Report_WorkItem.asp?WKI_ID=67490
Next meeting #65: 5. Sept – 9. Sept 2023, online