## Slide 1: Unofficial translation of selected contents of the Thailand NBTC’s consultation on 6 GHz
Date: 6 April 2024
Author:

## Slide 2: Disclaimer
The contents presented in this slide deck are the author’s unofficial translation of selected contents of the Thailand NBTC’s consultation “Draft amendment to technical standards for telecommunications equipment and equipment using the frequency 5.925 – 6.425 GHz”. It is a public consultation that asks for public opinions on the proposed updates to the Technical standards of telecommunications equipment and equipment, NBTC MT. 1039 - 256X, Radio communications equipment that uses the frequency 5.925 - 6.425 gigahertz.
Please refer to the administration’s website for the exact contents (in Thai) of the consultation.

## Slide 3: Change in Section 2.1.1 (Maximum EIRP)
Maximum transmit power (mW) | Spectral density value (mW/MHz) | Terms of use
250 | 12.5 | Inside the building
25 | 1.25 | Inside and outside the building
Maximum transmit power (mW) | Spectral density value (mW/MHz) | Terms of use
250 | 12.5 | Inside the building
25 | 1.25 | Inside and outside the building
25 | 12.5 | Inside and outside the building For channel bandwidth no more than 20 MHz
Existing requirements:
Proposed changes:
Notes: ,

## Slide 4: Change in Section 2.1.2 (Other technical characteristics of the transmitting and receiving sectors)
In addition to the existing reference of FCC Part 15.407, the following reference is added:
  ETSI EN 303 687 V1.1.1 or newer version
Notes: ,