## Slide 1: Selected aspects of radio spectrum management and regulation in the Republic of Poland
Date: 14 May 2024
Author: Mariusz Gruszczyński
Notes: September 2012

## Slide 2: Content
Short introduction about UKE
Nationwide broadband mobile networks
Local/private broadband mobile networks
Current and planned frequency resources for 5G networks
Unlicensed radio spectrum for wideband data transmission devices
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 2

## Slide 3: The President of UKE - regulatory authority
Main tasks of the President of UKE:
  analysis, regulation and monitoring of the telecommunications market,
  management of radio spectrum,
  management of numbering resources,
  control of fulfilling electromagnetic compatibility requirements,
  analysis, regulation and monitoring of the postal market.
Mission of the President of UKE:
  provide citizens with access to modern telecommunications and postal services on a developing market and in a dynamic international environment.
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 3

## Slide 4: The President of UKE - radio spectrum management
Frequency allocation
National coordination
International coordination
Radio licencing
Spectrum auctions
Spectrum sharing
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 4

## Slide 5: Nationwide broadband mobile networks - overview
MNO | Sum of allocated radio spectrum in the frequency bands [MHz] |  |  |  |  |  |  |  | Sum of allocated radio spectrum [MHz] | Share in total allocated radio spectrum [%]
 | 420 (-) | 800 (B20) | 900 (B8) | 1800 (B3) | 2100 (B1) | 2600 (B7) | 2600 (B38) | 3600 (B78) |  | 
P4 | - | 10 | 10 | 30 | 30 | 40 | - | 100 | 220 | 22,35
Polkomtel | 5 | - | 28 | 59,6 | 30 | 40 | 50 | 100 | 312,6 | 31,76
T-Mobile | - | 20 | 18 | 40 | 30 | 30 | - | 100 | 238 | 24,18
Orange | - | 20 | 13,6 | 20 | 30 | 30 | - | 100 | 213,6 | 21,70
Total: | 5 | 50 | 69,6 | 149,6 | 120 | 140 | 50 | 400 | 984,2 | 100,00
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 5

## Slide 6: Nationwide broadband mobile networks - technologies
2G
900 MHz (B8)
3G
900 MHz (B8)
4G
800 MHz (B20)
5G
2100 MHz (n1)
1800 MHz (B3)
2100 MHz (B1)
900 MHz (B8)
1800 MHz (B3)
2100 MHz (B1)
2600 MHz (both)
2600 MHz (n38)
3600 MHz (n78)
420 MHz
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 6

## Slide 7: 5G private networks in 3800-4200 MHz band (n77)
WBB LMP systems terrestrial wireless broadband systems providing local-area network
local and private networks area of maximum 20 municipalities
prohibition on extending the coverage or capacity of other networks
standalone isolated networks no sharing of radio equipment and frequency resources is allowed between the local network and: (1) other local networks operating in the 3800-4200 MHz band (2) public telecommunications networks
3800-3900 MHz | 3900-4000 MHz | 4000-4100 MHz | 4100-4200 MHz
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 7

## Slide 8: 5G private networks in 3800-4200 MHz band (n77)
individual radio licences „first come, first served” principle, no frequency licence
maximum expiration date: 2028-12-31 pending the issuance of CEPT regulations (probably in 2025)
channel blocks with multiples of 10 MHz (1) the minimum spectrum width is 10 MHz, the maximum is 100 MHz (2) spectrum limitation to 100 MHz per user
low-power and medium-power radio licences
3800-3900 MHz | 3900-4000 MHz | 4000-4100 MHz | 4100-4200 MHz
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 8

## Slide 9: 5G private networks in 3800-4200 MHz band (n77)
3800-3900 MHz | 3900-4200 MHz
for local self-government units | for other entities for local networks used in standalone private networks and for fixed wireless access (FWA) services
only for local non-public network | the ability of providing telecommunications services
C-band protection | radio altimeters protection
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 9

## Slide 10: Current frequency resources for 5G
3600 MHz (n78)
~ 4 211
P4
Orange
T-Mobile
Polkomtel
2100 MHz (n1)
~ 24 260
P4
Orange
T-Mobile
Polkomtel
2600 MHz (n38)
~ 4 019
Polkomtel
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 10

## Slide 11: Planned frequency resources for 5G - 700 MHz (n28)
IoT
PMSE
703-733 MHz (UL)
758-788 MHz (DL)
PPDR
M2M
SDL
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 11

## Slide 12: Potential interference in 700 MHz band (n28)
Channel 50
Channel 52
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 12

## Slide 13: Planned frequency resources for 5G - 26 GHz (n258)
200
200
200
200
200
200
200
200
200
200
200
200
200
24.3 GHZ
26.5 GHZ
25.5 GHZ
200
5G
GOV
CIVIL
CIVIL/GOV
200
200
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 13

## Slide 14: Unlicensed radio spectrum for wideband devices
No. | Frequency band | Power / Magnetic Field | Additional notes
1 | 863-868 MHz | 25 mW e.r.p. | Occupied bandwidth > 600 kHz and ≤ 1 MHz. This set of usage conditions is only available for wideband short range devices in data networks.
2 | 2400-2483.5 MHz | 100 mW eirp and 100 mW/100 kHz e.i.r.p. density applies when frequency hopping modulation is used, 10 mW/MHz e.i.r.p. density applies when other types of modulation are used. | For wideband modulations other than FHSS, the maximum e.i.r.p. density is limited to 10 mW/MHz.
3 | 5150-5250 MHz | 200 mW e.i.r.p. and 10 mW/MHz e.i.r.p. density. Exceptions: - 40 mW maximum mean e.i.r.p. applies for installations inside train carriages with an attenuation loss on average of less than 12 dB; - 40 mW maximum mean e.i.r.p. applies for installations inside road vehicles. | Indoor use, including installations inside road vehicles, trains and aircraft, and limited outdoor use. Use by Unmanned Aircraft Systems (“UAS”) is limited to within the 5170-5250 MHz band.
4 | 5250-5350 MHz | 200 mW e.i.r.p. and 10 mW/MHz e.i.r.p. density. | Indoor use: inside buildings only. Installations in road vehicles, trains and aircraft are not permitted. Outdoor use is not permitted.
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 14

## Slide 15: Unlicensed radio spectrum for wideband devices
No. | Frequency band | Power / Magnetic Field | Additional notes
5 | 5470-5725 MHz | 1 W e.i.r.p. and 50 mW/MHz e.i.r.p. density. Exceptions: - 200 mW maximum mean e.i.r.p. applies for installations in road vehicles. | Indoor and outdoor use. Installations in road vehicles are permitted only for WAS/RLANs devices operating in slave mode controlled by a fixed WAS/RLANs device with Dynamic Frequency Selection (DFS) functionality operating in master mode. Installations in trains and aircraft and use for UAS are not permitted.
6 | 5945-6425 MHz | 23 dBm e.i.r.p., 10 dBm/MHz e.i.r.p. density and -22 dBm/MHz e.i.r.p. density for out-of-band emission below 5935 MHz. | Restricted to indoor use, including in trains with metalcoated windows and aircraft. Outdoor use, including in road vehicles, is not permitted.
7 | 5945-6425 MHz | 14 dBm e.i.r.p., 1 dBm/MHz e.i.r.p. density and -45 dBm/MHz e.i.r.p. density for out-of-band emission below 5935 MHz. | Indoors and outdoors. Use on UAS is not permitted.
8 | 57-71 GHz | 40 dBm e.i.r.p. and 23 dBm/MHz e.i.r.p. density. | Fixed outdoor installations are not allowed.
9 | 57-71 GHz | 40 dBm e.i.r.p., 23 dBm/MHz e.i.r.p. density and maximum transmit power of 27 dBm at the antenna port or ports. | -
10 | 57-71 GHz | 55 dBm e.i.r.p., 38 dBm/MHz e.i.r.p. density and a transmit antenna gain ≥ 30 dBi. | This set of usage conditions is only available to fixed outdoor installations.
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 15

## Slide 16
Thank you for your attention!
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 16