## Slide 1: Coexistence architecture of 802.19.1
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2010-01-19
Authors:

## Slide 2: Introduction
This presentation is intended to facilitate discussion about the architecture of IEEE 802.19.1 TV White Space coexistence standard
The presentation starts with an overview of the design assumptions and objectives
That will be followed by a list of functional objectives
Next a reference model example is shown
That’s followed by a list of functional elements
  What’s meant with each element?
  What could they comprise of?
A summary slide will close the presentation

## Slide 3: Design assumptions and objectives
This presentation builds upon two assumption
  Collaborative coexistence
    TVWS networks and devices collaborate for efficient spectrum usage; communication between different players assumed
  Distributed decision making
    Spectrum usage decisions made in the TVWS networks and devices; no external decision making entity assumed
On the other hand we believe that the standard needs to specify a logical entity in a TVBD to facilitate coexistence management
  Rest of the presentation provides a view to such an entity

## Slide 4: Protocol view on coexistence for WS radios
Multiple independent 802 stations using the 802.19.1 coexistence support
Devices communicate with each others about coexistence
SMEs implement the agreements on spectrum use by using existing management SAPs
=> Coexistence standard that doesn’t specify WS radio specific methods
802.11
WS
MAC+PHY
SME
802.x
WS
MAC+PHY
SME
802.19 Coexistence Support
802.22
WS
MAC+PHY
SME
Specific
Generic
I.F.
SME
LTE / Scheduled radios
Communication for coexistence

## Slide 5: Reference model example
We believe the standard needs a logical entity to take care of coexistence in TVWS
  It’s a kind of generic extension to the device’s SME with CEX_MGMT_SAP as the interface
  Communication with peer instances happens through the CEX_COMM_SAP
PHY
MAC
LLC, CS, etc.
PHY_SAP
MAC_SAP
SME
Coexistence Entity (CEE)
LLC_SAP, etc.
CEX_MGMT_SAP
CEX_COMM_SAP

## Slide 6: Elements of the coexistence entity
Coexistence communication (CEX_COMM_SAP)
Neighbor discovery
Trust
Open/Close channel
Send/Publish
Coexistence management
Protocol
  Requests to peer instances
    Which requests?
  Indications to peer instances
    Which indications?
Decision making, etiquette
Local commands and events
Time base management
Support function to provide common time base

## Slide 7: Coexistence management (1/2)
Coexistence management entity enables efficient use of available spectrum
  It’s the core of the 802.19.1 specification
Essential elements of the coexistence management are
  Common language for coexistence communication – Protocol
    Information for decision making
  Common rules for coexistence decisions – Etiquette
    Decisions on operating parameters as per the available information
  Means to communicate with the local SME
    Implementation of the decisions

## Slide 8: Coexistence management (2/2)
It provides functionalities such as
  Spectrum sensing – etiquettes for spectrum sensing and mechanisms for collaborative spectrum sensing with neighbors.
    Example signaling: Sensing_ind (sensing results), Sensing_config_req (silence periods, band, channels), Sensing_config_resp(used sensing times, band, channels)
  Spectrum sharing – etiquettes for spectrum use and mechanisms for spectrum use negotiations.
    Example signaling: Resource_use_ind (ID, band, channel, utilization, priority)
  Policy discovery – mechanisms to determine and discover policies used by a network or applied in the area.
    Example signaling: Policy_ind (band, channel, regulation, tx_power, duty_cycle, timing_structure)
  SME management – mechanisms to discover and control station parameters which affect coexistence, e.g. operating frequencies.

## Slide 9: Coexistence communication
Coexistence communication entity provides basis for the coexistence protocol
It comprises of following kind of elements
  Peer/neighbor discovery
    How to find peer instances to coexist with?
  Trust
    What are the basis of trust? Secured communication? Certification?
  Communication channel management
    What kind of communication is needed? Always available? Active push or on request only?
  Messaging functionality

## Slide 10: Time base management
Time base management is a support function that provides common time view to different parties
  Neighboring networks and devices have a form of common clock
Common time base is the enabler for different kind of time based coexistence functions
  Silence periods to perform primary detection (sensing)
  Time sharing a channel between neighbors

## Slide 11: SAPs for coexistence
The two interfaces in the proposed reference model are the minimum to provide means for communication and decision making
  Logical interfaces with set of primitives
CEX_MGMT_SAP
  Contains everything that is needed to implement coexistence decisions in a STA
CEX_COMM_SAP
  Contain everything that is needed to manage communication paths with peer STAs and to exchange coexistence protocol messages with them

## Slide 12: Summary
The presentation provided a view to coexistence architecture of 802.19.1
A reference model example was presented to facilitate discussions on architecture and functional requirements