## Slide 1: High Level Architecture View
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2010-02-04
Authors:

## Slide 2: Abstract
This presentation has been submitted to the Architecture and Assumptions ad hoc group for discussion. The intent is to facilitate development of the System Design Document (SDD) the 802.19.1 TG agreed to prepare before starting work on specification.
Proposed elements and interfaces have been designed to enable both centralized and distributed decision making.

## Slide 3: Acronyms Used in the Presentation
AP | Access Point
CE | Coexistence Enabler
CM | Coexistence Manager
SME | Station Management Entity
SDD | System Description Document
TVBD | Television Band Device
WS | White Space

## Slide 4: Logical Elements and Interfaces
Logical Elements
  Coexistence Manager
  Coexistence Enabler
Interfaces
  Interface A
  Interface B
  Interface C
  Interface C’
External Elements
  WS Database
  SME
Coexistence Manager
Coexistence Enabler
Interface B
WS Database
Interface C’
Coexistence Manager
Interface C
802.19.1 Scope
SME
Interface A

## Slide 5: Logical Elements
Coexistence Manager (CM)
  Makes decisions on operation parameters of TVBD networks/devices it serves to facilitate coexistence
  Can serve multiple Coexistence Enablers, i.e. can be interfaced to multiple Coexistence Enablers
    Every 802.19.1 compliant TVBD network/device is served by one CM only
Coexistence Enabler (CE)
  Implements decisions from the Coexistence Manager
  Provides operational parameters etc. to the Coexistence Manager
  Every 802.19.1 compliant TVBD network/device has a Coexistence Enabler
    One-to-one mapping between a TVBD network/device and a CE

## Slide 6: Logical Interfaces (1/3)
Interface A
  Interface between a CE and a SME
  Provides means for the CE to
    Acquire information about radio resource usage and needs of the TVBD network/device
    Affect on the operational parameters of the TVBD network/device
  Used to exchange information like
    Radio resource usage and needs
    Radio environment
  Note
    Not sure if we need to specify this in the details like the other interfaces

## Slide 7: Logical Interfaces (2/3)
Interface B
  Interface between a CM and CE(s)
  Used by the CE to provide information about radio resource usage and needs of the TVBD network/devices
  Used by the CM to give coexistence commands to CE’s it serves
  Used to exchange information like
    Radio resource usage and needs of the TVBD networks/devices served by the CM (CE => CM)
    Radio environment (CE => CM)
    TVBD network/device operational parameters (CM => CE)

## Slide 8: Logical Interfaces (3/3)
Interface C
  Interface between CM’s
  Used for coexistence communication between CM’s
  Used to exchange information like
    Radio resource usage and needs of the TVBD networks/devices served by the CM
    Radio environment
Interface C’
  Interface between a CM and a WS Database
  Used at least for WS Database access but possibly also e.g. to open communication channels in the Interface C
  Note
    The reason for noting this interface with C’ is that from high level perspective this interface is very much like the Interface C between CM’s; message content differs but same transport should be applicable

## Slide 9: A Few Deployment Examples
Distributed Approach
Centralized Approach
Spectrum mgmt entity
CM
Device
(e.g. AP)
CE
Device
(e.g. AP)
CE
Device
(e.g. AP)
CE
Device
(e.g. AP)
CE
CM
Device
(e.g. AP)
CE
CM
Device
(e.g. AP)
CE
CM
Device
(e.g. AP)
CE
CM
All interfaces are not mandatory in all deployment scenarios.
SME interfaces are not visible in these pictures.
WS Database
WS Database

## Slide 10: Summary
In this submission we propose a high level architecture view for 802.19.1 SDD
  Logical elements
  Logical interfaces
  External elements as basic assumptions
The proposed architecture allows for both distributed and centralized decision making
  A few exemplary deployment scenarios presented to illustrate this