## Slide 1: P802.19.1 System Architecture
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2009-03-05
Authors:
Name | Company | Address | Phone | email
Päivi Ruuska | Nokia | Itämerenkatu 11-13, 00180 Helsinki, Finland | +358-50-4835433 | paivi.m.ruuska@nokia.com
Mika Kasslin | Nokia | Itämerenkatu 11-13, 00180 Helsinki, Finland |  | 
Juha Salokannel | Nokia | Itämerenkatu 11-13, 00180 Helsinki, Finland |  | 
Ha Nguyen Tran | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | 
M. Aziz Rahman | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | 
Stanislav Filin | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | 
Chen Sun | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | 
Yohannes D. Alemseged | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | 
Gabriel Villardi | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | 
Tuncer Baykas | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | 
Hiroshi Harada | NICT | 3-4, Hikarino-oka, Yokosuka, Kanagawa, Japan, 239-0847 |  | 

## Slide 2: Abstract
This contribution proposes P802.19.1 System Architecture.
It describes logical entities and their interfaces to enable coexistence on TVWS.

## Slide 3: Acronyms Used in the Presentation
AP | Access Point
CDB | Coexistence Database
CE | Coexistence Enabler
CM | Coexistence Manager
TVBD | Television Band Device
WS | White Space

## Slide 4: System Architecture
Logical entities
  Coexistence Manager
  Coexistence Enabler
  Coexistence Database
Interfaces
  Interface A
  Interface B1
  Interface B2
  Interface B3
  Interface C
  Interface D
External element
  TVWS database
  TVBD network or device
Coexistence Manager
Coexistence Enabler
Interface B1
Coexistence Manager
Interface B3
802.19.1 Scope
TVBD network or device
Interface A
Coexistence Database
TVWS Database
Interface B2
Interface C
Interface D

## Slide 5: Logical Entities
802.19.1 logical entity
  IEEE 802.19.1 logical entity is defined by its functional role(s) and interfaces with other IEEE 802.19.1 logical entities and with external elements
  Three types of logical entities are defined
    Coexistence Enabler (CE)
    Coexistence Manager (CM)
    Coexistence Database (CDB)

## Slide 6: Logical Entities
Coexistence Enabler (CE)
  Functions related to the functional role of the entity
    Obtain information, required for coexistence, from TVBD network or device
      This includes configuration and control of measurements performed by TVBD network or device
    Provide reconfiguration commands and control information, corresponding to coexisting decisions received from CM, to TVBD network or device
  Functions related to the interfaces of the entity
    Obtain information required for coexistence from TVBD network or device (interface A)
    Provide information required for coexistence to CM (interface B1)
      information obtained from TVBD network or device
    Obtain coexistence commands and control information from CM (interface B1)
    Provide reconfiguration commands and control information to TVBD network or device (interface A)
      commands and control information corresponding to coexisting commands and control information received from CM

## Slide 7: Logical Entities
Coexistence manager (CM)
  Functions related to the functional role of the entity
    Coexistence decision making
      This includes generating and providing corresponding coexistence commands and control information to CE(s)
    Discovery of other CMs
    Supporting exchange of information required for coexistence among CMs
  Functions related to the interfaces of the entity
    Provide information required for discovery to CDB, i.e. registration in CDB (interface B2)
    Obtain information required for discovery from CDB (interface B2)
    Obtain information required for coexistence from CE (information obtained by CE from TVBD network or device) (interface B1)
    Provide information facilitating coexistence to CDB (information received from CE(s)) (interface B2)
    Obtain information facilitating coexistence from CDB (e.g. information provided to CDB by other CMs) (interface B2)
    Obtain information required for coexistence from TVWS DB (information on available TV channels) (interface C)
    Provide coexistence commands and control information to CE (interface B1)
    Exchange information and control messages required for coexistence with other CM(s) (interface B3)

## Slide 8: Logical Entities
Coexistence Database (CDB)
  Functions related to the functional role of the entity
    Support discovery of CMs by each other
      Facilitates opening interface between CMs which need to exchange information due CEs they serve
    Contain information facilitating coexistence and provide it to CM
      This includes data storage, data processing, etc
  Functions related to the interfaces of the entity
    Provide information required for discovery to CM (interface B2)
    Obtain information required for discovery from CM (registration information) (interface B2)
    Obtain information required for coexistence from TVWS DB (information on available TV channels) (interface D)
    Obtain information facilitating coexistence from CM (information provided to CM by CE(s)) (interface B2)
    Provide information facilitating coexistence to CM (e.g. information provided to CDB by other CMs) (interface B2)

## Slide 9: Interfaces
802.19.1 defines three groups of interfaces
  Interface between 802.19.1 entities
    Interface B1
    Interface B2
    Interface B3
  Interface between an 802.19.1 entity and TVWS network/devices
    Interface A
  Interface between an 802.19.1 entities and TVWS database
    Interface C
    Interface D
Different interfaces in each group are distinguished by their usage, types of information exchanged, and underlying protocols

## Slide 10: Interfaces
Interface between 802.19.1 entity and TVBD network or device
  A: CE-TVBD network or device
    From TVBD network or device to CE
      Information required for coexistence
    From CE to TVBD network or device
      Reconfiguration commands and control information (corresponding to coexistence commands and control information received from CM)
      Commands related to control of measurements performed by TVBD network or device

## Slide 11: Interfaces
Interface between 802.19.1 entities
  B1: CE-CM
    From CE to CM
      Information required for coexistence (information obtained from TVBD network or device)
    From CM to CE
      Coexistence commands and control information

## Slide 12: Interfaces
Interface between 802.19.1 entities
  B2: CM-CDB
    From CM to CDB
      Information required for discovery (obtained by this CM)
      Information required for coexistence (obtained by this CM)
    From CDB to CM
      Information required for discovery (obtained by other CMs)
      Information required for coexistence (obtained by other CMs)

## Slide 13: Interfaces
Interface between 802.19.1 entities
  B3: CM-CM
    Between different CMs
      Information and messages required for discovery and coexistence

## Slide 14: Interfaces
Interface between 802.19.1 entities and TVWS DB
  C: CM-TVWS DB
    From TVWS DB to CM
      Information required for coexistence (information on available TV channels)

## Slide 15: Interfaces
Interface between 802.19.1 entities and TVWS DB
  D: CDB-TVWS DB
    From TVWS DB to CDB
      Information required for coexistence (information on available TV channels)

## Slide 16: Summary
This contribution proposes high level system architecture for 802.19.1 SDD.
It describes logical entities and their interfaces to provide coexistence for TVBD networks and devices
The architecture supports various coexistence deployments scenarios.