## Slide 1: Output power management for TVWS network coexistence
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2010-11-08
Authors:
Name | Company | Address | Phone | email
Ryo Sawai | Sony corporation | 5-1-12, Kitashinagawa, Shinagawa-ku, Tokyo, 141-0001, Japan |  | Ryo.Sawai@jp.sony.com
Ryota Kimura | Sony corporation |  |  | Ryota.Kimura@jp.sony.com
Naotaka Sato | Sony corporation |  |  | Naotaka.sato@ieee.org
Guo Xin | Sony China |  |  | 

## Slide 2: Introduction
Proposed IEEE P802.19.1 service models, mechanisms and its algorithms(*1) on output power management for TVWS network coexistence are highlighted here.
(*1) The explanation is in section 7.2 of reference [1]

## Slide 3: Service model #1 Maximum output power allocation service
This service provides the maximum output power allocation for TVDBs to protect the incumbent service, such as TV broadcasting and wireless microphone service, from the aggregated interference due to simultaneous transmission of neighbour TVWS networks which are independently operated each other.
    The topics on aggregated interference problems from multiple WSD (White Space Device =TVBD)s in-block (= co-channel) and out-of-block (neighbor channel) emission in TVWS operation have been discussed in CEPT SE43[2].
    Also for a TVWS operation where fixed output power level approach in FCC is adopted, the TVBDs shall care about this problem from a viewpoint of incumbent service protection[3]-[5].

## Slide 4: Service model #2 Information service on aggregated interference power level
This information service provides the interference power level on each operable TVWS channel for each TVBD.
    This interference level information will be helpful for the channel selection for TVWSs.
    Because the master TVBD(s) of a TVWS network may be able to find adequate channel(s) from its operable frequency channel(s) without large system overhead due to spectrum sensing deployment, if the master TVBD knows its minimum network requirements such as required link quality, network coverage and so on.

## Slide 5: Basic criterion to specify output power of TVBDs
Aggregated mutual interference power in a co-channel operation among TVBDs for target channel #
Aggregated mutual interference power in neighbour channel operation among TVBDs for target channel #
Maximally allowed interference level in a reference point
Required received signal power of a incumbent service (i.e. broadcasting and wireless microphone and so on) receiver
Minimum required SIR (Signal to Interference Ratio) level of incumbent service receiver
Interfere-victim Reference point
Maximally allowed interference level of broadcasting service receiver

## Slide 6: Parameters (1)
Parameter | Notes
 | Maximally allowed interference level to the incumbent service (i.e. broadcasting and wireless microphone and so on) receiver in interfere-victim reference point # for the frequency channel #
 | Maximum permitted EIRP of TVBD # for frequency channel # . This maximum value may be different from the other TVBD(s) according to its location. In a case where some fixed output power levels are defined like FCC rule, predetermined value(s) for all the TVBDs may be set in this parameter.
 | Path loss between TVBD # and interfere-victim reference point # for frequency channel #
 | Maximum permitted EIRP of TVBD #( or ) for frequency channel #( or )
 | Path loss between TVBD #( or ) and the interfere-victim reference point # for frequency channel #( or )
 | Total gain of TVBD #( or ) for frequency channel #( or ). Antenna gain, antenna beam pattern and so on are given in the example parameters
 | Total loss of TVBD# for adjacent frequency channel# for the target frequency channel # . Adjacent channel selectivity, adjacent channel leakage ratio and so on are given in the example parameters.
 | Number of TVBD(s) which may use the target frequency channel #( ) simultaneously
 | Number of TVBD(s) which may use the target frequency channel #( ) simultaneously
 | Number of neighbour channel(s) for the target frequency channel # being considered in calculating aggregated mutual interference power level

## Slide 7: Parameters (2)
Selection criterion of target TVBD(s)
  The system may only have to consider (active) master TVBD(s) coordinate each (active) TVWS network in the selection of this target TVBD.
Selection criterion of positioning information of the target master TVBD(s)
  The positioning information of the target TVBD may be the one of the closest slave TVBD or virtual slave TVBD in its network coverage area for the protected contour of incumbent service, if the interference signal in the reference point caused by the transmission of the slave TVBD is larger than the interference signal caused by the transmission of the master TVBD according to these transmission parameters. The “virtual” means here that a slave TVBD is assumed to be in the edge of network coverage area of the master TVBD. In these cases, the transmission parameters of the slave TVBD are used for this calculation step, the reference point of the slave node should be each closest point for the protected contour of the incumbent service.
Counting policy of M, N and O
  These numbers may count only active TVWS network coordinated by each active master TVBD.

## Slide 8: Margin based approach in specifying the maximum output power of TVBDs
Parameter | Notes
 | Definition of MI (Multiple Interference margin) in the section 4.3 of reference [1]: “Multiple interference margin of 3-6 [dB] (depending on the number of the interfaces) that takes account of aggregated interference from multiple (co-channel and adjacent channel ) WSD(White Space Device)s operating in a given area at the same time (3 dB corresponds to 2 interferes, 5 dB – 3 interfaces, 6 dB – 4 interfaces).”
 | SM (Safety Margin) means the margin for some estimation errors such as path loss, interference power level and so on.
Calculation methods
Parameters
If the target TVBD uses the same channel as the usage channel(s) of interfere-victim receiver in the reference point
If the target TVBD uses the different channel with the usage channel(s) of interfere-victim receiver in the reference point,

## Slide 9: Maximized approach of TVWS network capacity in specifying the maximum output power of TVBDs
Step 0:
The parameters for each TVBD to calculate the equation in Slide 5 are input.
Step 1:
Calculation of local specific maximum output power of TVBD(s) without considering
mutual interference effects on in-block/out-of-block interference signal from the other
TVBD(s). The criteria for the calculation are summarized in Appendix (1).
Step 2:
Recalculation of local specific power for each TVBD with the in-block/out-of-block interference
effects from the other TVBD(s), which could be calculated based on the results ( Ptx ) of step 1
for each TVBD, in the following form (7.11) in Appendix (3)
Step 3:
Some interference margin due to the degradation of each may be in the step 2. Therefore, in this
step, the most severe interfere-victim reference point to adjust the maximum output power of
TVBDs is chosen according to the criteria in Equation (7.12) in Appendix (3)
Step 4:
Calculation of output power adjustment value to fulfil the interference margin for each TVBD in
the criteria in Equation (7.13) in Appendix (4)
Step 5:
The final results of local specific maximum output power of TVBDs are calculated in the
Equation (7.15) in Appendix (4).
Proposed procedures

## Slide 10: Pros./cons.
Margin based approach in specifying the maximum output power of TVBDs
  Pros.: Easy to calculate
  Cons.: Network capacity of each TVWS network permanently decreases, because of its excessive margin setting
Maximized approach of TVWS network capacity in specifying the maximum output power of TVBDs
  Pros.: Maximized network capacity of each TVWS network permanently can be obtained
  Cons.: Burden for the calculation overhead

## Slide 11: Conclusions
Proposed IEEE P802.19.1 service models, mechanisms and its algorithms on output power management for TVWS network coexistence were summarized.

## Slide 12: References
      [1] “19-10-0145-00-0001-coexistence-mechanism-and-its-algorithm”, IEEE mentor, October 2010
[2] “Technical and operational requirements for the possible operation of cognitive radio systems in the ‘White Spaces’ of the frequency band 470-790MHz”, DRAFT ECC Report 159, October 2010.
[3] “19-10-0101-00-0001-expectation-for-ieee-p802-19-1-system-from-a-primary-protection-viewpoint”, IEEE mentor, July 2010
[4] “Second report and order and memorandum option and order”, FCC 08-260, 2008
[5] “Second memorandum option and order”, FCC 10-174, 2010

## Slide 13: Appendix

## Slide 14: Appendix (1) Criteria using in step 1
The following four methods are given in equations (7.5) – (7.10),
  #1: Equal transmission power distribution method,
  #2: Path-loss based/Unequal transmission power distribution method,
  #3: Extension of the former two methods using the SM (Safety Margin) value, which will be caused by the interference power level estimation errors in master TVBD of each TVBD network, and
  #4: Network prioritized method of the former two approaches.

## Slide 15: Appendix (2) Equations
#1: Equation (7.5)
#2: Equation (7.6)
#3: Equation (7.7)
#4: Equation (7.8)
shows the weight TVBD#

## Slide 16: Appendix (3) Equations
Equation (7.11)
Equation (7.12)
Equation (7.11)

## Slide 17: Appendix (4) Equations
Equation (7.14)
Equation (7.15)
Equation (7.13)