## Slide 1: Coexistence Discovery Procedures
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-04-12
Authors:

## Slide 2: Abstract
This presentation discusses procedures for CDIS and CM to make them discoverable for other entities in the coexistence system.

## Slide 3: Basic discovery step-by-step
How an entity can communicate with another, previously unknown, entity over Internet?
CM 1
CE11
CM 2
CDIS Server
CE12
CE21
CE22

## Slide 4: Discovery proposal 1/3
Requirements
  A DNS server is running in the network
  A CDIS has rights to update DNS records in the DNS server
CDIS setup
  A CDIS updates its IP and port data to the DNS server. Also a cdis alias is created to allow discovery queries
      nsupdate
      update add cdis01.testbed.lan. 300 A 192.168.0.11
      update add cdis01.testbed.lan. 300 TXT port:5001
      update add cdis.testbed.lan. 300 CNAME cdis01.testbed.lan.
      send

## Slide 5: Discovery proposal 2/3
CDIS Discovery
  A CM has DNS server info received example with DHCP
  CMs try to find a CDIS server. Example:
      Query: host cdis
      Response: cdis.testbed.lan is an alias for cdis01.testbed.lan cdis01.testbed.lan has address 192.168.0.11
CM Update
  The CM registers itself to the CDIS server with procedures defined by 802.19.1
  The CDIS checks the communication socket used by a registered CM
  The CDIS updates DNS data
      nsupdate
      update add cm01.testbed.lan. 300 A 192.168.0.71
      update add cm01.testbed.lan. 300 TXT port:5003
      send

## Slide 6: Discovery proposal 3/3
CM Discovery
  When a CM tries to communicate with another CM it checks the DNS record of the target CM
      Query: host –t ANY cm1.testbed.lan
      Response: cm1.testbed.lan has address 192.168.0.71 cm1.testbed.lan descriptive text “port:5003
  CM-CM communication channel opening
  Same DNS info can be also used when a CE tries to find address and port of a CM. A service provider can have the CM as service running in the network. In this case the CM alias can be set
      nsupdate
      update add cm01.testbed.lan. 300 A 192.168.0.71
      update add cm01.testbed.lan. 300 TXT port:5003
      update add cm.testbed.lan. 300 CNAME cm01.testbed.lan.
      send

## Slide 7: Proxy proposal
If either of the peer CMs is behind NAT, some proxy solution is needed to enable communication channel
Standard IETF RFC http://tools.ietf.org/html/rfc5389 (Session Traversal Utilities for NAT (STUN) can be used to check NAT capabilities of routers that are between CM-CDIS or CM-CM
CDIS can act as communication proxy between CMs if peer-to-peer communication between CMs is not possible
CM NAT capability information can be stored to DNS records to allow automatic proxy setup

## Slide 8: DNS Structure Proposal
Next slides describes the problem of local discovery problem. Also preliminary proposal of DNS usage is presented.

## Slide 9: Geo Location Dilemma
Distance in the physical space differs from the distance in the IP space
CM 1
Node 1
CM 2
GW 1
GW 2
Backbone
1 – 100 m
1 – 100 m
1 – 10 km
1 – 10 km
1 0 – 100 km
10 – 100 km
1 – 10000 km
CDIS Server
1 – 100 m
Node 2
Node 3
Node 4
Node 5
Node 6

## Slide 10: Physical vs. IP space
Distances in real world are measured with meters. Same metric apply also to radio interferences and that way coexistence solution.
IP networks define distances in different way. Metric is either hop or round-trip time (RTT). Hop is simply a number that tells how many IP devices forward the packet until packet reach the destination. RTT is time that it takes to send a packet to the destination and send it back.
There is no reliable mapping between real world distance and IP distance. You can’t map hops or RTT to meters. This means that discovery mechanism needs to be addressed in higher level.

## Slide 11: DNS Proposal
DNS protocol has been defined so that it allows multiple servers to be presented. DNs Client can use multiple DNS servers same time.
DNS protocol has build in mechanism to forward queries and split responsibilities of different DNS zones. Sync between servers is also possible.
No need for centralized CDIS implementation structure where CDIS servers have master-slave roles. However, DNS zone space needs to be unique and managed so that different zones have unique owners.
  Example DNS zone N61E25.finland.coex is operated by operator 1 and zone N66E27.finland.coex operated by Operator 2
  This is an open issue that needs to be resolved later