## Slide 1: Coexistence Discovery Procedures
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-05-10
Authors:

## Slide 2: Abstract
This presentation discusses procedures for CDIS and CM to make them discoverable for other entities in the coexistence system.
This is a revised version of the presentation that has been discussed in TG1 calls. We have extended the presentation with discussion on requirements and provided some more details about relations to neighbor discovery procedure.
The contributors would like to see the TG1 to have the system discovery topic as an agenda item now on with the objective to have the TG1 and interested contributors to work on a solution description.

## Slide 3: Contents
Introduction
  What is system discovery about?
  What is the assumed framework?
Assumptions of the proposal
The proposal
  One way for a CM to find out another CM that serves a neighbor TVBD
Critical questions
  What are the requirements we have for system discovery?
Summary

## Slide 4: What this all is about?
How an entity can communicate with another, previously unknown, entity over Internet?
CM 1
CE11
CM 2
CDIS Server
CE12
CE21
CE22

## Slide 5: Categorization to easy and difficult tasks
Easy tasks
A CE to find out the address of a CM
A CM to find out the address of a CDIS
Difficult task
A CM to find out the address of another CM that serves a neighbor TVBD
  This is called now on in this presentation a global neighbor discovery

## Slide 6: Assumptions of the proposal
IEEE 802.19.1 system related assumptions
A CM uses a CDIS to find out neighbor TVBDs of a TVBD it serves, at least for the neighbor TVBDs that are served by some other CM
CDIS is not a server but more like a DNS-like system from which a CM can get a list of neighbors and any related information regardless of CMs serving them
External assumptions
A DNS server is running in the network
A CDIS has rights to update DNS records in the DNS server

## Slide 7: Discovery proposal – Executive summary
Standard DNS is the solution for the easy tasks
  IEEE 802.19.1 doesn’t have anything that prevents use of DNS
  So, the proposal is to use DNS as it is for CM and CDIS discovery
As part of the neighbor discovery service a CDIS figures out which CMs serve the neighboring TVBDs and provide the related information to the CMs as required
  IEEE 802.19.1 specifies a neighbor discovery system that is very much like the DNS
    Hierarchical, distributed and fault tolerant

## Slide 8: A DNS-kind of neighbor discovery system
DNS protocol has been defined so that it allows multiple servers to be presented. DNS Client can use multiple DNS servers same time.
DNS protocol has a built-in mechanism to forward queries and split responsibilities of different DNS zones. Sync between servers is also possible.
No need for centralized CDIS implementation structure where CDIS servers have master-slave roles. However, DNS zone space needs to be unique and managed so that different zones have unique owners.
  Example DNS zone N61E25.finland.coex is operated by operator 1 and zone N66E27.finland.coex operated by Operator 2
  This is an open issue that needs to be resolved later

## Slide 9: Easy tasks – CDIS discovery
CDIS setup
  A CDIS updates its IP and port data to the DNS server. Also a cdis alias is created to allow discovery queries
      nsupdate
      update add cdis01.testbed.lan. 300 A 192.168.0.11
      update add cdis01.testbed.lan. 300 TXT port:5001
      update add cdis.testbed.lan. 300 CNAME cdis01.testbed.lan.
      send
CDIS discovery
  A CM has DNS server info received example with DHCP
  CMs try to find a CDIS server. Example:
      Query: host cdis
      Response: cdis.testbed.lan is an alias for cdis01.testbed.lan cdis01.testbed.lan has address 192.168.0.11

## Slide 10: Difficult task – Global neighbor discovery
CM-CDIS interaction
  The CM registers itself to the CDIS server and subscribes to the neighbor discovery service with procedures defined by 802.19.1
  The CM keeps the CDIS updated on changes in TVBD paramaeters
  The CDIS checks the communication socket used by a registered CM
  The CDIS updates DNS data
      nsupdate
      update add cm01.testbed.lan. 300 A 192.168.0.71
      update add cm01.testbed.lan. 300 TXT port:5003
      send
  The CDIS determines neighboring TVBDs for the registered TVBDs of registered and subscribed CMs
  The CDIS keeps the CMs updated on changes in neighboring TVBDs related to the TVBDs the CMs serve. This includes CM name/alias for each that serves a neighbor TVBD.

## Slide 11: Easy tasks – CM discovery
CM discovery
  When a CM tries to communicate with another CM it checks the DNS record of the target CM
      Query: host –t ANY cm1.testbed.lan
      Response: cm1.testbed.lan has address 192.168.0.71 cm1.testbed.lan descriptive text “port:5003
  CM-CM communication channel opening
  Same DNS info can be also used when a CE tries to find address and port of a CM. A service provider can have the CM as service running in the network. In this case the CM alias can be set
      nsupdate
      update add cm01.testbed.lan. 300 A 192.168.0.71
      update add cm01.testbed.lan. 300 TXT port:5003
      update add cm.testbed.lan. 300 CNAME cm01.testbed.lan.
      send

## Slide 12: Summary
The very basics of the system discovery problem and concept are discussed
A solution framework has been proposed
  DNS used for simple tasks
  Something new is needed to discover all the neighbors regardless of CMs serving them
We haven’t proposed a complete solution but we need to sort out, as an example, what’s the way to have neighbor discovery system that is very much like the DNS
  Our proposal doesn’t make modifications to DNS but assumes that we have a DNS-kind of system specified with CDISs having roles and protocols like with DNS

## Slide 13: Proposal
We’d like to have the issue of system discovery and especially the neighbor discovery system as an agenda item in TG1 meetings now on
We would like see joint development on these issues to happen between interested parties in the task group using this and other contributions on these issues

## Slide 14: Appendix

## Slide 15: Proxy proposal
If either of the peer CMs is behind NAT, some proxy solution is needed to enable communication channel
Standard IETF RFC http://tools.ietf.org/html/rfc5389 (Session Traversal Utilities for NAT (STUN) can be used to check NAT capabilities of routers that are between CM-CDIS or CM-CM
CDIS can act as communication proxy between CMs if peer-to-peer communication between CMs is not possible
CM NAT capability information can be stored to DNS records to allow automatic proxy setup

## Slide 16: Geo location dilemma
Distance in the physical space differs from the distance in the IP space
CM 1
Node 1
CM 2
GW 1
GW 2
Backbone
1 – 100 m
1 – 100 m
1 – 10 km
1 – 10 km
1 0 – 100 km
10 – 100 km
1 – 10000 km
CDIS Server
1 – 100 m
Node 2
Node 3
Node 4
Node 5
Node 6

## Slide 17: Physical vs. IP space
Distances in real world are measured with meters. Same metric apply also to radio interferences and that way coexistence solution.
IP networks define distances in different way. Metric is either hop or round-trip time (RTT). Hop is simply a number that tells how many IP devices forward the packet until packet reach the destination. RTT is time that it takes to send a packet to the destination and send it back.
There is no reliable mapping between real world distance and IP distance. You can’t map hops or RTT to meters. This means that discovery mechanism needs to be addressed in higher level.