## Slide 1: Discovery system overview
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-06-29
Authors:

## Slide 2: Abstract
This presentation deals with system and service discovery aspects of 802.19.1 system but touches also the issues related to interfering TVBD discovery
This presentation contains an overview of the proposal to have the 802.19.1 system architecture to include a further logical element to support CDIS in interferer discovery
  The proposal was verbally presented in a TG1 call on June 22nd and this presentation is intended to continue the discussions started in that call

## Slide 3: Basic assumptions
A CM is an entity that serves TVBDs via their CEs
  Different kind of management services for TVBDs that want to receive orders or guidance on operating parameters
  Information service for TVBDs that want to make all the decisions by themselves but want to receive information about environment from the coexistence system
A CDIS is an entity that serves CMs
  Finds out for a CM those TVBDs that are potential interferers of the TVBDs the CM serves and the CMs that serve those potential interferers
    The potential interferers have been also called neighbors
    Needed at least to find out those potential interferers that are served by other CMs

## Slide 4: Problem statement
The 802.19.1 specification needs to provide means for a coexistence manager (CM) to find out TVBDs that may interfere the TVBDs that the CM serves or that may be interfered by those TVBDs
The coexistence system architecture discussed in the TG1 has coexistence discovery and information server (CDIS) for this purpose
How do we ensure that a CM gets all the interfering/interered TVBDs from a CDIS regardless of the CDIS instance the CM is using?

## Slide 5: Some definitions and terms
Communication area and interference area are defined for a TVBD network that is represented by a TVBD that is using the coexistence system services and registered to the coexistence system
Communication area = A geographical area within which the TVBD can communicate with other TVBDs, i.e. coverage area of the TVBD network
Interference area = A geographical area within which signal level from any TVBD of the TVBD network is equal to or larger than N+Im
  N stands for noise and Im represents interference margin

## Slide 6: Questions by a CDIS
Who interferes my TVBD?
  My TVBD is interfered if my communication area overlaps with an interference area of another TVBD
Who is interfered by my TVBD?
  My TVBD iinterferes another TVBD if my interference area overlaps with the communication area of the other TVBD

## Slide 7: Two potential solutions
Mandate the CDISs to synchronize themselves
  Rely on available database synchronization mechanisms and leave the details to implementation
  Each CDIS has all the required information about all the possible TVBDs regardless of which CM and subsequently CDIS serves the TVBDs
Specify a system and related entity to support CDIS in discovery
  Specify a new support service that is available for CDISs to find out interferer/interfered TVBDs that are registered to other CDISs
  Each CDIS has all the required information about the TVBDs registered to them by the CMs using their services. The support service is used to find out the TVBDs registered to the other CDISs.

## Slide 8: Short comparison of the two options
Mandate the CDISs to synchronize themselves
  Pros: Easy to standardize
  Cons: Heavy burden to CDIS implementations, limits scalability
Specify a system and related entity to support CDIS in discovery
  Pros: Scalable, allows different types of CDIS implementations, reliable
  Cons: More to standardize

## Slide 9: One detail: IP address resolution
A list of interfered/interfering TVBDs is not enough for a CM, but the CM needs to get also such information about CMs that serve those TVBDs that the CM can communicate with the other CMs
One proposal discussed earlier in the task group is to give CM’s IP address as such information
  A CDIS would provide a CM IP addresses of the other CMs as part of the interfered/interfering TVBD list
We would like to see the DNS to be used to find out IP addresses
  A CM receives from a CDIS hostname of each CM that serve interfered/interfering TVBD
  The CM gets the CM’s IP address from the DNS with the hostname
With this approach we don’t have to deal with changes in IP addresses and we can leverage the security solutions available / becoming available for DNS

## Slide 10: Summary
The 802.19.1 specification needs to provide means for a CM to find out TVBDs that may interfere the TVBDs that the CM serves or that may be interfered by those TVBDs
Two design options were described to resolve the issue
The proposal is to have a support service and a new entity defined for CDISs to find out interfered/interfering TVBDs registered to other CDISs
Additionally, the proposal is to use the DNS to full extent and provide CM hostnames as part of interferer disocvery result