## Slide 1: Discovery system proposal
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-07-20
Authors:

## Slide 2: Abstract
This presentation is a follow up to the earlier presentations and contributions on the interferer discovery. Contribution 19-11/0061r1 dealt with the problem and gave an overview of the proposed remedy.
In this presentation we go to the details of the solution that we propose for the IEEE 802.19.1 coexistence system

## Slide 3: Basic assumptions
A CM is an entity that serves TVBDs via their CEs
  Different kind of management services for TVBDs that want to receive orders or guidance on operating parameters
  Information service for TVBDs that want to make all the decisions by themselves but want to receive information about environment from the coexistence system
A CDIS is an entity that serves CMs
  Finds out for a CM those TVBDs that are potential interferers of the TVBDs the CM serves and the CMs that serve those potential interferers
    The potential interferers have been also called neighbors
    Needed at least to find out those potential interferers that are served by other CMs

## Slide 4: Problem statement
The 802.19.1 specification needs to provide means for a coexistence manager (CM) to find out TVBDs that may interfere the TVBDs that the CM serves or that may be interfered by those TVBDs
The coexistence system architecture discussed in the TG1 has coexistence discovery and information server (CDIS) for this purpose
How do we ensure that a CM gets all the interfering/interered TVBDs from a CDIS regardless of the CDIS instance the CM is using?

## Slide 5: Some definitions and terms
Communication area and interference area are defined for a TVBD network that is represented by a TVBD that is using the coexistence system services and registered to the coexistence system
Communication area = A geographical area within which the TVBD can communicate with other TVBDs, i.e. coverage area of the TVBD network
Interference area = A geographical area within which signal level from any TVBD of the TVBD network is equal to or larger than N+Im
  N stands for noise and Im represents interference margin

## Slide 6: Questions by a CDIS
Who interferes my TVBD?
  My TVBD is interfered if my communication area overlaps with an interference area of another TVBD
Who is interfered by my TVBD?
  My TVBD iinterferes another TVBD if my interference area overlaps with the communication area of the other TVBD

## Slide 7: The basis of the proposed solution
Specify a system and related entity to support CDIS in discovery
  Specify a new support service that is available for CDISs to find out interferer/interfered TVBDs that are registered to other CDISs
  Each CDIS has all the required information about the TVBDs registered to them by the CMs using their services. The support service is used to find out the TVBDs registered to the other CDISs.

## Slide 8: System architecture view
A new entity and an associated exposed interface would be needed to support the CDIS
New Entity

## Slide 9: Operating principles
The new discovery system provides means to
  Register geographical areas and information associated to them
  Find out registered geographical areas with some search criteria
A CDIS forms geographical areas for the TVBD networks or devices registered to it
The CDIS registers the TVBD network or device related geographical areas to the new discovery system
The CDIS requests the new discovery system to provide those registered geographical areas and associated information that meet the search criteria
On request the new discovery system finds out those registered geographical areas that meet the search criteria and provides them and the associated information in response to the CDIS

## Slide 10: Basics of the new discovery system
A DNS-like distributed and hierarchical database that builds upon concept of unique geographical zones that are managed by servers
The system uses geographical areas that may of different type and that are defined with means of an area contour
  The area contour may have a contour parameter (e.g. dBm value)
  Each area is associated with information like area identifier (TVBD identifier, etc.), service descriptor (CM, CDIS, etc.) and hostname
Geographical areas may overlap with multiple geographical zones and thus the system ensures that each registered area becomes registered to the appropriate zone specific servers
The system needs to be able to direct the area inquiries to the correct zone specific servers

## Slide 11: Basics of the use of the new discovery system
Area registration
  A communication area with the contour defining the border of the area and the contour parameter indicating the interference level (dBm) tolerated on the border of the area
  Few interference areas with different maximum interference levels (dBm) generated by the TVBDs within the communication area
Area inquiry
  Give me interference areas that overlap with this area (communication area) I have here with contour value x dBm
  Give me communication areas that overlap with this area (the interference area with the highest interference level)

## Slide 12: After the inquiry in the CDIS
The CDIS has a list of communication areas and interference areas from the discovery system and assocatied information
  Contour parameters
  TVBD identifier
  Service descriptions (CDIS, CM, etc.)
  Hostnames (for CDIS, CM, etc.)
The CDIS uses the DNS to find out the IP addresses of the CDIS The CDIS may need to contact the other CDISs to obtain more information about identified interferers
Finally the CDIS provides the list of interferers to the CM with the necessary associated information
  At least the TVBD identifier and the CM hostname

## Slide 13: Summary
Basic operating principles of the new discovery system are described
Use of the new discovery system is shortly explained
The intent is to continue with more detailed descriptions during the next few weeks