## Slide 1: Neighbors and Neighbor Discovery
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-09-20
Authors:

## Slide 2: Abstract
This presentation deals with definitions related to neighbor discovery in context of IEEE 802.19.1 coexistence system and specification

## Slide 3: Framework as of today
CDIS
CM
CM
CE
CE
Neighbor list (CDIS->CM)
- All or IntraCM
Neighbor list (CDIS->CM)
- All or IntraCM
Neighbor report (CM->CE)
Neighbor report (CM->CE)
Neighbor information (CM->CM)
Neighbor discovery

## Slide 4: Neighbor discovery
Neighbor discovery is a function/service with which a CM finds out both those TVBD receivers that may be interfered by the TVBD transmitters the CM serves and those TVBD transmitters that may interfere the TVBD receivers the CM serves
  As the outcome of the neighbor discovery the CM has a neighbor list for each TVBD (TVBD receiver and transmitter) it serves
The neighbor discovery can be split into two stages
  Intra-CM neighbor disocvery
    A CM may do this or use a CDIS to do this
  Inter-CM neighbor discovery
    A CM shall use a CDIS to do this
The neighbor discovery shall to be conducted on each TVBD served by a CM
  Intra-CM neighbor discovery by the CM and inter-CM neighbor discovery by a CDIS, or
  Both the intra-CM and the inter-CM neighbor discovery by a CDIS

## Slide 5: A neighbor set from the neighbor discovery
Once the neighbor discovery has been conducted on a TVBD served by a CM, the CM has neighbors of the TVBD
  Neighbors are those TVBD receivers that may be interfered by the TVBD transmitter and those TVBD transmitters that may interfere the TVBD receiver
The neighbors form a neighbor set

## Slide 6: Main points of neighbor discovery and neighbor set
The neighbor discovery is done in the coexistence system with means of interference estimation using the information obtained from CEs about TVBDs
  TVBD registration is the mean to obtain and provide the required information to the system
  Neighbor discovery is an independent function from coexistence decision making (i.e. resource allocation).
  CMs decisions on TVBD’s operating parameters don’t have an impact on the neighbor set

## Slide 7: A route from a neighbor set to neighbor report and neighbor information
Neighbor set is basis of both neighbor report and neighbor information
  Neighbor report is the mean for a CM to provide information to a TVBD about the operating environment in case the TVBD is subscribed to the information service
  Neighbor information is the mean for a CM to provide information to another CM in case of inter-CM neighbors
The proposal is that the whole neighbor set is reported in a neighbor report
The proposal is that a CM is mandated to provide neighbor information to other CMs with respect to all inter-CM neighbors of the neighbor set

## Slide 8: A route from a neighbor set to decision making
How strict rules we should set to CM’s decision making with respect to a neighbor set?
  Does a CM have to consider all the TVBDs in the neighbor set in the decision making?
  Is it more like a CM should consider all the TVBDs in the neighbor set in the decision making?
Our proposal is to leave it up to the CMs to decide whether the whole neighbor set is taken into account or e.g. the most potential interferers only are considered
  Decision making algorithm is not expected to be standardized and thus it is close to impossible to verify that the whole neighbor set is considered

## Slide 9: Using measurement reports with the neighbor set
Measurement reports from TVBDs are valuable input for decision making and to the neighbor reports and neighbor information messages
The proposal is that measurement reports shall not be used to update neighbor sets

## Slide 10: Summary
Definition of a neighbor set proposed
  Neighbor set is the outcome of the neighbor discovery
  Neighbor set is updated only upon updates in TVBD registrations
Rules for neighbor reporting and neighbor information delivery between CMs proposed
  The whole neighbor set to be used
Proposal is to allow a CM to consider only a portion of a neighbor set in decision making