## Slide 1: Coexistence Discovery Terminology
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-09-22
Authors:

## Slide 2: Abstract
This presentation continues discussion on neigh… oops, sorry
This presentation provides proposal on terms to be used in IEEE 802.19.1 coexistence specification when dealing with those coexistence system users that may interfere each other

## Slide 3: A very basic term
Coexistence system user
  One that connects to the coexistence system, becomes registered to the coexistence system and subscribes to the coexistence services available for the coexistence system user
  All the above happens via a coexistence enabler
  So far we have called the coexistence system user a TVBD or TVBD network
  Coexistence system user has a receiver, a transmitter or the both
Are there any problems with this term? Could we use this instead of ”TVBD or TVBD network”?
  An alternate term that has been proposed earlier is a coexistence system client

## Slide 4: Framework as of today
CDIS
CM
CM
CE
CE
Neighbor list (CDIS->CM)
- All or InterCM
Neighbor list (CDIS->CM)
- All or InterCM
Neighbor report (CM->CE)
Neighbor report (CM->CE)
Neighbor information (CM->CM)
Neighbor discovery
Neighbor is the problem. We don’t like neigbhors

## Slide 5: A new framework proposal
CDIS
CM
CM
CE
CE
Coexistence list (CDIS->CM)
- All or InterCM
Coexistence list (CDIS->CM)
- All or InterCM
Coexistence report (CM->CE)
Coexistence report (CM->CE)
Coexistence information (CM->CM)
Coexistence discovery
No more neighbors but only coexistence. We like that!!!!

## Slide 6: Coexistence discovery
Coexistence discovery is a function with which a CM finds out both those receivers of coexistence system users that may be interfered by the transmitter of a coexistence system user register to the CM, and those transmitters of coexistence system users that may interfere the receiver of a coexistence system user registered to the CM
  Transmitter of a coexistence system user that may interfere a receiver of coexistence system user is called an interference source
  Rceiver of a coexistence system user that may be interfered by a transmitter of a coexistence system user is called an interference victim

## Slide 7: Outcome of the coexistence discovery
The CM shall conduct the coexistence discovery on each coexistence system user that is registered to it
As the result the CM has for each coexistence system user that is registered to it a list of coexistence system users that are categorized to one or both of the following categories
  Interference source
  Interference victim
Let’s call this list a coexistence set and members of the set coexistence set members

## Slide 8: Main points of coexistence discovery and coexistence set
The coexistence discovery is done in the coexistence system with means of interference estimation using the information obtained from CEs about the coexistence system users
  Coexistence system user registration is the mean to obtain and provide the required information to the system
  A CM shall invoke the coexistence discovery upon a new coexistence system user registration and upon re-registration of a coexistence system user
The coexistence set forms the basis of the coexistence decision making and inter-CM communication

## Slide 9: Possibility to split the coexistence discovery to two stages
A CM shall use a CDIS for the coexistence discovery
A CM shall use a CDIS either
  To find out all the interference sources and interference victims of a coexistence system user registered to it
  To find out those interference sources and interference victims of a coexistence system user registered to it that are registered to other CMs
    Let’s call this inter-CM coexistence discovery
If a CM uses a CDIS for the inter-CM coexistence discovery, it shall look for interference sources and interference victims of a coexistence system user registered to it from the rest of the coexistence system users that are registered to it with the means of the interference estimation
  Let’s call the latter part of the coexistence discovery that happens within the CM intra-CM coexistence discovery
If a CM uses a CDIS for the inter-CM coexistence discovery and performs the intra-CM coexistence discovery, it shall combine the results to a coexistence set

## Slide 10: Summary
Definition of a coexistence system user proposed
  Coexistence system user has either a transmitter, a receiver or the both
Definition of a coexistence discovery function proposed
Definition of a coexistence set proposed
  Coexistence set is the outcome of the coexistence discovery
  Coexistence set comprises of coexistence set members