## Slide 1: Coexistence Discovery Terminology
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-11-08
Authors:

## Slide 2: Abstract
This presentation is follow-up of the terminology proposal submitted to the task group in September 2011 interim meeting.

## Slide 3: Vocabulary
CE = Coexistence enabler
CM = Coexistence manager
CDIS = Coexistence discovery and information server

## Slide 4: The framework proposal
CDIS
CM
CM
CE
CE
Coexistence list (CDIS->CM)
- All or those registered to other CMs
Coexistence list (CDIS->CM)
- All or those registered to other CMs
Coexistence report (CM->CE)
Coexistence report (CM->CE)
Coexistence information (CM->CM)
Coexistence discovery
Coexistence set
Coexistence system user
Coexistence system user
Coexistence set

## Slide 5: Components of the framework
Coexistence system user
Coexistence discovery
Coexistence list
Coexistence set
Coexistence report

## Slide 6: Coexistence system user
A logical entity that is using services of the coexistence system via a CE
A coexistence system user may be associated to a device with a wireless transceiver (Rx+Tx) or with a wireless transmitter (Tx) or receiver (Rx) only
We may have any type of coexistence system users but we should first focus on devices that have a Tx and are master devices, i.e. devices that can initiate and control operations of a wireless network
  One needs to somehow indicate also whether the user/device may enable transmissions of other devices, i.e. client devices, so that the system can determine whether estimation on indirect transmissions is needed
A CE represents a coexistence system user and the user doesn’t have to speak the ”802.19.1 language”

## Slide 7: Coexistence discovery (1/3)
A CM shall conduct coexistence discovery on each coexistence system user that is registered to it
Coexistence discovery is the procedure for the CM to find out the other coexistence system users with which the coexistence system user needs to coexist
  Need for coexistence exists if the coexistence system user receiver may be interfered by a coexistence system user transmitter register or if the coexistence system user transmitter may interefere a coexistence system user receiver
Unlike in our previous proposals we now propose the coexistence discovery to be designed as a continuous process run in each CM
  Comprises of a set of mandatory functions and steps but leaves room for improvements and innovation

## Slide 8: Coexistence discovery (2/3)
Elements of the coexistence discovery process are assumed to be as follows
  Coexistence system user discovery
  Coexistence set management
With the coexistence system user discovery the CM finds out those coexistence system users that needs to be considered as the users with which the CM’s user needs to coexist
Coexistence set management is a CM’s internal functionality that is not specified
  The CM determines the coexistence system users that are considered in the coexistence decisions

## Slide 9: Coexistence discovery (3/3)
The coexistence system user discovery is done in the coexistence system with means of interference estimation using the information obtained from CEs about the coexistence system users
  Coexistence system user (re-)registration is the mean to obtain and provide the required information to the system
A CM shall invoke the coexistence system user discovery upon a new coexistence system user registration and upon re-registration of a coexistence system user
  Part of the discovery can be done internally in the CM
  The CM shall use the CDIS for the coexistence system user discovery at least for those users registered to other CMs

## Slide 10: Coexistence list
A CM shall acquire a coexistence list for each coexistence system user that is registered to it
Coexistence list is the outcome of the coexistence system user discovery
  At least a part of that shall come from the CDIS to the CM upon inquiry
  A part of the list may be determined by the CM

## Slide 11: Coexistence set
A CM shall determine a coexistence set for each coexistence system user that is registered to it
It contains those other coexistence system users with which the coexistence system user needs to coexist
The coexistence set forms the basis of the coexistence decisions and inter-CM communication

## Slide 12: Coexistence report
A coexistence report is used by the CM to convey information to a coexistence system user subscribed to the information service

## Slide 13: Summary
Coexistence framework proposed with related terminology
Thank you!