## Slide 1: Some Open Issues for Discussion
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-11-07
Authors:

## Slide 2: Abstract
This presentation contains some open issues in the candidate draft spotted by the authors during the task group review
We would like to discuss the issues in the task group in order to get feeling on what’s the group’s opinion on the issues and whether they should be resolved in the draft and whether the 802.19.1 specification should provide a solution for them

## Slide 3: Vocabulary
CE = Coexistence enabler
CM = Coexistence manager

## Slide 4: Some definitions
Coexistence system user = A logical entity that is using services of the coexistence system via a CE. A coexistence system user may be associated to a device with a wireless transceiver (Rx+Tx) or with a wireless transmitter (Tx) only.
Coexistence set = A CM determines a coexistence set for each coexistence system user that is registered to it. It contains those other coexistence system users with which the coexistence system user needs to coexist.

## Slide 5: An issue list
Interconnections between CMs
Information exchange between CMs
CMs with different coexistence decision algorithms
Information from a coexistence system user to a CM

## Slide 6: Interconnections between CMs
Currently the candidate draft provides some basic means for CMs to get connected. There are no rules, however, when the CMs needs to become connected and whether coexistence decision algorithm support has any implications to the interconnections.
The authors believe the 802.19.1 specification needs to set firm requirements for CM interconnections
  CM interconnections are determined based on coexistence sets
  A CM needs to get connected to another CM whenever the other CM serves a coexistence system user in one of the CM’s coexistence sets
  So, each interconnection is driven by a coexistence need originating from a coexistence system user

## Slide 7: Information exchange between CMs
Interconnections between CMs is not enough but we believe the 802.19.1 specification should set rules for information exchange between interconnected CMs
  A CM that serves a coexistence system user needs to be aware of information related to the other coexistence system users in the coexistence set of the coexistence system user
  We believe the 802.19.1 specification needs provide the mechanisms to obtain the information
  Actually we believe each CM should be responsible for keeping a peer CM updated on changes in information related to a CM’s coexistence system user when the user is in a peer CM’s coexistence set
    With information push we may avoid unnecessary information requests

## Slide 8: CMs with different coexistence decision algorithms
The 802.19.1 specification is expected to allow CMs to implement any type of coexistence decision algorithm and the specification is expected to define some possible algorithms
What is expected from CMs that implement and support different algorithms?
  What’s expected from the CM interconnections?
  What’s expected from information exchange between the CMs?
We believe the CM interconnection and information exchange rules should be independent from the coexistence decision algorithm
  Interactions and information exchange related to decision making is specific to the algorithm and doesn’t belong to this category

## Slide 9: Information from a coexistence system user to a CM
Most of the information from a coexistence system user to the coexistence system comes as part of the user registration (or re-registration)
  Quite a lot of information is available in the messages and in the interfaces but many of the parameters are currently optional
  The assumption seems to be that the coexistence system user may decide on what information it supports and provides to the system
CM’s coexistence decision algorithms assume that certain information is available from the coexistence system users
There seems to be a clear mismatch between these two approaches and assumptions which is expected to lead to situations in which the coexistence system and especially the CM can’t serve a coexistence system user because that can’t provide expected and required information

## Slide 10: Summary
Interconnections between CMs
  Should the spec have some rules on CM interconnections?
Information exchange between CMs
  Should the spec provide means for information exchange between CMs?
  Should the spec set rules for the information exchange between CMs?
CMs with different coexistence decision algorithms
  How do CMs with different coexistence decision algorithms interact? Do they interact?
Information from a coexistence system user to a CM
  How to ensure that a CM has required information from a coexistence system user so that it can serve it?

## Slide 11: Why to bother?
We are concerned about quite a lot of issues in the current 802.19.1 draft and especially on what the group expects from the final spec
This presentation covered only a few of those issues that we want to discuss in the TG in order to figure out whether the issues are real and whether we can find out an easy and common solution for them