## Slide 1: Comment Resolutions (CID 40, 43, 44)
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2011-11-09
Authors:

## Slide 2: Abstract
This presentation contains three proposals
Information/management service handling (CID 40)
Proposed changes in message format (CID 43)
Master CM selection algorithm normative text proposal (CID 44)

## Slide 3: System Overview
Network Type A
Network Type B
Network Type C
CDIS
CE
CM
CE
CE
CE
CE
CE
CE
CE
CM
CE
CE
CE
CE
CE
CM

## Slide 4: Assumptions
1 to 1 mapping between CE and TVBD network or device
The address of a CE is pre-configured for a TVBD network or device
A CE or TVBD network/device knows the address of CDIS upon start-up
  E.g., CDIS address may come from TVWS DB
A CM knows the address of CDIS upon start-up
Inter-CM neighbors are calculated by CDIS upon a request from a CM

## Slide 5: Coexistence Interference Channel Map (CICM)
Internal to a CM
For each management serviced TVBD network/device, we define the following C-WSM to represent the list of available channel and occupancy of the channel
How to calculate Occupancy
  Estimated channel busy time due to intra-CM information serviced neighboring TVBD N/Ds, inter-CM information serviced neighboring TVBD N/Ds, and unregistered TVBD N/Ds
Channel Number | Occupancy (100% = 255)
21 | 100
22 | 200

## Slide 6
CM1
CM2
Management serviced TVBD network or device
Information serviced TVBD network or device
Unregistered TVBD network or device
Information serviced inter-CM neighboring TVBD network or device
Target_TVBD
Occupancy estimation
through Query process
Occupancy measurement
through measurement process
Occupancy estimation
through inter-CM Query process
CDIS

## Slide 7: An Example
Coexistence Decision Algorithm (BLACKBOX)
{CICM (i)}
Set of CCIM per each management serviced TVBD
CM
Intra-CM neighbors
(e.g., neighbor report)
Inter-CM neighbors
(e.g., neighbor report)
{Operating CH (i)}

## Slide 8: Occupancy Estimation
Intra-CM information serviced neighboring TVBD N/D
  Obtain occupancy information through “occupied channel query” process
TVBD N/D
CE
CM
Occupied_Channel_Query_Request
Occupied_Channel_Query_Response
Occupied_Channel_Query.request
Occupied_Channel_Query.response

## Slide 9: Occupancy Estimation
Inter-CM information serviced neighboring TVBD N/D
  Obtain occupancy information through CM to CM exchange process
TVBD N/D
CE
CM2
Occupied_Channel_Query_Request
Occupied_Channel_Query_Response
Occupied_Channel_Query.request
Occupied_Channel_Query.response
CM1
CM_Occupied_Channel_Query_Request
CM_Occupied_Channel_Query_Response

## Slide 10: Occupancy Estimation
Unregistered neighboring TVBD N/D
  Obtain occupancy information channel measurement
    Measure accumulated channel busy time over the measurement duration if received signal strength is greater than a threshold given in the request
    Calculate the percentage of busy time over measurement duration
TVBD N/D
CE
CM
Measurement_Request
Measurement_Response
GetMeasurement.request
GetMeasurement.response

## Slide 11: Message Format Change
Change the message header format (Table 32) as follows
Information Element | Data Type | Description/Value
MsgType | Char | Message type
sourceType | CX_ID | Source type
sourceIdentifier | IA5String | Source identifier
destType | CX_ID | Destination type
destinationIdentifier | IA5String | Destination identifier
ACKPolicy | Boolean | Request to send an acknowledgement of reception by setting this field to 1
Length | Integer | The total length of payload

## Slide 12: Master CM Selection
A master CM selection can be used as a reconfiguration tool
  See the example in the next slide
Three selection schemes are presented
  Load-balancing focused master/slave CM selection
    Based on computational load on each CM, master/slave CM selection is triggered and performed
  Geological coverage based Master/Slave CM Selection
    Based on overlapped coverage (calculated by CDIS), master/slave CM selection is triggered and performed
  Interference-level based Master/Slave CM Selection
    When interference level is too high, master CM selection can be triggered

## Slide 13: Example
  Initial coexistence topology
  Reconfigured coexistence topology
  (through Master CM selection)