## Slide 1: Coexistence of CMs with different decision making algorithms
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-03-13
Authors:

## Slide 2: Abstract
This presentation is a submission to an action item listed in 19-12/0004r2.
The presentation splits up the item into sub-items
The presentation provides a description for each sub-item and a solution proposal
  A set of questions given for each sub-item to illustrate the open issues
  A solution proposal is a piece of draft normative text
The intention is to have motions later on the week in the TG1 to agree on solutions for sub-items related to coexistence of CMs with different decision making algorithms

## Slide 3: Introduction
We have different decision topologies
We have different decision algorithms
We have multiple CMs
What are obligations and possibilities of a CM that serves a WSO in the management service, and the WSO’s coexistence set has another WSO that another CM serves in the management service with respect to the other CM and the WSO it serves?

## Slide 4: Decision topology definitions
Autonomous
  When a CM applies autonomous decision making, it shall be able to make decisions on the WSOs that it serves.
Distributed
  When a CM applies distributed decision making, it shall be able to make decisions on the WSOs that it serves and on other WSOs that are in the coexistence sets of the WSOs it serves.
Centralized
  When a CM applies centralized decision making and the CM acts as a master CM, it shall be able to make decisions on the WSOs it serves directly or through the slave CMs it manages, and on other WSOs that are in the coexistence sets of the WSO it serves.
    It would be beneficial to specify that a WSO connected and registered through its CE to a CM that acts as a slave CM is served by the master CM. This helps with definitions on coexistence set.

## Slide 5: Sub-item list
Coexistence of CMs with different decision making algorithms
  Interconnection rules
  Information sharing rules
  Decision making behavior

## Slide 6: Interconnection rules
Q: When a CM needs to be connected to another CM?
A: A CM that serves a WSO and the WSO’s coexistence set has another WSO that another CM serves shall be connected to the other CM.
  This assumes that when the centralized decision making is applied, a WSO is served by a master CM even if the WSO’s CE is registered to a slave CM.
  Alternatively, we could state the following: A CM that serves a WSO and the WSO’s coexistence set has another WSO that another CM serves shall be connected to the other CM except that in case of centralized decision topology a slave CM shall be connected only to a CM that acts as the master CM for it.

## Slide 7: Information sharing rules
Q: What information sharing obligations a CM has with respect to the other CM to which it is connected because of the coexistence set relationship?
A: A CM that serves a WSO and the WSO’s coexistence set has another WSO that another CM serves shall keep the other CM aware of changes in the capabilities, operating parameters and coexistence environment of the WSO.

## Slide 8: Decision making in connected CMs with different decision algorithms
Q1: May a CM that applies the distributed decision topology make decisions on a WSO served by another CM to which it is connected and that applies the autonomous decision topology?
A: No. Autonomous decision making limits the scope of decisions to the WSOs served by the CM and it treats other CMs as autonomous decision makers.
Q2: May a CM that applies the distributed decision topology make decisions on a WSO served by another CM to which it is connected regardless of the coexistence decision algorithm applied by the CMs?
A: Let’s see...

## Slide 9: Connected CMs with distributed topology and different algorithms
We would like to see the answer to the Q2 to be ”Yes”
A few possible ways to receive the ”Yes” answer
  A straightforward solution is to mandate the CMs to implement reconfiguration commands received from connected CMs as such
    We should address at least race conditions to avoid concurrent decisions and their implications
  An alternative is to mandate the CMs to interact in the decision making
    This would require one commonly applied interaction mechanism
Other mechanisms may exist but before going into them we shold decide on whether the answer to the Q2 is ”Yes” or ”No”

## Slide 10: Coexistence decision algorithm related information sharing between connected CMs
Currently the draft has no means for CMs to indicate to each other which decision topology and algorithm is used
Such a mean is needed to facilitate ”coexistence” of connected CMs
  A CM that serves a WSO and the WSO’s coexistence set has another WSO that another CM serves shall indicate to the other CM which decision topology and algorithm is used by the CM when serving the WSO

## Slide 11: Summary
Thank You