## Slide 1: Coexistence of CMs with different decision making algorithms
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-03-13
Authors:

## Slide 2: Abstract
This presentation is a submission to an action item listed in 19-12/0004r2.
First, basic assumptions about CM interconnections and information sharing between connected CMs are discussed
Second, the presentation splits up the item into sub-items
The presentation provides a description for each sub-item and a solution proposal
  A set of questions given for each sub-item to illustrate the open issues
  A solution proposal is a piece of draft normative text
The intention is to have motions later on the week in the TG1 to agree on solutions for sub-items related to coexistence of CMs with different decision making algorithms

## Slide 3: Introduction
We have different decision topologies
We have different decision algorithms
We have multiple CMs
What are obligations and possibilities of a CM1 that serves a WSO1 in the management service, and the WSO1’s coexistence set includes a WSO2 that another CM2 serves in the management service with respect to the other CM2 and the WSO2 it serves?

## Slide 4: Interconnection rules – Independent from decision making
Q: When a CM needs to be connected to another CM?
A: A CM1 that serves a WSO1 and the WSO1’s coexistence set has WSO2 that CM2 serves shall be connected to the CM2
  This assumes that when the centralized decision making is applied, a WSO is served by a master CM even if the WSO’s CE is registered to a slave CM.

## Slide 5: Information sharing rules – Independent from decision making
Q: What information sharing obligations a CM has with respect to the other CM to which it is connected because of the coexistence set relationship?
A: A CM1 that serves a WSO1 and the WSO1’s coexistence set includes a WSO2 that CM2 serves shall keep the CM2 aware of changes in the capabilities, operating parameters and coexistence environment of the WSO1 and vice versa.

## Slide 6: Decision topologies
Autonomous
  When the autonomous decision making is applied, a CM makes decisions on coexistence independently from other CMs.
Distributed
  When the distributed decision making is applied, a CM negotiates about decisions with other CMs that serve the coexistence set elements of the CM
Centralized
  When the centralized decision making is applied, one CM controls decision making of one or more other CMs. The CM that controls the decision making is called a master CM. The CM that is controlled by a master CM is called a slave CM.
    It would be beneficial to specify that a WSO connected and registered through its CE to a CM that acts as a slave CM is served by the master CM. This helps with definitions on coexistence set.

## Slide 7: Decision making in connected CMs with different decision algorithms
Q1: May a CM that applies the distributed decision topology make decisions on a WSO served by another CM to which it is connected and that applies the autonomous decision topology?
A: No. Autonomous decision making limits the scope of decisions to the WSOs served by the CM and it treats other CMs as autonomous decision makers.
Q2: May a CM that applies the distributed decision topology make decisions on a WSO served by another CM to which it is connected regardless of the coexistence decision algorithm applied by the CMs?
A: Let’s see...

## Slide 8: Connected CMs with distributed topology and different algorithms
We would like to see the answer to the Q2 to be ”Yes”
A few possible ways to receive the ”Yes” answer
  A straightforward solution is to mandate the CMs to implement reconfiguration commands received from connected CMs as such
    We should address at least race conditions to avoid concurrent decisions and their implications
  An alternative is to mandate the CMs to interact in the decision making
    This would require one commonly applied interaction mechanism
Other mechanisms may exist but before going into them we shold decide on whether the answer to the Q2 is ”Yes” or ”No”

## Slide 9: Coexistence decision algorithm related information sharing between connected CMs
Currently the draft has no means for CMs to indicate to each other which decision topology and algorithm is used
Such a mean is needed to facilitate ”coexistence” of connected CMs
  A CM that serves a WSO and the WSO’s coexistence set has another WSO that another CM serves shall indicate to the other CM which decision topology and algorithm is used by the CM when serving the WSO

## Slide 10: Summary
Thank You