## Slide 1: Design Principles for Entity Responsibilities
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Date: 2012-06-20
Authors:

## Slide 2: Abstract
This presentation continues discussion on entity responsibilities and corresponding implications to procedures which were discussed in 19-12/0057r1.

## Slide 3: Design Assumptions
The IEEE 802.19.1 system comprises of coexistence enablers (CEs), coexistence managers (CMs) and coexistence discovery and information servers (CDISs)
Each piece of information has a source which is a coexistence system entity (CE, CM or CDIS)
The 802.19.1 system consumes information to provide services (coexistence discovery, coexistence management and information service)
The 802.19.1 system generates information in the services

## Slide 4: Design Principles
The information source entities are responsible for sharing the information with the other entities of the coexistence system to the extent needed
  The entities that have information for consumption in the coexistence system are responsible for pushing up to date information to other relevant entities
  The entities that provide services push service related information to service subscribers
Request based procedures have reasons and places but they are not the best ones to distribute information that is dynamic in nature
  Indication and push based approach should be used to share information since the information source is the entity which knows when there is change in the information